1
-
-
-
-
-
0                          Kermit File Transfer Package
-
                                   August 1986
-
-
-
-
-
-
-                            Copyright (C) 1981,1986
             Trustees of Columbia University in the City of New York
0      Permission is granted to any individual or institution to use, copy,
     or redistribute this document so long as it is not sold for profit, and
                   provided this copyright notice is retained.
0      This manual, which is based on the Columbia University Kermit User's
     Guide, contains modifications made by the National Institutes of Health.
-
-                                Computer Center
                    Division of Computer Research & Technology
                          National Institutes of Health
                            Bethesda, Maryland  20892
1
1                                                                               i
-
                                Table of Contents
0Statement of Kermit Software Support ..................................   1
0Preface ...............................................................   4
0How to Use This Manual ................................................   7
01.  Introduction ......................................................   9
0    1.1.  Why Kermit? .................................................  10
     1.2.  How Kermit Works ............................................  11
02.  How to Use Kermit .................................................  13
0    2.1.  Transferring a File .........................................  15
     2.2.  Basic Kermit Commands .......................................  16
     2.3.  Real Examples ...............................................  19
           2.3.1.  IBM PC to DEC-10 Connection .........................  20
                   2.3.1.1.  Transfer Files Between the DEC-10 and
                             IBM PC Using Server Mode ..................  20
                   2.3.1.2.  Transfer Files Between the DEC-10 and
                             IBM PC Using Send/Receive .................  22
           2.3.2.  IBM PC to TSO Connection ............................  24
                   2.3.2.1.  Transfer Files Between TSO and IBM PC
                             Using Server Mode .........................  24
                   2.3.2.2.  Transfer Files Between TSO and IBM PC
                             Using Send/Receive ........................  26
03.  Kermit Commands ...................................................  29
0    3.1.  Remote and Local Operation ..................................  30
     3.2.  The Command Dialog ..........................................  32
     3.3.  Notation ....................................................  34
     3.4.  Summary of Kermit Commands ..................................  35
     3.5.  The SEND Command ............................................  37
     3.6.  The RECEIVE Command .........................................  39
     3.7.  GET .........................................................  40
     3.8.  SERVER ......................................................  41
     3.9.  BYE .........................................................  41
     3.10.  FINISH .....................................................  41
     3.11.  REMOTE .....................................................  42
     3.12.  LOCAL ......................................................  44
     3.13.  CONNECT ....................................................  45
     3.14.  HELP .......................................................  45
     3.15.  TAKE .......................................................  45
     3.16.  EXIT, QUIT .................................................  45
     3.17.  The SET Command ............................................  46
     3.18.  DEFINE .....................................................  55
     3.19.  SHOW .......................................................  56
     3.20.  STATISTICS .................................................  56
     3.21.  LOG ........................................................  56
     3.22.  TRANSMIT ...................................................  56
     3.23.  INPUT ......................................................  57
     3.24.  OUTPUT .....................................................  57
1ii
-
     3.25.  PAUSE ......................................................  57
     3.26.  SCRIPT .....................................................  57
04.  Kermit Implementations ............................................  59
05.  DECsystem-10 Kermit ...............................................  63
0    5.1.  The DECsystem-10 File System ................................  64
           5.1.1.  TOPS-10 File Specifications .........................  64
           5.1.2.  TEXT FILES AND BINARY FILES .........................  65
           5.1.3.  FILES KERMIT-10 CANNOT HANDLE .......................  67
     5.2.  Program Operation ...........................................  68
     5.3.  Remote and Local Operation ..................................  70
     5.4.  Conditioning Your Job for Kermit ............................  71
     5.5.  Kermit-10 Commands ..........................................  72
           5.5.1.  Commands for File Transfer ..........................  72
           5.5.2.  Server Operation ....................................  76
           5.5.3.  Commands for Local File Management ..................  76
           5.5.4.  The SET, SHOW, and DEFINE Commands ..................  78
           5.5.5.  Program Management Commands .........................  83
     5.6.  Raw Download ................................................  84
     5.7.  Kermit-10 Examples ..........................................  85
06.  TSO Kermit ........................................................  87
0    6.1.  The IBM MVS File System .....................................  88
     6.2.  Program Operation ...........................................  90
           6.2.1.  Starting TSO Kermit .................................  94
           6.2.2.  TSO Kermit Commands .................................  94
     6.3.  Conditioning Your Session for Kermit ........................  96
     6.4.  TSO Kermit Commands .........................................  97
           6.4.1.  Server Operation ....................................  97
           6.4.2.  Commands for File Transfer ..........................  99
           6.4.3.  Commands for Local Data Set Management ..............  99
           6.4.4.  The SET, RESET, and SHOW Commands ................... 101
           6.4.5.  Program Management Commands ......................... 104
     6.5.  TSO Kermit Examples ......................................... 105
     6.6.  Additional Information ...................................... 109
     6.7.  Error Messages .............................................. 109
07.  MS-DOS Kermit for the IBM-PC ...................................... 111
0    7.1.  The MS-DOS File System ...................................... 113
           7.1.1.  File Specifications ................................. 113
           7.1.2.  File Formats ........................................ 114
     7.2.  Program Operation ........................................... 115
     7.3.  Kermit-MS Commands .......................................... 120
           7.3.1.  Commands for Terminal Connection .................... 121
           7.3.2.  Commands for File Transfer .......................... 122
           7.3.3.  Commands Controlling Remote Kermit Servers .......... 127
           7.3.4.  Commands for File Management ........................ 128
           7.3.5.  The SERVER Command .................................. 134
           7.3.6.  The SET Command ..................................... 135
           7.3.7.  The SHOW Command .................................... 150
           7.3.8.  Command Macros ...................................... 151
1                                                                             iii
-
     7.4.  Terminal Emulation .......................................... 152
           7.4.1.  Screen Scroll ....................................... 155
           7.4.2.  Screen Dump ......................................... 155
           7.4.3.  Printer Control ..................................... 156
           7.4.4.  Key Redefinitions ................................... 156
     7.5.  IBM-PC MS Kermit Terminal Emulator Summary .................. 158
           7.5.1.  Keyboard Layout and Characters Sent ................. 158
           7.5.2.  Responses to Characters Received by the Terminal
                   Emulator ............................................ 161
           7.5.3.  DEC VT102 Functions while in VT52 Mode .............. 164
           7.5.4.  Heath-19 Functions .................................. 165
     7.6.  Installing MS-DOS Kermit on a Fixed Disk .................... 167
08.  APPLE-DOS Kermit .................................................. 169
0    8.1.  The DOS 3.3 File System ..................................... 170
     8.2.  Program Operation ........................................... 172
     8.3.  Remote and Local Operation .................................. 174
     8.4.  KERMIT-A2 Commands .......................................... 175
     8.5.  Matching KERMIT-A2 to Your System ........................... 190
0Appendix A -- When Things Go Wrong .................................... 193
0    A.1.  Basic Connection Problems ................................... 193
     A.2.  Terminal Connection Works But The Transfer Won't Start ...... 194
     A.3.  Special Characters .......................................... 196
     A.4.  3270 Protocol Emulators ..................................... 196
     A.5.  The Transfer Starts But Then Gets Stuck ..................... 197
           A.5.1.  The Microcomputer is Hung ........................... 197
           A.5.2.  The Connection is Broken ............................ 197
           A.5.3.  The Disk is Full .................................... 197
           A.5.4.  Message Interference ................................ 198
           A.5.5.  Transmission Delays ................................. 198
           A.5.6.  Noise Corruption .................................... 198
           A.5.7.  Host Errors ......................................... 199
     A.6.  File is Garbage ............................................. 199
     A.7.  Junk After End of File ...................................... 199
     A.8.  Data Set Problems Under TSO ................................. 199
0Appendix B -- ASCII and EBCDIC Tables ................................. 201
0    B.1.  The ASCII Character Set ..................................... 201
     B.2.  ASCII to EBCDIC Translation Table ........................... 205
     B.3.  EBCDIC to ASCII Translation Table ........................... 207
0Appendix C -- Microcomputer to Microcomputer File Transfer ............ 209
0    C.1.  Getting Ready to Use Kermit ................................. 209
     C.2.  Connecting the Computers .................................... 211
     C.3.  Communicating Between Computers ............................. 213
     C.4.  Sending and Receiving Files ................................. 215
     C.5.  Figuring Out Why (If) Kermit Does Not Work .................. 217
1iv
-
1                                                                               v
-
                                 List of Figures
0   Figure 1-1:   A Kermit Packet ...................................  11
    Figure 1-2:   Kermit File Transfer ..............................  12
    Figure 3-1:   Local and Remote Kermits ..........................  31
1vi
-
1                                                                             vii
-
                                  List of Tables
0   Table 7-1:   Kermit-MS Screen Scroll Keys ....................... 155
1viii
-
1Kermit File Transfer Package                                                   1
-
                       Statement of Kermit Software Support
0Kermit is a unique product for the NIH Computer Center.  There are two  personal
 computer  implementations  (IBM  PC and APPLE ][) that can be used with two host
 implementations (IBM TSO and DECsystem-10).  For the various versions there  are
 different points of contact for questions and problems.  These points of contact
 are summarized in the table below.  Users unsure as to which group  to  contact,
 should  contact  the PAL Unit or submit a Programmer Trouble Report (PTR) to get
 clarification.
0                                NIH Users              Non-NIH Users
           Kermit Version        Who to Contact         Who to Contact
           --------------        --------------         --------------
           DECsystem-10          DEC-10 or PTR          DEC-10 or PTR
           TSO                   PAL or PTR             PAL or PTR
           MS-DOS for IBM PC     PWO or PTR             PTR
           APPLE ][              PTR                    PTR
0DEC-10 - DEC-10 Support (496-4823)
 PAL    - Programmer Assistance and Liaison Unit (496-5525)
 PTR    - Programmer Trouble Report (via ENTER PTR in WYLBUR or WYLBUR under TSO;
          via R PTR on the DEC-10)
 PWO    - Personal Workstation Office (496-2282)
0The IBM TSO and  DECsystem-10  implementations  have  been  designated  Level  1
 Software  and  receive  the  full  range  of support services offered by the NIH
 Computer Center.
0The IBM PC and APPLE ][ implementations have been designated Level  2  Software.
 The "Definition of Support for Level 2 Software" can be found on the next page.
0Although other implementations of Kermit (not  supported  by  the  NIH  Computer
 Center)  may  sometimes  work  successfully,  problems that arise are wholly the
 responsibility of the  user.   Unsupported  implementations  may  cease  working
 without  warning  since  Computer  Center  changes are preannounced only if they
 affect supported products.
-
-
-
-
-
-
0                                            Statement of Kermit Software Support
12                                                   Kermit File Transfer Package
-
                             Level 2 Software Support
                              (Revised August, 1986)
-This software product, or a certain portion of it, has  been  assigned  Level  2
 support  status.  The Level 2 designation is made by the Computer Center for any
 of three reasons:  First, an entire software product may be designated  Level  2
 if  it is in test status, or the Center determines that rapid problem resolution
 and long-term product availability can not be ensured with  the  vendor  support
 available.   Second, an interface to specific peripheral hardware devices (e.g.,
 terminals or plotters) will receive Level 2 support, even if  the  remainder  of
 the product is designated Level 1.  Third, an interface to processors not at the
 NIH Computer Utility (e.g., microprocessors  or  other  computer  installations)
 will receive Level 2 support, even if the remainder of the product is designated
 Level 1.
0If a hardware device/terminal is not specifically mentioned in the documentation
 for  this  product,  no  interface  to it is supported (even as Level 2).  While
 unsupported devices may sometimes function with  the  interfaces  provided,  any
 problems  encountered are wholly the user's responsibility.  This support policy
 is necessary in order to provide services for the large number of devices (e.g.,
 terminals,  plotters,  microprocessors) commonly owned/used by end users.  It is
 not practical for the NIH Computer Center  to  be  familiar  with  the  hardware
 characteristics of the myriad devices that can take advantage of these services.
0Users of this product should be  fully  aware  that  the  support  for  Level  2
 software  provides  documentation,  non-critical Programmer Trouble Report (PTR)
 service,  and  limited  INTERFACE  preannouncement  of  changes,  but  does  not
 guarantee  continued  availability  or conversion assistance if this software is
 discontinued by the vendor or the Computer Center.
0In addition, no Programmer Assistance and Liaison (PAL) Unit consulting will  be
 available  on  questions  pertaining  to  the  use  of  or problems with Level 2
 software.  The Computer Center  will  accept  PTRs  for  problems  if  they  are
 accompanied  by all of the documentation necessary for diagnosis and resolution.
 When the Computer Center staff member responsible for the problem area described
 in  a Level 2 PTR receives all pertinent documentation on the problem, the staff
 member will frequently act as a technical guide with  the  burden  of  the  work
 remaining with the user.
0Resolving or circumventing problems with Level 2 software may require  resources
 (e.g., hardware/terminals or source code) that are not available to the Computer
 Center staff.  Since the Computer Center is often completely unfamiliar with the
 specific  devices/terminals involved, the vendor may be the sole source of vital
 information required for problem resolution or circumvention.  For this  reason,
 the "Critical" designation for PTRs is not applicable and will be disregarded by
 the Center.  Once a PTR and all supporting  documentation  is  received  by  the
 Computer  Center,  the  work to get a resolution is a mutual effort of the user,
 the Computer Center and the author or vendor for those  products  designated  as
 Level 2.  Since the Computer Center must rely on the cooperation/interest of the
 vendor/developer of a product, it is possible that some problems  may  never  be
 resolved.
-
 Statement of Kermit Software Support
1Kermit File Transfer Package                                                   3
-
 The effects of the support given by the Computer  Center  to  Level  2  software
 should be thoroughly considered before incorporating this software into critical
 applications.  It must be stressed that  the  proper  functioning  or  long-term
 availability of Level 2 software cannot be guaranteed by the Computer Center.
0The following chart outlines Computer Center  services  available  for  Level  2
 software.  For further information on Levels of software and how to submit PTRs,
 see the appropriate section of the Computer Center Users  Guide    If  questions
+                                   ________ ______ _____  _____.
 remain  on this policy, contact the PAL Unit Consulting Desk of the NIH Computer
 Center.
-SERVICE                            SUPPORT FOR LEVEL 2 SOFTWARE
0CONSULTING (PAL DESK)
   a) personal visit                        No
   b) telephone                             No
                                         (Users will have to rely
                                         on technical documentation
                                         provided by the Computer
                                         Center and their own
                                         resources)
0PROGRAMMER TROUBLE REPORT (PTR)            Yes
0"CRITICAL" PTR DESIGNATION                 No
0REFUNDS                                    Yes
0DOCUMENTATION                              Yes
0TRAINING                                   Resources
                                            permitting
 SOFTWARE MAINTENANCE
  a) Currency maintained with respect       Resources
     to new versions and facilities         permitting
  b) Formal change testing (Test Job        No
     Stream)
  c) Informal change testing                Yes
  d) Guarantee of orderly, fully            No
     documented conversion if product
     is discontinued
  e) Preannouncement in INTERFACE of        Resources
     all new facilities                     permitting
  f) Preannouncement in INTERFACE of        Resources
     changes which cause old versions       permitting
     of programs to function
     incorrectly or differently
  g) Preannouncement in INTERFACE of        Yes
     discontinuance of support or changes
     in support status (Level)
  h) Preventive and corrective fixing       Resources
     by Computer Center staff               permitting
-                                            Statement of Kermit Software Support
14                                                   Kermit File Transfer Package
-
                                     Preface
0Kermit is the name of a protocol for transferring files  from  one  computer  to
 another over ordinary asynchronous terminal connections.  Kermit implementations
 have been written for many different computers, and in general any two computers
 that  have  Kermit can exchange sequential files correctly and completely.  This
 manual describes the use of Kermit.
0This manual describes an "ideal" Kermit implementation and  then  describes  the
 Kermit  implementations  supported  by  the NIH Computer Center in detail.  Each
 implementation of Kermit has a HELP facility that serves as an adjunct  to  this
 manual.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0Preface
1Kermit File Transfer Package                                                   5
-
                           History and Acknowledgements
0The Kermit file transfer protocol was designed at the Columbia University Center
 for  Computing  Activities (CUCCA) in 1981-82 mainly by Bill Catchings and Frank
 da Cruz.  Bill wrote the first two programs, one for the  DECsystem-20  and  one
 for a CP/M-80 microcomputer.
0The initial objective was to allow CUCCA users on  DEC-20  and  IBM  timesharing
 systems  to  archive their files on microcomputer floppy disks.  The design owes
 much to the ANSI and ISO models, and ideas were borrowed from  similar  projects
 at Stanford University and the University of Utah.  The protocol was designed to
 accommodate the "sensitive" communications front end of the  full-duplex  DEC-20
 system as well as the peculiarities of half-duplex IBM mainframe communications.
 The protocol was soon implemented successfully on CUCCA IBM 4341  systems  under
 VM/CMS by Daphne Tzoar of CUCCA.
0Meanwhile it was becoming apparent that Kermit was useful  for  more  than  just
 file archiving; IBM PCs were beginning to appear in the offices and departments,
 and there arose a general need for file transfer  among  all  Columbia  systems.
 Daphne soon had prepared an IBM PC implementation.
0After the initial success with Kermit, it was presented at conferences  of  user
 groups  like  DECUS and SHARE, and requests for Kermit began to be received from
 other sites.  Since the protocol description had  been  documented,  some  sites
 wrote  their  own implementations for new computers, or adapted one of the CUCCA
 implementations to run on additional systems, and sent back these  new  versions
 to  Columbia so they could be shared with others.  In this way, Kermit has grown
 to support more than 100 different systems; it has been sent  on  magnetic  tape
 from  Columbia  to  thousands  of  sites in dozens of countries, and has reached
 hundreds or thousands more through various user groups and networks.
0Thanks are due  to  the  hundreds  of  individuals  and  institutions  who  have
 contributed over the years to making Kermit what it is today.
0Credit for the Kermit  implementations  described  in  this  manual  belongs  to
 Columbia  University and Utah State University (IBM PC), the National Institutes
 of Health (TSO), Stevens Institute of Technology (DEC-10), and the University of
 Maryland (Apple ][).
0The Kermit protocol was named after Kermit the  Frog,  star  of  the  television
 series  THE  MUPPET  SHOW;  the  name  Kermit  is  used  by permission of Henson
 Associates, Inc., New York.
0A two-part article describing the Kermit protocol appeared in the June and  July
 1984 issues of BYTE Magazine.
0The book Kermit, A File Transfer Protocol  by  Frank  da  Cruz,  Digital  Press,
 Bedford,  MA 01730 (1986) describes Kermit in detail, from the points of view of
 the user, of computer professionals who have to install it or support  its  use,
 and  of  programmers  who  wish  to  write  new Kermit implementations, and also
 contains tutorial sections on data communications,  file  organization,  plus  a
 detailed troubleshooting guide, along with many illustrations and tables.
-
                                                                          Preface
16                                                   Kermit File Transfer Package
-
                                    Disclaimer
0Neither Columbia University, nor the National  Institutes  of  Health,  nor  the
 editor,  nor  the  authors  of  the  individual  chapters, nor any individual or
 institution contributing Kermit implementations or documentation to the Columbia
 University Kermit Distribution, acknowledge any liability for any claims arising
 from use or  misuse  of  Kermit  implementations  or  for  inaccuracies  in  the
 documentation  or  bugs  in  the  implementations.   Kermit  implementations are
 produced on a voluntary basis and contributed freely for public use in the  hope
 that  they will be useful, but without any kind of warranty or guarantee, or any
 commitment to address or fix problems.  In practice, Kermit implementations  and
 documentation  are  contributed  in  good  faith,  and  will  be  supported on a
 best-effort basis, time and other commitments permitting.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
 Preface
1Kermit File Transfer Package                                                   7
-
                              How to Use This Manual
0Section 2, How to Use Kermit, tells all you need to know to  transfer  files  in
 most  cases,  and  shows some specific examples.  Note that in all examples, the
 user entered fields are underlined to separate the computer  generated  messages
 and prompts from the commands given by the user.
0If you follow the examples in Section 2 but you can't make a terminal connection
 or  you  can't  transfer  files successfully, consult Appendix A, When Things Go
 Wrong.
0If you expect to be a heavy user of Kermit, you should read  Section  3,  Kermit
 Commands,  which  describes  all the features of Kermit in detail.  You may find
 that familiarity with the material in  this  section  will  help  you  get  past
 difficulties  that  can  crop up when you are making new kinds of connections or
 transferring unusual kinds of files.  You will also find  descriptions  of  some
 advanced  file  management  features  that  have  been  omitted from the earlier
 sections.
0Section 4, Kermit Implementations, briefly lists the systems for which Kermit is
 available  as  of this writing.  The subsequent chapters describe the particular
 implementations that are supported by the NIH Computer Center.  You should  read
 the  appropriate  section  for each system with which you are using Kermit; each
 section describes the file naming conventions and other system features that are
 important  to Kermit users, and lists the Kermit commands for that system mainly
 in terms of their differences from the "ideal" Kermit described in Section 3.
0Appendix B shows the ASCII character set and the  translation  tables  used  for
 ASCII/EBCDIC  conversion by TSO Kermit.  Users wanting to transfer files between
 microcomputers should read  Appendix  C,  Microcomputer  to  Microcomputer  File
 Transfer.
-
-
-
-
-
-
-
-
                                                           How to Use This Manual
18                                                   Kermit File Transfer Package
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0How to Use This Manual
1Kermit File Transfer Package                                                   9
-
 1.  Introduction
0There is an ever-increasing need  to  move  information  from  one  computer  to
 another.  Information can be exchanged using magnetic media -- tapes or disks --
 or over networks.  Networks  are  expensive,  and  when  your  computer  is  not
 connected  to  one  (or to the right one), you must find other means to transfer
 information.  In the early  days  of  computing,  magnetic  media  formats  were
 relatively  standardized,  but  with  the  arrival of microcomputers things have
 changed:  most microcomputer users have no access to tapes, and disk formats are
 incompatible  between  most  microcomputer  makes  and  models.   Even when disk
 formats agree, the disk must be physically moved from one system to the other in
 order for information to be exchanged -- the effort and delay can be significant
 if the systems are widely separated.
0The telecommunication line provides an  alternative  to  networks  and  magnetic
 media.   Asynchronous  telecommunication is the method used by most terminals to
 connect to most computers.  When  dedicated  "hardwired"  connections,  such  as
 those  found  between  a  timesharing  computer and its local terminals, are not
 available, computer users can create their own connections with a telephone  and
 a modem.
0Most computers come equipped with asynchronous telecommunications interfaces, or
 "serial ports," which allow them to act as, or communicate with, terminals.  The
 question is how to use the serial  port  to  exchange  data.   Fortunately,  the
 standards for connecting terminals to computers are almost universally followed:
 connector configuration (DB-25 or DB-9), transmission signals  (EIA  RS-232),  a
 commonly accepted set of transmission speeds (bits per second), and a convention
 for encoding characters in  storage  and  during  transmission  (ASCII).   These
 standards  provide  the  physical  medium  and  the data format, but they do not
 specify a process for exchanging data.
-
-
-
-
-
-
-
-
0                                                       Section 1 -- Introduction
110                                                  Kermit File Transfer Package
-
 1.1.  Why Kermit?
0When data is transmitted from one computer to another,  the  receiving  computer
 has to be instructed to take in the data and put it somewhere, and it also needs
 a way of ensuring that the data has been received correctly  and  completely  in
 spite of several factors that will tend to interfere with this process:
0    1.  Noise -- It is rarely safe to assume that there will  be  no  electrical
         interference  on  a  line;  any long or switched data communication line
         will have occasional interference, or noise, which typically results  in
         garbled  or  extra  characters.   Noise corrupts data, perhaps in subtle
         ways that might not be noticed until it's too late.
0    2.  Timing -- Data must not come in faster than the  receiving  machine  can
         handle  it.  Although line speeds at the two ends of the connection must
         match before communication can take place, the receiving  machine  might
         not  be  able  to  process  a steady stream of input at that speed.  Its
         central processor may be too slow or too heavily loaded, or its  buffers
         too  full or too small.  The typical symptom of a timing problem is lost
         data; most operating systems will simply discard incoming data they  are
         not prepared to receive.
0    3.  Line Outages -- A line may stop working for short periods because  of  a
         faulty  connector,  loss  of  power,  or  similar  reason.  On dialup or
         switched connections, such intermittent failures may cause  the  carrier
         to drop and the connection to be closed, but for any connection in which
         the carrier signal is not used, the symptom will be lost data.
0To prevent corruption of data  and  to  synchronize  communication,  cooperating
 computers  can  send  special  messages  to  one  another  along  with the data.
 Intermingling of control information with data together requires a set of  rules
 for  distinguishing control messages from data, and specifying what the messages
 are and the actions associated with each message.  Such a set of rules is called
 a protocol.
0Kermit is a file transfer protocol.  It is specifically designed for transfer of
 sequential  files  over  ordinary serial telecommunication lines.  Kermit is not
 necessarily better than other terminal-oriented file transfer protocols  but  it
 is free, it is well documented, and it has been implemented compatibly on a wide
 variety of microcomputers and mainframes.
-
-
-
-
-
 Introduction -- Section 1
1Kermit File Transfer Package                                                  11
-
 1.2.  How Kermit Works
0Kermit transfers data by encapsulating it in  packets  of  control  information.
 This  information includes a synchronization marker, a packet sequence number to
 allow detection of lost packets, a length indicator,  and  a  "block  check"  to
 allow verification of the data, as shown in Figure 1-1.
0    +------+------+------+------+--------- - - - -+-------+
     | MARK | LEN  | SEQ  | TYPE | DATA            | CHECK |
     +------+------+------+------+--------- - - - -+-------+
0                  Figure 1-1:  A Kermit Packet
0The MARK (usually an ASCII Control-A character) appears at the beginning of  the
 packet.   The  next  character  is a length field (LEN), specifying how long the
 rest of the packet is.  The sequence number (SEQ) is  used  to  detect  lost  or
 duplicated  packets;  retransmission is requested for lost packets and duplicate
 packets are discarded.  The TYPE field specifies  whether  the  packet  contains
 data  or  control  information.  The CHECK field contains a quantity obtained by
 combining all the other characters in the packet  together  in  one  of  several
 ways;  the  sender  computes  this value and sends it.  The packet receiver also
 computes the value and checks it against the value  sent;  if  they  agree,  the
 packet  is  accepted;  if  they disagree, then the packet has been corrupted and
 retransmission is requested.  The DATA field contains up  to  90  characters  of
 data.   All fields except the mark are encoded as printable ASCII characters, to
 prevent host or network interference.  Figure  1-2  shows  how  a  typical  file
 transfer  proceeds.   Figure  1-2 does not show how Kermit recovers from errors.
 Very briefly, here's how it works:
0   - If a packet is corrupted in transit by noise or  loss  of  characters,  the
      block  check  will  be  wrong.   A  file  receiver  will  NAK  ("negatively
      acknowledge") a corrupted packet, which causes the sender to retransmit the
      same    packet.     A   file   sender   only   receives   ACKs   ("positive
      acknowledgements") and NAKs from the receiver; a corrupted ACK or NAK  from
      the receiver is treated exactly the same as a NAK.
0   - If the file sender does not receive an ACK within  the  prescribed  timeout
      interval,  it  retransmits  the same packet.  If the file receiver does not
      receive an expected packet within the timeout interval, it sends a NAK  for
      the expected packet.
-
-
-
-
-
                                                        Section 1 -- Introduction
112                                                  Kermit File Transfer Package
-
   Sender                 Receiver
0  Send-Init ------------->         Sender and Receiver exchange greetings
        <-------------------- ACK
0  File-Header ----------->         Sender sends first file name to Receiver
        <-------------------- ACK   Receiver acknowledges
0  File-Data ------------->         Sender sends first file data packet
        <-------------------- ACK
0  File-Data ------------->         Sender sends second file data packet
        <-------------------- ACK
0  File-Data --xx~~~p'''-->         Third data packet is corrupted by noise
        <-------------------- NAK    and Receiver negatively acknowledges it
0  File-Data ------------->         Sender retransmits third packet
        <-------------------- ACK
0  File-Data packets are sent and acknowledged until the whole file is sent
0  End-Of-File ----------->         Sender indicates first file is complete
        <-------------------- ACK
0  File-Header ----------->         Name second of file
        <-------------------- ACK
0  File-Data ------------->         First data packet for second file
        <-------------------- ACK
0  File-Data packets are sent and ack'd until the whole file is sent
0  End-Of-File ----------->         Sender indicates second file is complete
        <-------------------- ACK
0  End-Of-Transaction ---->         Sender indicates no more files to come
        <-------------------  ACK
0                      Figure 1-2:  Kermit File Transfer
0Several encoding, compression, and block check options are provided.   Very  few
 assumptions  are  made  about the capabilities of either computer, so the Kermit
 protocol can work between many different kinds  of  systems.   The  protocol  is
 described  in  detail  in  the  Kermit  Protocol Manual (available from Columbia
 University), and in the BYTE Magazine article on Kermit, published in  the  June
 and July 1984 issues.
-
-
-Introduction -- Section 1
1Kermit File Transfer Package                                                  13
-
 2.  How to Use Kermit
0Kermit embodies a set of rules  for  transferring  files  reliably  between  two
 computers.   Usually,  one  computer  is  a  large  system  (a  host,  such as a
 timesharing system with many terminals), and the other is  a  personal  computer
 (PC),  although  use  of Kermit between two personal computers is also possible.
 The host believes that the PC is an ordinary terminal.  In order for the  Kermit
 protocol  to  work,  a  Kermit  program  must  be  running  on  each  end of the
 communication line -- one on the host, one on the PC.
0Your task is just to get the two Kermits started.  You  have  to  use  a  single
 keyboard  and screen to talk to two different computers, two different programs.
 Let's talk about a common case:  you are sitting at a  personal  computer  (PC),
 which  has  a serial communication port.  The serial port is connected to a host
 computer using a dialup modem.
0Normally, when you use your PC, you are "talking" directly to it; your  commands
 are  interpreted  directly  by  the PC's operating system (CP/M, PC-DOS, MS-DOS,
 UNIX, etc.), or by some  program  that  runs  on  the  PC  (an  editor,  a  text
 formatter, a spreadsheet...). The version of Kermit on your PC is a program like
 any other, but it has a  special  ability  to  either  interpret  your  commands
 directly,  like  other  programs,  or to pass everything you type through to the
 other, remote computer.  When  you  tell  Kermit  to  CONNECT,  it  sends  every
 character you type out the serial port to the remote computer, and it puts every
 character that comes in the serial port from the remote computer onto the screen
 of your PC.  This is called terminal emulation -- one computer acts as though it
 were a terminal on another.  You are now "talking" to the remote  computer,  and
 the PC is mimicking a terminal.
0Kermit, like most interactive programs, has a prompt.  The prompt is a string of
 characters  it  types on the left margin to indicate that it is ready for you to
 type a command.  Kermit's prompt is normally "Kermit-xx>."   The  xx  identifies
 the  implementation  of  Kermit;  the  Kermit  that runs on the DEC-10 is called
 "Kermit-10" and its prompt is "Kermit-10>"; the Kermit that runs on the  IBM  PC
 microcomputers  is called "Kermit-MS" and its prompt is "Kermit-MS>"; the Kermit
 that runs under TSO is "Kermit-TSO>", and so  forth.   If  you  become  confused
 about  which  Kermit  you  are talking to, the prompt should provide a clue.  In
 addition, most Kermits print an informative message like
0  [Connecting to host, type Control-] C to return to PC]
0when you CONNECT, and type another message like
0  [Back to PC]
0when you return.
0Having "connected" to the host, there must be a way for you to "get back" to the
 PC.   This  is  accomplished  by  an  escape  sequence.   As  Kermit passes your
 characters through to the host, it checks each one to  see  if  it's  a  special
 predefined  escape  character  (usually  not the key labelled ESC).  When the PC
 sees this character, it stops ignoring you -- you are once  again  "talking"  to
-
                                                   Section 2 -- How to Use Kermit
114                                                  Kermit File Transfer Package
-
 the  PC,  not  the host.  The escape character is normally chosen to be one that
 you will not need to type while talking to the host, and one  that  is  hard  to
 type  by  accident -- it's usually a control character, such as Control-], which
 is entered by holding down the  key  marked  CTRL  or  CONTROL  and  typing  the
 indicated  character  (in  this  case, a right bracket "]").  The CTRL key works
 just like a SHIFT key.  Control characters are written either as CTRL-]  or  X],
 where ] is the character to be typed while holding down CTRL.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
 How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  15
-
 2.1.  Transferring a File
0To transfer a file, you must first run the Kermit program on your PC.  Then tell
 Kermit to CONNECT you to the host.  Next dial the telephone number of the remote
 Kermit's modem and now you're talking to the remote host -- at  this  point  you
 must login/logon, and then run Kermit on the host.
0Now you have a Kermit on each end of the wire.  The next step is  to  tell  each
 Kermit what to do.  Suppose you want to transfer a file from the host to the PC;
 you would first tell the host to go into server mode with  the  SERVER  command,
 then "escape" back to the PC Kermit and tell it to GET (download) the file.  The
 transfer begins -- you can sit back and watch, or go do something else.  The  PC
 Kermit  will  produce a running display on your screen as the transfer proceeds,
 and will notify you when it is complete.
0The desired file is now on your PC's disk.  The Kermit protocol has ensured that
 the  file  arrived  correctly and completely.  Now if you have no other files to
 transfer, you must clean up after yourself:  type BYE to terminate Kermit on the
 host,  your  session on the host, and Kermit on the PC.  Now you can do whatever
 you had planned for your file -- edit it, print it on your PC printer, etc.   To
 transfer a file from the PC to the host (upload), issue the SEND command instead
 of the GET command.
0Kermit allows an alternative to the server  mode  for  transferring  files,  the
 send/receive  mode.   The send/receive mode was the only mode available in older
 implementations of Kermit and is generally more cumbersome to  use  than  server
 mode.   If  you  were  downloading using send/receive mode, you would start your
 session just as described above.  But instead  of  typing  SERVER  to  the  host
 Kermit,  you  tell  Kermit to SEND the file, then "escape" back to the PC Kermit
 and tell it to RECEIVE the file.  The PC Kermit will produce a  running  display
 on  your  screen  as  the  transfer  proceeds,  and  will  notify you when it is
 complete.  To cleanup, CONNECT back to the host, exit from Kermit on  the  host,
 logout/logoff from the host, "escape" back to PC Kermit and exit from it.
0The Kermit protocol, and most Kermit programs, allow you to send a file reliably
 from  the  host  to the PC, from the PC to the host, from host to host, or PC to
 PC, usually without any special regard for the nature of the particular machines
 involved.   Most  implementations  also allow files to be sent in groups, with a
 single command, such as "send *.*". The scenario for each of these is  the  same
 as above -- only the details of how to establish the actual connection differ.
0Kermit works best with "text" (or "printable") files -- files composed  only  of
 letters,  digits,  punctuation  marks,  carriage  returns, tabs, and so forth --
 since these can be represented on almost any kind of computer.  Kermit  is  also
 able to transfer "binary" files -- files such as executable programs -- composed
 of arbitrary bit patterns, but binary files normally are meaningful only to  the
 kind  of computer on which they are generated.  Nevertheless, Kermit can usually
 move such files from system A to system B (where they are not much use) and back
 to system A in their original condition, although in most cases special measures
 must be taken to accomplish this.
-
-                                                  Section 2 -- How to Use Kermit
116                                                  Kermit File Transfer Package
-
 We'll look at some concrete examples in Section 2.3.  First  you  need  to  know
 what the basic Kermit commands are.
-
 2.2.  Basic Kermit Commands
0These are generic descriptions of the  most  basic  Kermit  commands.   Detailed
 descriptions will come later.  In these descriptions, local refers to the system
 that you are using directly (IBM PC, APPLE ][), remote refers to the  system  to
 which  you  are CONNECTed via Kermit (DECsystem-10, TSO).  Commands may take one
 or more operands on the same line, and are terminated by a carriage return.
-CONNECT
0Make a "virtual terminal" connection to the remote system.  To "escape"  from  a
 virtual  terminal  connection  back  to  the  local Kermit, type Kermit's escape
 character (e.g., Control-]), followed by the letter "C".
0NOTE: Control-], Ctrl-], and X] are three equivalent notations which mean to use
       the  CONTROL  key  like a SHIFT key with respect to the next character (in
       this case the right bracket key).
-SERVER
0Cease taking commands from the keyboard and receive all further instructions  in
 the  form  of  Kermit  packets  from the other (local) Kermit.  Issue the SERVER
 command to the remote Kermit only, never to the local Kermit.  The local  Kermit
 must  have  commands  for  communicating with remote servers; these include GET,
 SEND, FINISH, and BYE or LOGOUT.
0After issuing SERVER, return to  the  local  system  and  issue  server-directed
 commands  from  there.   If  your  local  Kermit does not have a BYE, LOGOUT, or
 FINISH command, then it does not have the full ability  to  communicate  with  a
 Kermit  server and you should not put the remote Kermit into server mode.  These
 commands (used to exit from server mode) are described below.
0Any non-standard parameters should be selected with SET commands before  putting
 the remote Kermit in server mode.
-
-
-
-
-How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  17
-
 GET remote-filespec
0Request a remote Kermit operating in server mode to send the file or file  group
 specified  by  remote-filespec.   A file group is usually specified by including
 "wildcard" characters like "*" in the file specification.  Examples:
0      GET foo.txt
       GET *.for
0The GET command can be issued to the local Kermit only.   This  means  that  you
 must have CONNECTed to the other system, logged in, run Kermit there, issued the
 SERVER command, and escaped back to the  local  Kermit.   Note  that  the  local
 Kermit  does  not attempt to validate the remote-filespec.  If the server cannot
 parse it, or  cannot  access  the  specified  file(s),  it  will  send  back  an
 appropriate error message.
-SEND filespec
0Send the file or file group specified by filespec from this Kermit to the  other
 Kermit.   The  name  of  each  file  is  passed to the other Kermit in a special
 control packet so it can be stored there with the same name.  A  file  group  is
 usually  specified  by  including  "wildcard"  characters  like  "*" in the file
 specification.  Examples:
0      SEND foo.txt
       SEND *.for
0Some implementations of Kermit may not support transfer of  file  groups;  these
 versions would require a separate SEND command for each file to be transferred.
-BYE or LOGOUT
0Shut down the remote server and exit from Kermit.  This will cause  the  job  at
 the remote end to log itself out.  You need not connect back and clean up unless
 you get an error message in response to this  command  (for  instance,  if  your
 logged-out  disk  quota  is  exceeded  on  the remote host).  BYE and LOGOUT may
 differ in their effect on the local Kermit.
-FINISH
0Shut down the server without having it log itself out, and don't exit  from  the
 local Kermit.  A subsequent CONNECT command will put you back at your session on
 the remote host, at system or Kermit command level.
-EXIT or QUIT
0Exit from Kermit back to the operating system.
-
0                                                  Section 2 -- How to Use Kermit
118                                                  Kermit File Transfer Package
-
 HELP
0Type a summary of Kermit commands and what they do.
-RECEIVE
0Receive a file or file group from the other Kermit.  If an incoming file name is
 not  legal,  then  the receiving Kermit may attempt to transform it to a similar
 legal name.  Options may be provided for handling filename collisions.  Note the
 distinction between the RECEIVE and GET commands:  RECEIVE instructs the program
 to wait passively; whereas, GET actively sends  a  request  to  a  server.   The
 RECEIVE command is not used when the remote Kermit is in server mode.
-SET
0Establish various non-standard settings, such as CONNECT escape character,  file
 characteristics, communication line number, speed, parity, or flow control.  All
 of these are explained later.
-SHOW
0Display the values of SET options.
-?
0Typed almost anywhere within a Kermit command:  List the commands,  options,  or
 operands that are possible at this point.  This command may or may not require a
 carriage return, depending on the operating system.
-
-
-
-
-
-
-
-How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  19
-
 2.3.  Real Examples
0Kermit can be used in several ways:  from a PC that is  connected  to  a  larger
 host computer; from a host computer which is connected to another host; from one
 PC to another.  This section restricts its examples to PC and  host  connections
 that are supported at NIH.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0                                                  Section 2 -- How to Use Kermit
120                                                  Kermit File Transfer Package
-
 2.3.1.  IBM PC to DEC-10 Connection
-2.3.1.1.  Transfer Files Between the DEC-10 and IBM PC Using Server Mode
0User responses are underlined  notes are enclosed in brackets or are  listed  to
+                   __________,
 the far right of the relevant input/output.
0A>k_____                      ; Start Kermit on the IBM PC.
+  _ermit
 IBM-PC Kermit-MS V2.29   26 May 86
 Type ? for help
0Kermit-MS>comment           DO WYLBUR for WYLBUR
 Kermit-MS>comment           DO DEC10  for DEC-10
 Kermit-MS>comment           DO TSO    for TSO
 Kermit-MS>comment           DO 3270   for Protocol Conversion Facility
 Kermit-MS>                    ; This is the Kermit prompt for the PC.
 Kermit-MS>do _____            ; Set Kermit parameters for the DEC-10.
+          ___dec10
0[Commands issued from the DEC10 macro are displayed]
0Kermit-MS>connect             ; Connect to the communications line.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0ATDT49_2222                   ; Issue modem command to dial the DEC-10.
+______2____
0[Assumes Hayes-compatible modem; dial 492-2222 using a  manual  dial  modem;  if
  using  an  AT&T  2224B  modem,  type  AT4922222 or use the interactive commands
  described in the NIH Terminal Operators Guide.]
0[Various modem messages]
0CONNECT                       ; You are now connected to the DEC-10.
0[Type a carriage return.]
0NIH Timesharing               ; The DEC-10 system prints its herald.
0NIH Tri-SMP 7.02-GG      15:35:24 TTY24 system 1378/1381/1453
 Connected to Node GRUMPY(42) Line # 12
 Please LOGIN or ATTACH
0.login prj,prg                ; Login with your PPN.
+ _____________
 JOB 56 NIH Tri-SMP 7.02-GG      TTY24
 Password:______               ; Enter your password.
0[DEC-10 messages related to login]
0.r ______                     ; Start Kermit on the DEC-10.
+ __kermit
0TOPS-10 KERMIT version 3(133)
-
 How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  21
-
 [Issue SET commands as needed.  If you want to transfer binary data, originating
  on the PC, change the FILE BYTE-SIZE setting to 8 (i.e., SET FILE BYTE-SIZE 8).
  All parameter values that you want to change must  be  set  before  the  remote
  Kermit  is  placed  in  server  mode.   These  parameters  and their values are
  described under the SET command in the DECsystem-10 Kermit section.]
0Kermit-10>server              ; Tell the DEC-10 Kermit to be a server.
+          ______
0[Kermit Server running on the DEC host.  Please type  your  escape  sequence  to
 return  to  your  local  machine.  Shut down the server by typing the Kermit BYE
 command on your local machine.]
0X]c                           ; Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>get ________        ; Get the DEC-10 file named test.pas.
+          ____test.pas
0[PC screen shows file transfer status during download of the DEC-10 file to  the
  IBM PC.]
0Kermit-MS>send ________       ; Send the IBM PC file named test.for.
+          _____test.for
0[PC screen shows file transfer status during upload of the IBM PC  file  to  the
  DEC-10.]
0Kermit-MS>bye                 ; Shut down the DEC-10 Kermit & session, PC Kermit.
+          ___
 A>                            ; Back at PC-DOS automatically.
0[Here you can do some work on the microcomputer, edit files, etc.]
-
-
-
-
-
-
-
-
0                                                  Section 2 -- How to Use Kermit
122                                                  Kermit File Transfer Package
-
 2.3.1.2.  Transfer Files Between the DEC-10 and IBM PC Using Send/Receive
0User responses are underlined  notes are enclosed in brackets or are  listed  to
+                   __________,
 the far right of the relevant input/output.
0A>k_____                      ; Start Kermit on the IBM PC.
+  _ermit
 IBM-PC Kermit-MS V2.29   26 May 86
 Type ? for help
0Kermit-MS>comment           DO WYLBUR for WYLBUR
 Kermit-MS>comment           DO DEC10  for DEC-10
 Kermit-MS>comment           DO TSO    for TSO
 Kermit-MS>comment           DO 3270   for Protocol Conversion Facility
 Kermit-MS>                    ; This is the Kermit prompt for the PC.
 Kermit-MS>do _____            ; Set Kermit parameters for the DEC-10.
+          ___dec10
0[Commands issued from the DEC10 macro are displayed]
0Kermit-MS>connect             ; Connect to the communications line.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0ATDT49_2222                   ; Issue modem command to dial the DEC-10.
+______2____
0[Assumes Hayes-compatible modem; dial 492-2222 using a  manual  dial  modem;  if
  using  an  AT&T  2224B  modem,  type  AT4922222 or use the interactive commands
  described in the NIH Terminal Operators Guide.]
0[Various modem messages]
0CONNECT                       ; You are now connected to the DEC-10.
0[Type a carriage return.]
0NIH Timesharing               ; The DEC-10 system prints its herald.
0NIH Tri-SMP 7.02-GG      15:35:24 TTY24 system 1378/1381/1453
 Connected to Node GRUMPY(42) Line # 12
 Please LOGIN or ATTACH
0.login prj,prg                ; Login with your PPN.
+ _____________
 JOB 56 NIH Tri-SMP 7.02-GG      TTY24
 Password:______               ; Enter your password.
0[DEC-10 messages related to login]
0.r ______                     ; Start Kermit on the DEC-10.
+ __kermit
0TOPS-10 KERMIT version 3(133)
0[Issue SET commands as needed.  If you want to transfer binary data, originating
-
0How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  23
-
  on the PC, change the FILE BYTE-SIZE setting to 8 (i.e., SET FILE BYTE-SIZE 8).
  All parameter values that you want to change must  be  set  before  the  remote
  Kermit  is  issued  the  SEND  command.   These parameters and their values are
  described under the SET command in the DECsystem-10 Kermit section.]
0Kermit-10>send ________       ; Send the DEC-10 file named test.rpt.
+          _____test.rpt
 X]c                           ; Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>receive             ; Tell the IBM PC a file is coming.
+          _______
0[PC screen shows file transfer status during download of the DEC-10 file to  the
  IBM PC.]
0Kermit-MS>connect             ; Connect to the DEC-10.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0[In this example DECsystem-10 Kermit is reset to receive a PC binary file.]
0Kermit-10>set file byte-size 8  ; Set parameter for PC binary file transfer.
+          ____________________
 Kermit-10>receive             ; Tell the DEC-10 a file is coming.
+          _______
 X]c                           ; Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>set eof noctrl-z    ; Set end of file handling for binary file.
+          ________________
 Kermit-MS>send _____dat       ; Send the IBM PC file named test.dat.
+          _____test.___
0[PC screen shows file transfer status during upload of the IBM PC  file  to  the
  DEC-10.]
0Kermit-MS>connect             ; Connect to the DEC-10.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0Kermit-10>quit                ; Get out of the DEC-10 Kermit.
+          ____
0.kjob__                       ; Logout.
+ ____/d
0[DEC-10 messages related to logout]
0X]c                           ; Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>quit                ; Shut down the PC Kermit.
+          ____
 A>                            ; Back at PC-DOS.
0[Here you can do some work on the microcomputer, edit files, etc.]
-
0                                                  Section 2 -- How to Use Kermit
124                                                  Kermit File Transfer Package
-
 2.3.2.  IBM PC to TSO Connection
-2.3.2.1.  Transfer Files Between TSO and IBM PC Using Server Mode
0User responses are underlined  notes are enclosed in brackets or are  listed  to
+                   __________,
 the far right of the relevant input/output.
0A>k_____                      Start Kermit on the IBM PC.
+  _ermit
 IBM-PC Kermit-MS V2.29   26 May 86
 Type ? for help
0Kermit-MS>comment           DO WYLBUR for WYLBUR
 Kermit-MS>comment           DO DEC10  for DEC-10
 Kermit-MS>comment           DO TSO    for TSO
 Kermit-MS>comment           DO 3270   for Protocol Conversion Facility
 Kermit-MS>                    This is the Kermit prompt for the PC.
 Kermit-MS>do ___              Set Kermit parameters for TSO.
+          ___tso
0[Commands issued from TSO macro are displayed]
0Kermit-MS>connect             Connect to the communications line.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0ATDT49_____                   Issue modem command to dial TSO.
+______22223
0[Assumes Hayes-compatible modem; dial 492-2223 using a  manual  dial  modem;  if
  using  an  AT&T  2224B  modem,  type  AT4922223 or use the interactive commands
  described in the NIH Terminal Operators Guide.]
0[Various modem messages]
0CONNECT                       You are now connected to TSO.
 logon                         Start the TSO LOGON process.
+_____
 INITIALS? iii
+          ___
 ACCOUNT? aaaa
+         ____
 KEYWORD? kkk
+         ___
 TERMINAL? none
+          ____
 BOX? bbb
+     ___
 AAAAIII LOGON IN PROGRESS AT 11:26:19 ON JUNE 11, 1986
  NIH/DCRT/CCB TSO
0[TSO messages related to logon]
0READY                         TSO LOGON process complete.
 kermit                        Start TSO Kermit.
+______
 NIH KERMIT-TSO VERSION 1.0
0[Issue SET commands as needed.  If you want to transfer binary data rather  than
  text  data, change the DATA setting (e.g., SET DATA BINARY).  If you want files
  that are transferred to TSO to not be stored  on  the  TMP  volumes,  you  must
-
 How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  25
-
  change  the  VOLUME setting (e.g., SET VOLUME FILE21), as in this example.  All
  parameter values that you want to change must be set before the  remote  Kermit
  is  placed  in  server  mode.   These parameters and their values are described
  under the SET command in the TSO Kermit section.]
0KERMIT-TSO> set vol    file21 Tell TSO Kermit where to put data sets.
+            _______ume
+                   __________
 KERMIT-TSO> server            Tell TSO Kermit to be a server.
+            ______
  Now entering SERVER mode - type FINISH or LOGOUT on micro to halt SERVER
 X]c                           Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>get ________        Get the TSO file named TEST.PLI.
+          ____test.pli
0[PC screen shows file transfer status during download of the TSO data set to the
  IBM PC.]
0Kermit-MS>send test.for       Send the IBM PC file named TEST.FOR.
+          _____________
0[PC screen shows file transfer status during upload of the IBM PC file to TSO.]
0Kermit-MS>bye                 Shut down TSO Kermit & session, PC Kermit.
+          ___
 A>                            Back at PC-DOS automatically.
0[Here you can do some work on the microcomputer, edit files, etc.]
-
-
-
-
-
-
-
-
-
-
                                                   Section 2 -- How to Use Kermit
126                                                  Kermit File Transfer Package
-
 2.3.2.2.  Transfer Files Between TSO and IBM PC Using Send/Receive
0User responses are underlined  notes are enclosed in brackets or are  listed  to
+                   __________,
 the far right of the relevant input/output.
0A>k_____                      Start Kermit on the IBM PC.
+  _ermit
 IBM-PC Kermit-MS V2.29   26 May 86
 Type ? for help
0Kermit-MS>comment           DO WYLBUR for WYLBUR
 Kermit-MS>comment           DO DEC10  for DEC-10
 Kermit-MS>comment           DO TSO    for TSO
 Kermit-MS>comment           DO 3270   for Protocol Conversion Facility
 Kermit-MS>                    This is the Kermit prompt for the PC.
 Kermit-MS>do ___              Set Kermit parameters for TSO.
+          ___tso
0[Commands issued from TSO macro are displayed]
0Kermit-MS>connect             Connect to the communications line.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0ATDT49_____                   Issue modem command to dial TSO.
+______22223
0[Assumes Hayes-compatible modem; dial 492-2223 using a  manual  dial  modem;  if
  using  an  AT&T  2224B  modem,  type  AT4922223 or use the interactive commands
  described in the NIH Terminal Operators Guide.]
0[Various modem messages]
0CONNECT                       You are now connected to TSO.
 logon                         Start the TSO LOGON process.
+_____
 INITIALS? iii
+          ___
 ACCOUNT? aaaa
+         ____
 KEYWORD? kkk
+         ___
 TERMINAL? none
+          ____
 BOX? bbb
+     ___
 AAAAIII LOGON IN PROGRESS AT 11:26:19 ON JUNE 11, 1986
  NIH/DCRT/CCB TSO
0[TSO messages related to logon]
0READY                         TSO LOGON process complete.
 kermit                        Start TSO Kermit.
+______
 NIH KERMIT-TSO VERSION 1.0
0[Issue SET commands as needed.  If you want to transfer binary data rather  than
  text  data,  change  the  DATA  setting (e.g., SET DATA BINARY).  All parameter
  values that you want to change must be set before the SEND command is issued to
  the  remote  Kermit.  These parameters and their values are described under the
  SET command in the TSO Kermit section.]
-
0How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  27
-
 KERMIT-TSO> send _______      Send the TSO file named DB2.RPT.
+            _____db2.rpt
 X]c                           Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>receive             Tell the PC that a file is coming.
+          _______
0[PC screen shows file transfer status during download of the TSO data set to the
  IBM PC.]
0Kermit-MS>connect             Connect to TSO.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0[Issue SET commands as needed.  If you want to transfer binary data rather  than
  text data, change the DATA setting (e.g., SET DATA BINARY), as in this example.
  If you want files that are transferred to TSO to  not  be  stored  on  the  TMP
  volumes,  you  must  change the VOLUME setting (e.g., SET VOLUME FILE21), as in
  this example.  All parameter values that you want to change must be set  before
  the RECEIVE command is issued to the remote Kermit.  These parameters and their
  values are described under the SET command in the TSO Kermit section.]
0KERMIT-TSO> set data binary   Set parameter for binary file transfer.
+            _______________
 KERMIT-TSO> set vol    file21 Tell TSO Kermit where to put data sets.
+            _______ume
+                   __________
 KERMIT-TSO> receive           Tell TSO Kermit a file is coming.
+            _______
 X]c                           Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>set eof noctrl-z    Set end of file handling for binary file.
+          ________________
 Kermit-MS>send _________      Send the IBM PC file TEST5.DAT.
+          _____test5.dat
0[PC screen shows file transfer status during upload of the IBM PC file to TSO.]
0Kermit-MS>connect             Connect to TSO.
+          _______
0[The screen changes to the display of the terminal being emulated.]
0KERMIT-TSO> quit              Get out of TSO Kermit.
+            ____
0READY
 logoff                        Logoff from TSO.
+______
0[TSO messages related to logoff]
0X]c                           Now escape back to the microcomputer.
+___
0[Back to the microcomputer.]
0Kermit-MS>quit                Shut down the PC Kermit.
+          ____
 A>                            Back at PC-DOS automatically.
-
0                                                  Section 2 -- How to Use Kermit
128                                                  Kermit File Transfer Package
-
 [Here you can do some work on the microcomputer, edit files, etc.]
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
 How to Use Kermit -- Section 2
1Kermit File Transfer Package                                                  29
-
 3.  Kermit Commands
0An "ideal" Kermit program will be described here, which has most of the features
 specified  in  the  Kermit Protocol Manual (available from Columbia University).
 No Kermit program will have all these commands or  support  all  these  options.
 The exact form of some of the commands may differ from version to version.  Some
 Kermit programs may support system-dependent options not  described  here.   The
 intention  of  this  description is to provide a base from which specific Kermit
 programs can be described in terms of their differences from the "ideal."
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0                                                    Section 3 -- Kermit Commands
130                                                  Kermit File Transfer Package
-
 3.1.  Remote and Local Operation
0In any connection between two Kermit programs, one  Kermit  is  remote  and  the
 other  is local.  The remote Kermit is usually running on a mainframe, which you
 have CONNECTed to through a PC or other computer.  When  Kermit  runs  remotely,
 all  file  transfer is done over the job's controlling terminal line -- the same
 line over which you logged in, and to which you would type interactive commands.
 What  the  system  thinks is your terminal is really another computer, usually a
 microcomputer, running its own copy of Kermit.
0When Kermit is in "local mode," file transfer is done over an  external  device,
 such  as  a  microcomputer's  serial communication port, or an assigned terminal
 line on a mainframe.  The local Kermit is connected  in  some  way  (such  as  a
 dialout mechanism) to another computer, again running its own copy of Kermit.  A
 local Kermit is in control of the screen, a remote Kermit has no  direct  access
 to it.  Microcomputer Kermits are run in local mode unless instructed otherwise;
 mainframe Kermits run remotely unless some special command places them in  local
 mode.   Some commands make sense only for remote Kermits, others only for local,
 still others can be used with either.  Local and remote operation of  Kermit  is
 shown  schematically  here:  The Kermit program on the PC is a local Kermit.  It
 can control the screen, the keyboard, and the  communications  port  separately,
 thus  it  can  update  the  screen  with status information, watch for interrupt
 signals from the keyboard, and transfer packets on the communications port,  all
 at   the  same  time.   See  Figure  3.1  on  the  next  page  for  a  schematic
 representation of these relationships.
0The Kermit program running on the mainframe is a remote Kermit.  The  user  logs
 in to the mainframe through a terminal port.  The host computer cannot tell that
 the user is really coming in through a microcomputer.  The keyboard, screen, and
 port  functions  are  all  combined  in  the  user's  mainframe  terminal  line.
 Therefore a remote Kermit is cut off from your screen and keyboard  during  file
 transfer.
-
-
-
-
-
-
-
-Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  31
-
 PC is Local, Mainframe is Remote:
0             Communication
              Line                    (Packets)
              +---------------/  /-----------------+  Other terminals
              |                                    |  |  |  |
              |                                    |  |  |  |
    PC        |     LOCAL              Mainframe   |  |  |  |  REMOTE
   +----------+----------+            +------------+--+--+--+--------+
   |   Serial Port       |            |            |                 |
   |                     |            |            |                 |
   |                     |            |            |                 |
   |  +---------------+  |            |            Your session's    |
   |  | Packets: 724  |  |            |            terminal line     |
   |  | Retries:   7  |  |            |                              |
   |  | File: FOO.BAR |  |            |                              |
   |  +---------------+  |            |                              |
   |   Screen            |            |                              |
   |                     |            |                              |
   +---------------+-----+            +------------------------------+
                   |
                   | (Commands)
                   |
      +------------+---------+
       \       Keyboard       \
        +----------------------+
                   You
0                     Figure 3-1:   Local and Remote Kermits
-
-
-
-
-
-
-
-
-                                                    Section 3 -- Kermit Commands
132                                                  Kermit File Transfer Package
-
 3.2.  The Command Dialog
0Most Kermit programs communicate  with  you  through  interactive  keyword-style
 command  dialog.  The program issues a prompt, indicating that it is waiting for
 you to type a command.  The prompt is usually of the form
0                                   Kermit-xx>
0where xx indicates the version  of  Kermit  --  Kermit-MS>  for  MS-DOS  Kermit,
 KERMIT-A2> for APPLE DOS Kermit, etc.
0In response to the program's prompt you  may  type  a  keyword,  such  as  SEND,
 RECEIVE,  or EXIT, possibly followed by additional keywords or operands, each of
 which is called a field.  You can abbreviate keywords (but not  file  names)  to
 any length that makes them distinguishable from any other keyword valid for that
 field.  You can type a question mark at any time to get information about what's
 expected or valid at that point.  You can push the ESC (escape) key at any point
 in a command keyword, and Kermit will complete the  partially  entered  keyword.
 The  ESC  and  "?"   features  work best on full duplex systems (all but the IBM
 mainframe, so far), where the program can "wake up" immediately and perform  the
 required  function.   On half duplex or record-oriented systems, the ESC feature
 is not available, and the "?"  requires a carriage return to follow.
0In the following example, the user types "set" and then a question mark to  find
 out  what the SET options are.  The user then continues the command at the point
 where the question mark was typed, adding a "d" and another question mark to see
 what  set  options  start  with  "d."   The  user  then  adds  a  "eb" to select
 "debugging" (the only SET option that starts with  "deb")  followed  by  an  ESC
 (shown  here  by  a  dollar  sign)  to  complete the current field, then another
 question mark to see what the possibilities are  for  the  next  field,  and  so
 forth.  The command is finally terminated by a carriage return.  Before carriage
 return is typed, however, the command can be edited or erased by backspacing and
 re-keying  the  command.   Finally,  the  same  command  is entered again with a
 minimum of keystrokes, with  each  field  abbreviated  to  its  shortest  unique
 length.
0In the example, the parts the user types are underlined; all the rest is  system
 typeout:
-
-
-
-
-
-Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  33
-
   Kermit-10>set ? keyword (no defined keywords match this input)
+            _____
     or one of the following:
    block-check-type       debugging        delay
    escape                 file             handshake
    incomplete-file        line             local-echo
    message                parity           prompt
    receive                repeat           retry
    send                   server-timer     XON-XOFF-processing
   Kermit-10>set d? one of the following:
+            ______
    debugging   delay
   Kermit-10>set deb$       ?  one of the following:
+            ________ugging _
    log-file     no-log-file  off          on
    full   half
   Kermit-10>set deb of
+            __________
-
-
-
-
-
-
-
-
-
-
-
-
-
-                                                    Section 3 -- Kermit Commands
134                                                  Kermit File Transfer Package
-
 3.3.  Notation
0In the command descriptions, the following notation is used:
0anything    A parameter - A field not enclosed in brackets or braces is replaced
             by an argument of the specified type (number, filename, etc.).
0[anything]  A field enclosed in square brackets is optional.   If  omitted,  the
             field  defaults  to  an  appropriate  value.   You  don't  type  the
             brackets.
0$x,y,z     A list of alternatives is enclosed in curly braces; you type one  of
             the alternatives.
0number      A whole number, entered in the prevailing notation of the system.
0character   A single character, entered literally, or as a number (perhaps octal
             or hexadecimal) representing the ASCII value of the character.
0floating-point-number
0            A  "real"  number,  possibly  containing  a  decimal  point  and   a
             fractional part.
0filespec    A file specification, i.e., the name of a file, possibly including a
             search   path,   device  or  directory  name,  or  other  qualifying
             information, and possibly containing "wildcard" or  pattern-matching
             characters to denote a group of files.
0XX          A control character  may  be  written  using  "uparrow"  or  "caret"
             notation,  since  many  systems display control characters this way.
             Control characters are produced by holding down the key marked  CTRL
             or Control and typing the appropriate character, e.g. X.
-Commands are shown in upper case, but can be entered in any combination of upper
 and lower case.
-
-
-
-
-
-
 Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  35
-
 3.4.  Summary of Kermit Commands
0Here is a brief list of Kermit commands as they are to be found in  most  Kermit
 programs.  The following sections will describe these commands in detail.
-For exchanging files:
0    SEND, RECEIVE, GET
-For connecting to a remote host:
0    CONNECT, SET LINE, SET PARITY, SET DUPLEX,
     SET HANDSHAKE, SET ESCAPE,
     SET FLOW-CONTROL, SET SPEED (or BAUD)
-For acting as a server:
0    SERVER
-For talking to a server:
0    BYE OR LOGOUT, FINISH, GET, SEND, REMOTE
-Setting non-standard transmission and file parameters:
0    SET BLOCK-CHECK, SET DEBUG, SET DELAY, SET FILE,
     SET INCOMPLETE, SET PARITY, SET RETRY, SET SEND (or
     RECEIVE), END-OF-LINE, START-OF-PACKET,
     PACKET-LENGTH, PAUSE, TIMEOUT, PADDING
-For defining "macros" of commands:
0    DEFINE
-For interrupting transmission:
0    Control-X, Control-Z, Control-C, Control-E
-Getting information:
0    HELP, STATISTICS, SHOW
-
-
                                                     Section 3 -- Kermit Commands
136                                                  Kermit File Transfer Package
-
 Executing command files:
0    TAKE
-For recording the history of a file transfer operation:
0    LOG TRANSACTIONS
-For non-protocol file capture or transmission:
0    LOG SESSION, TRANSMIT, INPUT, OUTPUT, PAUSE, CLEAR, SCRIPT
-For closing log files:
0    CLOSE
-Leaving the program:
0    EXIT, QUIT
-If you have a file called KERMIT.INI in your default or home disk,  Kermit  will
 execute  an  automatic  TAKE command on it upon initial startup.  KERMIT.INI may
 contain any Kermit commands, for instance SET commands, or DEFINEs for macros to
 configure  Kermit  to  various  systems  or  communications  media.  Note:  Your
 particular implementation of Kermit may use a different name for this file.  The
 NIH Computer Center supplies a suitable file on the Kermit distribution diskette
 for the IBM PC.
-
-
-
-
-
-
-
-Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  37
-
 3.5.  The SEND Command
0Syntax:
0Sending a single file:
0    SEND nonwild-filespec1 [filespec2]
-Sending multiple files:
0    SEND wild-filespec1 [filespec2]
-The SEND command causes a file or file group to be sent  to  the  other  system.
 There  are  two  forms  of  the command, depending on whether filespec1 contains
 "wildcard" characters.  Use of wildcard characters is the most common method  of
 indicating  a  group  of  files in a single file specification.  For instance if
 FOO.FOR is a single file, a FORTRAN program named FOO, then  *.FOR  might  be  a
 group of FORTRAN programs.
-    Sending a File Group --
0If filespec1 contains wildcard characters then all matching files will be  sent,
 in  directory-listing order.  If a file can't be opened for READ access, it will
 be skipped.  Some Kermit programs allow the initial file in a wildcard group  to
 be  specified with the optional filespec2.  This allows a previously interrupted
 wildcard transfer to continue from where it left off, or it can be used to  skip
 some files that would be transmitted first.
-    Sending a Single File --
0If filespec1 does not contain any wildcard  characters,  then  the  single  file
 specified  by  filespec1  will  be  sent.   Optionally, filespec2 may be used to
 specify the name under  which  the  file  will  arrive  at  the  target  system;
 filespec2  is  not  parsed or validated locally in any way.  If filespec2 is not
 specified, the file will be sent with its own name.
-    SEND Command General Operation --
0Files will be sent with their filename and filetype (for  instance  FOO.BAR,  no
 device   or   directory   field,   no  generation  number  or  attributes).   If
 communication line parity is being used (see SET  PARITY),  the  sending  Kermit
 will  request that the other Kermit accept a special kind of prefix notation for
 binary files.  This is an advanced feature, and not all Kermits have it; if  the
 other  Kermit  does  not  agree to use this feature, binary files cannot be sent
 correctly.
-
-                                                    Section 3 -- Kermit Commands
138                                                  Kermit File Transfer Package
-
 The sending Kermit will also ask the  other  Kermit  whether  it  can  handle  a
 special  prefix  encoding  for  repeated characters.  If it can, then files with
 long strings of  repeated  characters  will  be  transmitted  very  efficiently.
 Columnar   data,   highly   indented  text,  and  binary  files  are  the  major
 beneficiaries of this technique.
-    SEND Remote Operation --
0If you are running Kermit remotely (for instance,  from  a  microcomputer),  you
 should "escape back" to your local Kermit within a reasonable amount of time and
 give the RECEIVE command.  Don't take more than a minute or two to complete  the
 switch,  or  Kermit  may  "time out" and give up.  (In that case, you'll have to
 CONNECT back to the remote system and reissue the SEND command.)
-    SEND Local Operation --
0If you're running Kermit locally, for instance on a  microcomputer,  you  should
 have  already  run  Kermit on the remote system and issued either a RECEIVE or a
 SERVER command.
0Once you give Kermit the SEND command, the name of each file will be printed  on
 your  screen  as  the  transfer  begins,  and  information  will be displayed to
 indicate the packet traffic.  When the  specified  operation  is  complete,  the
 program  will sound a beep, and the status of the operation will be indicated by
 a message like OK, Complete, Interrupted, or Failed.
0If you see many packet retry indications, you  are  probably  suffering  from  a
 noisy  connection.   You may be able to cut down on the retransmissions by using
 SET SEND PACKET-LENGTH to decrease the  packet  length;  this  will  reduce  the
 probability  that a given packet will be corrupted by noise, and reduce the time
 required to retransmit a corrupted packet.
0If you notice a file being sent which you do not really want to  send,  you  may
 cancel  the  operation  immediately by typing either Control-X or Control-Z.  If
 you are sending a file group, Control-X  will  cause  the  current  file  to  be
 skipped,  and  Kermit will go on to the next file, whereas Control-Z will cancel
 sending the entire group and return you to Kermit command level.
-
-
-
-
-
0Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  39
-
 3.6.  The RECEIVE Command
0Syntax:  RECEIVE [filespec]
0The RECEIVE command tells Kermit to wait for the arrival of a file or file group
 sent  by  a  SEND  command  from  the  other  system.  If only one file is being
 received, you may include the  optional  filespec  as  the  name  to  store  the
 incoming file under; otherwise, the name is taken from the incoming file header.
 If the name in the header is not a legal file name on the local  system,  Kermit
 will attempt to transform it to a legal name.
0If an incoming file has the same name as an existing file,  Kermit  will  either
 overwrite the old file or else try to create a new unique name, depending on the
 setting of FILE WARNING.
0If you have SET PARITY, then 8th-bit prefixing will be requested.  If the  other
 side  cannot do this, binary files cannot be transferred correctly.  The sending
 Kermit may also request that repeated characters be compressed.
0If an incoming file does not  arrive  in  its  entirety,  Kermit  will  normally
 discard  it; it will not appear in your directory.  You may change this behavior
 by using the command SET INCOMPLETE KEEP, which will cause as much of  the  file
 as arrived to be saved in your directory.
-    RECEIVE Remote Operation --
0If you are running Kermit remotely, you should escape back to your local  Kermit
 and  give the SEND command.  You should do this within about two minutes, or the
 protocol may time out and give up; if this happens, you can CONNECT back to  the
 remote system and reissue the RECEIVE command.
-    RECEIVE Local Operation --
0If you are running Kermit locally, you should already have issued a SEND command
 to  the  remote  Kermit, and then escaped back to the host Kermit.  (You can not
 issue a RECEIVE command to a Kermit server, you must use  the  GET  command  for
 that.)
0As files arrive, their names  will  be  shown  on  your  screen,  along  with  a
 continuous display of the packet traffic.
0If a file begins to arrive that you don't really want, you can attempt to cancel
 it  by typing Control-X; this sends a cancellation request to the remote Kermit.
 If the remote Kermit understands this request (not all implementations of Kermit
 support this feature), it will comply; otherwise it will continue to send.  If a
 file group is being sent, you can request  the  entire  group  be  cancelled  by
 typing Control-Z.
-
-
                                                     Section 3 -- Kermit Commands
140                                                  Kermit File Transfer Package
-
 3.7.  GET
0LOCAL ONLY -- Syntax: GET [remote-filespec]
0The GET command requests a remote Kermit server to send the file or  file  group
 specified  by remote-filespec.  Note the distinction between the RECEIVE and GET
 commands:  RECEIVE  instructs  the  program  to  wait  passively;  whereas,  GET
 actively sends a request to a server.
0The GET command can be used only when Kermit is local, with a Kermit  server  on
 the other end of the line.  This means that you must have CONNECTed to the other
 system, logged in, run Kermit there, issued the SERVER command, and escaped back
 to the local Kermit.
0The remote filespec is any string that can be a legal file specification for the
 remote  system;  it  is not parsed or validated locally.  As files arrive, their
 names will be displayed on your screen, along with a  continuous  indication  of
 the  packet  traffic.   As  in  the  RECEIVE  command, you may type Control-X to
 request that the current incoming file be cancelled,  or  Control-Z  to  request
 that the entire incoming batch be cancelled.
0Optional Syntax:  If you are requesting a single file,  you  may  type  the  GET
 command  without  a  filespec.  In that case, Kermit programs that implement the
 optional GET syntax will prompt you for the remote filespec  on  the  subsequent
 line, and the name to store it under when it arrives on the line after that:
-  Kermit-MS>get
+            ___
    Remote Source File: aux.txt
+                       _______
    Local Destination File: auxfile.txt
+                           ___________
-
-
-
-
-
-
-
-
0Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  41
-
 3.8.  SERVER
0Syntax:  SERVER
0The SERVER command instructs Kermit to cease taking commands from  the  keyboard
 and  to  receive  all  further  instructions  in the form of Kermit packets from
 another system.  The other Kermit must  have  commands  for  communicating  with
 remote servers; these include GET, SEND, FINISH, and BYE or LOGOUT.
0After issuing this command, return to the "client" system and issue  SEND,  GET,
 BYE,  LOGOUT,  FINISH,  or  other  server-directed commands from there.  If your
 local Kermit does not have a BYE command, then it does not have the full ability
 to  communicate  with  a  Kermit server and you should not put the remote Kermit
 into SERVER mode.  If your local Kermit does have a BYE command, use it to  shut
 down and log out the Kermit server when you are done with it.
0Any non-standard parameters should be selected with SET commands before  putting
 Kermit in server mode.
-3.9.  BYE
0LOCAL ONLY -- Syntax:  BYE
0When running as a local Kermit talking to a Kermit server, use the  BYE  command
 to  shut  down  and  log out the server.  This will also close any debugging log
 files and exit from the local Kermit.
-3.10.  FINISH
0LOCAL ONLY -- Syntax:  FINISH
0When running as a local Kermit talking to a remote Kermit server use the  FINISH
 command  to shut down the server without logging out the remote job, so that you
 can CONNECT back to it.  Also, close any local debugging log file.
-
-
-
-
-
-
0                                                    Section 3 -- Kermit Commands
142                                                  Kermit File Transfer Package
-
 3.11.  REMOTE
0LOCAL ONLY -- Syntax:  REMOTE command
0When running as a local Kermit talking to a remote Kermit server, use the REMOTE
 command  to  request special functions of the remote server.  If the server does
 not understand the command or offer the requested service (all of these commands
 and services are optional features of the Kermit protocol), it will reply with a
 message like "Unknown Kermit Server Command."  If does understand, it will  send
 the results back, and they will be displayed on the screen.  The REMOTE commands
 are:
-REMOTE CWD [directory]
0     Change Working Directory.  If no directory name  is  provided,  the  server
      will  change to the default directory.  Otherwise, you will be prompted for
      a password, and  the  server  will  attempt  to  change  to  the  specified
      directory.   If access is not granted, the server will provide a message to
      that effect.
-REMOTE DELETE filespec
0     Delete the specified file or files.   The  names  of  the  files  that  are
      deleted should be displayed on your screen.
-REMOTE DIRECTORY [filespec]
0     The names of the files that match the  given  file  specification  will  be
      displayed  on your screen, possibly along with additional information about
      file sizes and dates.  If no file specification is given,  all  files  from
      the current directory will be listed.
-REMOTE SPACE [directory]
0     Information about disk usage in the  current  remote  directory  --  quota,
      current  storage, or amount of remaining free space -- is displayed on your
      screen.
-REMOTE HELP
0     A list of available server functions is displayed.
-REMOTE HOST [command]
0     The given command is passed to the server's host command processor, and the
      resulting output is displayed on your screen.
-
 Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  43
-
 REMOTE Kermit [command]
0     The  given  command,  which  is  expressed  in  the  server  Kermit's   own
      interactive-mode  command  syntax,  is  passed to the server for execution.
      This is useful for changing settings, logging, and other functions.
-REMOTE RUN program-name [command-line-argument]
0     The remote Kermit is asked to run the indicated program with the  indicated
      command line; the program's terminal output is sent back to your screen.
-REMOTE PROGRAM [command]
0     The command is sent to the  program  started  by  most  recent  REMOTE  RUN
      program,  and  the  program's  response  is displayed on the screen.  If no
      command is given, a newline character is sent.
-REMOTE TYPE filespec
0     The contents of the specified file is displayed on your screen.
-
-
-
-
-
-
-
-
-
-
-                                                    Section 3 -- Kermit Commands
144                                                  Kermit File Transfer Package
-
 3.12.  LOCAL
0Syntax: LOCAL command
0Execute the specified command on the local system -- on the system where  Kermit
 to  which  your are typing this command is running.  These commands provide some
 local file management capability without having to  leave  the  Kermit  program,
 which  is  particularly  useful  on  microcomputers.  The LOCAL prefix for these
 commands can be omitted.
-CWD [directory]
0     "Change Working Directory" to the specified directory.
-DELETE filespec
0     Delete the specified file or files.
-DIRECTORY [filespec]
0     Provide a directory listing of the specified files.
-SPACE
0     Display local disk usage and/or free space.
-RUN filespec [operands]
0     Run the indicated program with the supplied command-line operands.
-PUSH
0     Invoke the local system command interpreter in  such  a  way  that  it  can
      return (or "pop" or "exit") back to Kermit.
-Some Kermit programs may provide commands for these or other  functions  in  the
 syntax  of  their own system, when this would cause no confusion.  For instance,
 CP/M Kermit may use ERA in place of LOCAL DELETE.
-
-
-
0Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  45
-
 3.13.  CONNECT
0LOCAL ONLY -- Syntax: CONNECT [terminal-designator]
0Establish a  terminal  connection  to  the  system  at  the  other  end  of  the
 communication line.  On a microcomputer, this is normally the serial port.  On a
 mainframe, you will have to specify a terminal line number or other  identifier,
 either in the CONNECT command itself, or in a SET LINE command.  Get back to the
 local Kermit by typing the escape  character  followed  by  a  single  character
 "command."  Several single-character commands are possible:
0  C   Close the connection and return to the local Kermit.
   S   Show status of the connection.
   B   Send a BREAK signal.
   0   (zero) Send a NUL (0) character.
   D   Drop the line, hangup the modem.
   P   Push  to  the  local  system  command  processor  without   breaking   the
       connection.
   Q   Quit logging session transcript.
   R   Resume logging session transcript.
   ?   List all the possible single-character arguments.
   X]  (or whatever you have set the escape character to be)  Typing  the  escape
       character twice sends one copy of it to the connected host.
0You can use the SET ESCAPE command to define a different escape  character,  and
 SET  PARITY,  SET DUPLEX, SET FLOW-CONTROL, SET HANDSHAKE to establish or change
 those parameters.
-3.14.  HELP
0Syntax: HELP
0Typing HELP alone prints a  brief  summary  of  Kermit  and  its  commands,  and
 possibly  instructions  for  obtaining  more detailed help on particular topics.
 Most Kermit implementations also allow the use  of  "?"   within  a  command  to
 produce a short help message.
-3.15.  TAKE
0Syntax: TAKE filespec
0Execute Kermit commands from the specified file.  The file may  contain  contain
 any valid Kermit commands, including other TAKE commands.
-3.16.  EXIT, QUIT
0Syntax:  EXIT or QUIT
0Exit from Kermit.  QUIT is a synonym for EXIT.
-
                                                     Section 3 -- Kermit Commands
146                                                  Kermit File Transfer Package
-
 3.17.  The SET Command
0Syntax: SET parameter [option] [value]
0Establish or modify various parameters for file transfer or terminal connection.
0When a file transfer operation begins, the two  Kermits  automatically  exchange
 special  initialization  messages, in which each program provides the other with
 certain information about itself.  This information includes the maximum  packet
 size it wants to receive, the timeout interval it wants the other Kermit to use,
 the number and type of padding characters it needs, the end-of-line character it
 needs  to  terminate  each  packet  (if  any), the block check type, the desired
 prefixes for control  characters,  characters  with  the  "high  bit"  set,  and
 repeated  characters.   Each  Kermit program has its own preset "default" values
 for these parameters, and you normally need not concern yourself with them.  You
 can  examine  their values with the SHOW command; the SET command is provided to
 allow you to change them in order to adapt to unusual conditions.
0The following parameters may be SET:
0     BAUD-RATE     Set the speed of the current communications port
      BLOCK-CHECK   Packet transmission error detection method
      DEBUGGING     Mode or log file
      DELAY         How long to wait before starting to send
      DUPLEX        For terminal connection, full (remote echo)  or  half  (local
                    echo)
      ESCAPE        Character for terminal connection
      FILE          For setting file parameters like  name  conversion  and  byte
                    size
      FLOW-CONTROL  Selecting flow control method, like XON/XOFF
      HANDSHAKE     For turning around half duplex communication line
      IBM           Set things up for communicating with an  IBM  mainframe  (not
                    used with TSO at NIH)
      INCOMPLETE    What to do with an incomplete file
      LINE          Terminal line to use for terminal connection or file transfer
      MODEM         Modem type or characteristics
      PARITY        Character parity to use
      PORT          For switching communication ports
      PROMPT        For changing the program's command prompt
      RECEIVE       Various parameters for receiving files
      RETRY         How many times to retry a packet before giving up
      SEND          Various parameters for sending files
      TIMER         Enable/disable timeouts
0The DEFINE command may be used to compose "macros" by  combining  SET  commands.
 The SET commands are now described in detail.
-
-
-
 Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  47
-
 SET BAUD-RATE
0Syntax:  SET BAUD-RATE number
0Set or change the baud rate (approximate  translation:   transmission  speed  in
 bits  per second) on the currently selected communications device.  Ten bits per
 second is equivalent to one character per second; 300 baud = 30 cps.  The way of
 specifying the baud rate varies from system to system; in most cases, the actual
 number (such as 1200 or 9600) is  typed.   Systems  that  do  not  provide  this
 command  generally  expect  that  the  speed  of  the  line has already been set
 appropriately outside of Kermit.  Common values are 300, 1200, 2400,  4800,  and
 9600.
-SET BLOCK-CHECK
0Syntax:  SET BLOCK-CHECK $1, 2, 3
0Kermit normally uses a 1-character block check, or "CHECKSUM," on  each  packet.
 The  sender of the packet computes the block check based on the other characters
 in the packet, and the receiver recomputes it the same way.  If these quantities
 agree,  the packet is accepted and transmission proceeds.  If they disagree, the
 packet is rejected and retransmission is requested.
0However, the block check is not a foolproof  method  of  error  detection.   The
 normal  single-character  Kermit  block  check is only a 6-bit quantity (the low
 order 8 bits of the arithmetic sum folded upon itself).  With only six  bits  of
 accuracy,  the  chances  are  one  in 2**6 -- that is, 1/64 -- that an error can
 occur which will not be detected in the CHECKSUM, assuming that all  errors  are
 equally likely.
0You can decrease the probability that an error can slip through, at the  expense
 of  transmission efficiency, by using the SET BLOCK-CHECK command to select more
 rigorous block check methods.  Note that  all  three  methods  will  detect  any
 single-bit error, or any error in an odd number of bits.  The options are:
01-CHARACTER-CHECKSUM:
      The normal single-character 6-bit CHECKSUM.
02-CHARACTER-CHECKSUM:
      A 2-character, 12-bit CHECKSUM.  Reduces the probability of an error  going
      undetected to 1/4096, but adds an extra character to each packet.
03-CHARACTER-CRC:
      A 3-character, 16-bit Cyclic Redundancy Check, CCITT format.   In  addition
      to errors in any odd number of bits, this method detects double bit errors,
      all error bursts of length 16 or less, and more than 99.99% of all possible
      longer bursts.  Adds two extra characters to each packet.
0The single character CHECKSUM has proven to be quite adequate in practice,  much
 more  effective  than  straightforward analysis would indicate, since all errors
 are not equally likely, and a simple CHECKSUM is well  suited  to  catching  the
-
                                                     Section 3 -- Kermit Commands
148                                                  Kermit File Transfer Package
-
 kinds  of errors that are typical of telecommunication lines.  The other methods
 should be requested only when the connection is very noisy and/or  when  sending
 binary files.
0Note that the 2- and 3-character block checks are not available in all  versions
 of Kermit; if the other Kermit is not capable of performing the higher-precision
 block checks, the transfer will automatically use the standard  single-character
 method.
0The NIH Computer Center recommends BLOCK-CHECK 3 always.  The overhead is only 2
 percent, and the extra assurance of reliability is worth it.
-SET DEBUG
0Syntax:  SET DEBUG $ON, OFF
0Record debugging information, either on your terminal or  in  a  file.   Options
 are:
0  ON  Turn on debugging.
0  OFF Don't display debugging information (the default).  If  debugging  was  in
       effect, turn it off and close any log file.
0Some Kermit programs may control debugging by use of the LOG DEBUG command.
-SET DELAY
0Syntax:  SET DELAY number
0Specify how many seconds to wait before sending the first packet  after  a  SEND
 command.   Use  when  remote  and SENDing files back to your local Kermit.  This
 gives you time to "escape" back and issue a RECEIVE command.  The  normal  delay
 is  5  seconds.   In  local  mode  or  server mode, Kermit does not delay before
 sending the first packet.
-SET DUPLEX
0Syntax:  SET DUPLEX $FULL, HALF
0For use when CONNECTed to a remote system.  The keyword  choices  are  FULL  and
 HALF.   FULL  means the remote system echoes the characters you type, HALF means
 the local system echoes them.  FULL is the default, and is used by  most  hosts.
 HALF  is  necessary  when  connecting  to  IBM  mainframes.  Half duplex is more
 correctly called "local echo."
-
-
0Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  49
-
 SET ESCAPE
0Syntax:  SET ESCAPE character
0Specify or change the  character  you  want  to  use  to  "escape"  from  remote
 connections back to Kermit.  This would normally be a character you don't expect
 to be using on the remote system, perhaps a control character like X\,  X],  XX,
 or X_.  Most versions of Kermit use one of these by default.  After you type the
 escape character, you must follow it by a single-character "argument,"  such  as
 "C" for Close Connection.  The arguments are listed above, under the description
 of the CONNECT command.
-SET FILE
0Syntax:  SET FILE parameter value
0Establish file-related parameters.  Depending  on  the  characteristics  of  the
 system,  it  may  be necessary to tell Kermit how to fetch an outbound file from
 the disk, or how to store an incoming  file.   The  actual  parameters  you  can
 specify  in this command will vary from system to system, and you should consult
 the documentation for your particular version of Kermit.  Some examples would be
 file  type  (text  or binary), byte size (PDP-10 architecture), record length or
 block  size  (record  oriented  systems),  end-of-file  detection   method   (on
 microcomputers), file naming conversion option.
0This can be a very important command if you intend to transfer binary files, but
 is normally un-necessary for transmitting text files.
-SET FLOW-CONTROL
0Syntax:  SET FLOW-CONTROL $XON/XOFF,NONE
0For communicating with full duplex systems.  System-level flow  control  is  not
 necessary  to  the Kermit protocol, but it can help to use it if the same method
 is available on both systems.  The most common type  of  flow  control  on  full
 duplex  systems  is XON/XOFF.  When a system's input buffer comes close to being
 full, it will send an XOFF character (Control-S) to request the other system  to
 stop  sending.  When it has emptied sufficient characters from its input buffer,
 it signals the other system to resume sending by transmitting an  XON  character
 (Control-Q).   This  process  operates  in  both directions simultaneously.  The
 options for the Kermit SET FLOW command are usually restricted to  XON/XOFF  and
 NONE, which is used to disable this feature.
-
-
-
-                                                    Section 3 -- Kermit Commands
150                                                  Kermit File Transfer Package
-
 SET HANDSHAKE
0Syntax:  SET HANDSHAKE option
0For communicating with half duplex systems.  This  lets  you  specify  the  line
 turnaround  character  sent by the half duplex host to indicate it has ended its
 transmission and is granting you permission to transmit.  When  a  handshake  is
 set,  Kermit  will  not  send  a  packet until the half duplex host has sent the
 specified character (or a timeout has occurred).  The options may include:
-    NONE    No handshake; undo the effect of any previous SET HANDSHAKE.
     XOFF    Control-S.
     XON     Control-Q.
     BELL    Control-G.
     CR      Carriage Return, Control-M.
     LF      Linefeed, Control-J.
     ESC     Escape, Control-[.
0Some Kermit programs may require the  option  to  be  specified  by  typing  the
 character  literally  or  entering  its  numeric  ASCII  value.  If you use this
 command to enable handshaking, you should also SET FLOW NONE.
-SET INCOMPLETE
0Syntax:  SET INCOMPLETE $KEEP, DISCARD
0Specify what to do when a file transfer  fails  before  it  is  completed.   The
 options  are  DISCARD  (the  default)  and  KEEP.  If you choose KEEP, then if a
 transfer fails to complete successfully, you will be able to keep the incomplete
 part that was received.
-SET LINE
0Syntax:  SET LINE [terminal-designator]
0Specify the terminal line to use for file transfer or CONNECT.  This command  is
 found  on mainframe Kermits, which normally run in "remote mode" using their own
 controlling terminal for file transfer.  Specifying a  separate  line  puts  the
 program  in  "local  mode."   If  no  line  is  specified,  revert  to the job's
 controlling terminal, i.e., go back to "remote mode."
-
-
-
-
 Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  51
-
 SET PORT
0Syntax:  SET PORT terminal-designator
0Specify the communications port for file transfer or CONNECT.  This  command  is
 found  on  microcomputer  Kermits  that  run in "local" mode.  SET PORT does not
 change the remote/local status but simply selects a  different  port  for  local
 operation.
-SET PARITY
0Syntax:  SET PARITY $EVEN, ODD, MARK, SPACE, NONE
0Parity is a technique used by communications equipment for detecting errors on a
 per-character basis; the "8th bit" of each character acts as a check bit for the
 other seven bits.  Kermit uses block checks to detect  errors  on  a  per-packet
 basis,  and it does not use character parity.  However, some systems that Kermit
 runs on, or equipment through which these  systems  communicate,  may  be  using
 character  parity.   If Kermit does not know about this, arriving data will have
 been modified and the block check will appear to be wrong, and packets  will  be
 rejected.
0If parity is being used on the communication line, you must inform both Kermits,
 so  the  desired  parity  can be added to outgoing characters, and stripped from
 incoming ones.  SET PARITY should be used  for  communicating  with  hosts  that
 require  character  parity  (IBM  mainframes  are  typical  examples) or through
 devices or networks (like GTE TELENET) that add parity to characters  that  pass
 through  them.   Both  Kermits  should be set to the same parity.  The specified
 parity is used both for terminal connection (CONNECT) and file  transfer  (SEND,
 RECEIVE, GET).
0The choices for SET PARITY are:
0  NONE  (the default) eight data bits and no parity bit.
   MARK  seven data bits with the parity bit set to one.
   SPACE seven data bits with the parity bit set to zero.
   EVEN  seven data bits with the parity bit set to make the overall parity even.
   ODD   seven data bits with the parity bit set to make the overall parity odd.
0NONE means no parity processing is done, and the 8th bit of each  character  can
 be used for data when transmitting binary files.
0If you have set parity to ODD, EVEN, MARK, or SPACE, then advanced  versions  of
 Kermit   will   request   that   binary   files   will   be   transferred  using
 8th-bit-prefixing.   If  the  Kermit  on  the  other  side  knows  how   to   do
 8th-bit-prefixing  (this  is an optional feature of the Kermit protocol, and not
 all implementations of Kermit have it), then binary  files  can  be  transmitted
 successfully.   If  NONE  is specified, 8th-bit-prefixing will not be requested.
 8th-bit-prefixing is slower, but necessary when parity is used.
-
-                                                    Section 3 -- Kermit Commands
152                                                  Kermit File Transfer Package
-
 SET PROMPT
0Syntax:  SET PROMPT string
0This allows you to change the program's prompt.  This is particularly useful  if
 you  are using Kermit to transfer files between two systems of the same kind, in
 which case you can change the prompts of the Kermit programs involved to include
 appropriate distinguishing information.
-SET SEND
0Syntax:  SET SEND parameter value
0Parameters for outgoing packets, as follows:
0END-OF-LINE character
0          The ASCII character to be used  as  a  line  terminator  for  outbound
           packets,  if  one  is required by the other system, carriage return by
           default.  You will only have to use  this  command  for  systems  that
           require a line terminator other than carriage return.
0PACKET-LENGTH number
0          Maximum packet length to send between 10 and 94 (decimal).  Shortening
           the  packets  might  allow more of them to get through through without
           error on noisy communication lines.  Lengthening the packets increases
           the throughput on clean lines.
0TIMEOUT number
0          How many seconds to wait for a packet before trying again.  A value of
           zero means don't time out -- wait forever.
0PAUSE floating-point-number
0          How many seconds to pause before sending each  data  packet.   Setting
           this  to  a  non-zero  value  may  allow  a slow system enough time to
           consolidate itself before  the  next  packet  arrives.   Normally,  no
           per-packet pausing is done.
0PADDING number, PADCHAR character
0          How much padding to send before a packet,  if  the  other  side  needs
           padding,  and  what  character  to  use  for padding.  Defaults are no
           padding, and NUL (0) for the padding character.  This command is  also
           handy  for  inserting  special  characters  that  may  be  required by
           communications equipment.
-
-
 Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  53
-
 QUOTE character
0          What printable character to use for quoting of control characters, "#"
           (ASCII  43  decimal)  by default.  There should be no reason to change
           this.
0START-OF-PACKET character
0          The start-of-packet character  is  the  only  control  character  used
           "bare"  by  the  Kermit protocol.  It is Control-A (ASCII 1 or SOH) by
           default.  If a bare Control-A causes problems for  your  communication
           hardware  or  software, you can use this command to select a different
           control character to mark the start of a packet.  You must also  issue
           the  reciprocal command (SET RECEIVE START-OF-PACKET) to the Kermit on
           the other system (providing it has such a command).
-SET RECEIVE
0Syntax:  SET RECEIVE parameter value
0Parameters to request or expect for incoming packets, as follows:
0END-OF-LINE character
0          Carriage return (ASCII 13 decimal) by default.
0PACKET-LENGTH number
0          Maximum length packet for the other  side  to  send,  decimal  number,
           between 10 and 94.
0TIMEOUT number
0          How many seconds the other Kermit should  wait  for  a  packet  before
           asking for retransmission.
0PAUSE floating-point-number
0          How many seconds to pause before acknowledging a packet.  Setting this
           to  a  non-zero  value  will  slow down the rate at which data packets
           arrive, which may be necessary for systems that have "sensitive" front
           ends and cannot accept input at a high rate.
0PADDING number, PADCHAR character
0          How many padding characters to request before  each  incoming  packet,
           and  what  the  padding  character should be.  No Kermits are known to
           need padding; and if one did, it would request it without your  having
           to tell it to do so.  This command would only be necessary, therefore,
           under very unusual circumstances.
-
0                                                    Section 3 -- Kermit Commands
154                                                  Kermit File Transfer Package
-
 QUOTE character
0          What printable character to use for quoting of control characters, "#"
           (ASCII  43  decimal)  by default.  There should be no reason to change
           this.
0START-OF-PACKET character
0          The control character to  mark  the  beginning  of  incoming  packets.
           Normally  SOH  (Control-A,  ASCII  1)  (see  SET SEND START-OF-PACKET,
           above).
-SET RETRY
0Syntax:  SET RETRY option number
0Set the maximum number of retries allowed for:
0INITIAL-CONNECTION
0          How many times to try establishing  the  initial  protocol  connection
           before giving up, normally something like 15.
0PACKETS
0          How many times to try sending a particular packet  before  giving  up,
           normally  5.  If a line is very noisy, you might want to increase this
           number.
-
-
-
-
-
-
-
-
-Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  55
-
 3.18.  DEFINE
0Syntax:  DEFINE macroname [set-parameters]
0Define a "SET macro"  to  allow  convenient  association  of  one  or  more  SET
 parameters  with  a  mnemonic  keyword of your choice.  The SET parameters are a
 list of one or more SET options, separated by commas.   If  you  use  Kermit  to
 communicate  with several different kinds of systems, you may set up a macro for
 each, for instance:
0 DEFINE IBM PARITY MARK, DUPLEX HALF, HANDSHAKE XON
  DEFINE UNIX PARITY NONE, DUPLEX FULL, HANDSHAKE NONE
  DEFINE TELENET PARITY MARK, RECEIVE TIMEOUT 20
0You may then type SET IBM, SET UNIX,  and  so  forth  to  set  all  the  desired
 parameters with a single command.  It is convenient to include these definitions
 in your KERMIT.INI file.
0Another other handy use  for  SET  macros  would  be  for  rapid  adaptation  to
 different conditions of line noise:
0 DEFINE CLEAN BLOCK-CHECK 1, SEND PACKET-LENGTH 94, RETRY PACKET 5
  DEFINE NOISY BLOCK-CHECK 2, SEND PACKET-LENGTH 60, RETRY PACKET 10
  DEFINE VERY-NOISY BLOCK 3, SEND PACKET 40, RETRY PACKET 20
0You may redefine an existing macro in the same manner as you  defined  it.   You
 can  undefine  an  existing  macro by typing an empty DEFINE command for it, for
 instance:
0 DEFINE IBM
0You can list all your macros and their definitions with the SHOW MACROS command.
 Some  Kermit programs allow macro definitions to include any Kermit command, not
 just SET commands.
-
-
-
-
-
-
-
                                                     Section 3 -- Kermit Commands
156                                                  Kermit File Transfer Package
-
 3.19.  SHOW
0Syntax:  SHOW [option]
0The SHOW command displays the values of  the  parameters  settable  by  the  SET
 command.   If  a  particular option is not requested, a complete display will be
 provided.
-
 3.20.  STATISTICS
0Syntax:  STATISTICS
0Give statistics about the most recent file transfer, such as the total number of
 characters transmitted, the effective speed, and so forth.
-
 3.21.  LOG
0Syntax:  LOG [option] [filespec]
0Log the specified entity to the specified log file.
0TRANSACTIONS    Direct Kermit to log transactions, such  as  files  successfully
                 sent or received or files that could not be successfully sent or
                 received.  A transaction is useful recording the progress  of  a
                 long, unattended multifile transfer.
0SESSION         Create a transcript of a CONNECT session, when running  a  local
                 Kermit connected to a remote system, in the specified file.  The
                 log  is   closed   when   connection   is   closed.    In   some
                 implementations,  logging can be "toggled" by typing the connect
                 escape character followed by  Q  (Quit  logging)  or  R  (Resume
                 logging)  or similar single-character commands.  Session-logging
                 is useful for recording dialog with an interactive  system,  and
                 for  "capturing"  from  systems  that  don't  have  Kermit.   No
                 guarantee can be made that the file  will  arrive  correctly  or
                 completely, since no error checking takes place.
0DEBUGGING       Record debugging information in the specified file.   There  may
                 be  several  options to select the desired information -- entire
                 packets, state  transitions,  internal  program  trace,  etc  --
                 available via the SET DEBUGGING command.
0PACKETS         Record packets, and all communication line traffic  during  file
                 transfer, in the specified file.
-
-
0Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  57
-
 3.22.  TRANSMIT
0Syntax:  TRANSMIT filespec
0Send the contents of the specified file to  the  other  system  "bare,"  without
 protocol,  packets,  error  checking, or retransmission.  This command is useful
 for sending standard logon or connection sequences, and  for  sending  files  to
 systems that don't have Kermit.  No guarantee can be made that the target system
 will receive the file correctly and completely.   When  receiving  a  file,  the
 target system would normally be running a text editor in text collection mode.
-
 3.23.  INPUT
0Syntax:  INPUT [interval] [string]
0Input characters from the remote system for the specified interval, looking  for
 the  specified  string.  Terminate when the string is found or when the interval
 has expired, whichever comes first.  Useful for synchronizing with remote system
 prompts.
-
 3.24.  OUTPUT
0Syntax:  OUTPUT [string]
0Send the specified string to the remote system.  Useful in conjunction with  the
 INPUT command to form "login scripts."
-
 3.25.  PAUSE
0Syntax:  PAUSE [interval]
0Pause for the specified interval.  Useful in login scripts.
-
 3.26.  SCRIPT
0Syntax:  SCRIPT [string]
0The string is a "login  script"  in  some  system-  or  implementation-dependent
 format, such as the UNIX(tm) UUCP "expect-send" format.
-
-
-                                                    Section 3 -- Kermit Commands
158                                                  Kermit File Transfer Package
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0Kermit Commands -- Section 3
1Kermit File Transfer Package                                                  59
-
 4.  Kermit Implementations
0Kermit has been written for a wide  variety  of  systems,  both  mainframes  and
 microcomputers.   Kermit  is  not  written  in a portable language; rather, each
 implementation is written in a language suited for the particular machine.   The
 specification,  given  in  the  Kermit  Protocol Manual (available from Columbia
 University), is quite general and allows implementation on almost any machine.
0Here's a brief table summarizing the known Kermit implementations,  as  of  this
 writing.   This  list  is  constantly growing, and may be far out of date by the
 time you read it.  To obtain information about implementations  of  Kermit  that
 are  not  supported  by  the NIH Computer Center, but which are available on the
 DECsystem-10,  login  to  the  DECsystem-10  and   issue   the   command   "TYPE
 KER:READ.ME".
0Columbia University distributes many versions of Kermit for  different  machines
 through  the BITNET Network.  For information on how to use this facility, enter
 the Information EXCHANGE with the ENTER EXCHANGE command in WYLBUR and  look  at
 Entry  ID  R20,  "BITNET  Network  Resources."   This  entry and any other ENTER
 EXCHANGE entries related to Kermit, may also be retrieved by  specifying  Kermit
 as  a  search word.  Note that only the Kermit versions described in this manual
 are supported by the NIH Computer Center.
-
 Versions for "Portable Operating Systems":  OS; Language (Machines)
0     CP/M-80; ASM (Kaypro, H/Z-89, H/Z-100, Osborne, DEC VT180, many others)
0     CP/M-86; ASM86 (DEC Rainbow, NEC APC, others)
0     MS-DOS; MASM (IBM PC,XT,AT, DEC Rainbow, HP-150, NEC APC, others...)
0     MUMPS (PDP-11)
0     Software Tools; Ratfor (HP3000, Sperry-Univac 1100)
0     UCSD p-System; Pascal (IBM PC, Terak, HP98x6, Pascal Microengine)
0     UNIX v7,4.xBSD,Sys III/V,Venix,Xenix,PC/IX; C (VAX, PDP-11, SUN, many more)
-
-
-
-
-
                                               Section 4 -- Kermit Implementation
160                                                  Kermit File Transfer Package
-
 Host Versions:  Machine (OS; Language)
0     Burroughs B6800 (Algol)
0     Cray-1, Cray-XMP (CTSS; Fortran-77)
0     CDC Cyber 170 (NOS, NOS/BE; Fortran-77)
0     Data General Nova (RDOS; Fortran-5)
0     Data General Eclipse (AOS; Fortran-5), MV Series (AOS/VS; Pascal)
0     DEC PDP-11 (RT11, RSX11M(+), RSTS, P/OS, TSX+; Macro-11)
0     DEC VAX-11 (VMS; Bliss-32 or Macro-32 or Pascal/Fortran)
0     DECsystem-10  (TOPS-10;   Bliss-36,   Macro-10),   DECsystem-20   (TOPS-20;
      Macro-20)
0     Harris 800 (VOS; Pascal)
0     Honeywell (MULTICS; PL/I), DPS-6,8 (GCOS; C)
0     Hewlett-Packard 1000 (RTE-6/VM; Fortran), HP3000 (MPE; SPL or Ratfor)
0     IBM 370 Series (VM/CMS, MVS/TSO, MVS/GUTS, MUSIC, MTS; Assembler)
0     Perkin Elmer 3200 Series (OS/32; Fortran)
0     PRIME (PRIMOS; PL/P)
0     Sperry/Univac-1100 (EXEC; Assembler or Ratfor or Pascal)
0     Tandem (Nonstop; TAL)
-
-
-
-
-
-
-
 Kermit Implementation -- Section 4
1Kermit File Transfer Package                                                  61
-
 PC Versions:  Machine (OS; Language)
0     Alpha Micro 68000 (Assembler)
0     Apollo (Aegis; Fortran or Pascal)
0     Apple ][ 6502 (Apple DOS; DEC-10/20 CROSS or Apple Assembler)
0     Apple Macintosh (SUMACC C)
0     Atari (DOS; Action!)
0     Commodore 64 (DEC-10/20 CROSS or FORTH)
0     DEC Pro-300 Series (P/OS; Bliss-16 or Macro-11), (Pro/RT;  Macro),  (Venix;
      C)
0     Intel Development System (ISIS; PL/M)
0     Perq (Pascal)
0     TRS80 I, III, Model 4 (TRSDOS; ASM)
0     TRS-80 Color Computer (Radio Shack DOS)
-The  remainder  of  this  manual  is   devoted   to   descriptions   of   Kermit
 implementations that are supported by the NIH Computer Center.
-
-
-
-
-
-
-
-
-
                                               Section 4 -- Kermit Implementation
162                                                  Kermit File Transfer Package
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0Kermit Implementation -- Section 4
1Kermit File Transfer Package                                                  63
-
 5.  DECsystem-10 Kermit
0The DECsystem-10 version of Kermit was adapted by Nick Bush,  Bob  McQueen,  and
 Antonio  Mione  at  the  Stevens Institute of Technology in Hoboken, NJ, from an
 earlier DECsystem-20 version.
-Kermit-10 Capabilities At a Glance:
0      Local operation:  Yes
       Remote operation:  Yes
       Transfers text files:  Yes
       Transfers binary files:  Yes
       Wildcard send:  Yes
       XX/XY interruption:  Yes
       Filename collision avoidance:  Yes
       Timeouts:  Yes
       8th-bit prefixing:  Yes
       Repeat character compression:  Yes
       Alternate block check types:  Yes
       Communication settings:  Yes
       Transmit BREAK:  Yes
       IBM mainframe communication:  Yes
       Transaction logging:  Yes
       Session logging:  Yes
       Debug logging:  Yes
       Raw transmit:  Yes
       Login scripts:  Yes
       Act as server:  Yes
       Talk to server:  Yes
       Advanced commands for servers:  Yes
       Local file management:  Yes
       Command/init files:  Yes
       Handle file attributes:  No
-Kermit-10 is a program that implements the Kermit file transfer protocol for the
 Digital Equipment Corporation DECsystem-10 mainframe computer.  It is written in
 MACRO-10 assembly language and should run on any DECsystem-10 with version 4  of
 TOPS-10 or later.
0The Kermit-10 section will  describe  the  things  you  should  know  about  the
 DECsystem-10  file  system in order to make effective use of Kermit, and then it
 will describe the special features of the Kermit-10 program.
-
-
-
-                                                Section 5 -- DECsystem-10 Kermit
164                                                  Kermit File Transfer Package
-
 5.1.  The DECsystem-10 File System
0The features of the DECsystem-10 file system  of  greatest  interest  to  Kermit
 users are the form of the file specifications, and the distinctions between text
 and binary files.
-5.1.1.  TOPS-10 File Specifications
0TOPS-10 file specifications are of the form
0     DEVICE:FILENAME.EXTENSION[DIRECTORY]
0Device may specify any valid generic, physical, logical, ersatz, or dummy device
 name.   FILENAME may have any positive length, but only the first six characters
 will be used.  EXTENSION may be any length, but only the first three  characters
 will  be  used.   When  the  EXTENSION  is null, the dot may usually be omitted.
 DIRECTORY may be any valid UFD or SFD.   The  device,  filename,  and  directory
 fields  may  contain upper case or lower case letters and numeric digits.  There
 are no imbedded or trailing spaces.  The fields of the  file  specification  are
 set off from one another by the punctuation indicated above.
0The filename is the primary identifier  for  the  file.   The  extension  is  an
 indicator  which,  by  convention,  tells what kind of file it is.  For instance
 FOO.FOR is the source of a Fortran program  named  FOO;  FOO.REL  might  be  the
 relocatable  object  module  produced  by  compiling  FOO.FOR;  FOO.EXE could an
 executable program produced by LOADing and SAVing FOO.REL, and so forth.
0FILENAME.EXTENSION is normally sufficient to  specify  a  file,  and  only  this
 information is sent along by Kermit-10 with an outgoing file.
0The directory name indicates the disk area in which the file is  located.   This
 will  default  to  the  user's  current  path  unless  he  specifies a different
 directory name.  A directory name is specified by [P,PN]  immediately  following
 the  extension  where  P  is  a project number and PN is a programmer number.  A
 directory may contain subdirectories.  These are known  as  subfile  directories
 (SFD's).   If the directory [P,PN] has an SFD called ZZZ, the directory field is
 designated [P,PN,ZZZ].
0The device field specifies a physical or "logical" device upon which the file is
 resident.   The  directory  field indicates the area on the device, for instance
 the area belonging to the owner of the file.  Kermit-10 does  not  transmit  the
 device  or  directory fields to the target system, and does not attempt to honor
 device or directory fields that may appear in incoming file names; for instance,
 it will not create new directories.
-
-
-
0DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  65
-
 The DECsystem-10 allows a group of files  to  be  specified  in  a  single  file
 specification  by  including  the special "wildcard" characters, "*" and "?".  A
 "*" matches any string of characters, including no  characters  at  all;  a  "?"
 matches  any  single character.  Because a "?"  will be interpreted as a request
 for help, Kermit-10 uses a "%" as its single character wildcard.  Here are  some
 examples of Kermit-10 wildcards:
0     *.FOR   All files of type FOR (all Fortran source  files)  in  the  current
              directory.
0     FOO.*   Files of all types with name FOO.
0     F*.*    All files whose names start with F.
0     %.*     All files whose names are exactly one character long.
-Wildcard notation is used on many computer systems in similar ways,  and  it  is
 the mechanism most commonly used to instruct Kermit to send a group of files.
-5.1.2.  Text Files and Binary Files
0The  DECsystem-10,  like  most  computers,  has  a  file  system  with  its  own
 peculiarities.   Like  many  other systems, the DECsystem-10 makes a distinction
 between text files and binary files.  Text files are  generally  those  composed
 only  of  printing  characters  (letters, digits, and punctuation) and "carriage
 control" characters (carriage return, line feed, form feed,  tab).   Text  files
 are  designed  to  be read by people.  Binary files are designed to be read by a
 computer program, or the computer itself, and may have any contents at all.   If
 you  use  the DECsystem-10 TYPE command to display a text file on your terminal,
 the result will be intelligible.  If you type a binary file  on  your  terminal,
 you  will  probably  see  mainly gibberish.  You can not tell a text file from a
 binary file just by its name, though in general files with extensions like .TXT,
 .DOC,  .HLP  are  textual (as are "source files" for computer programs like text
 formatters and programming language compilers, e.g., .FOR  .SAI  .PAS  .C),  and
 files with types like .EXE, .REL, .BIN are binary.
0DECsystem-10 Kermit has three  methods  for  transferring  files:   using  7-bit
 bytes, 8-bit bytes, and 36-bit bytes.  By default it will use 7-bit bytes.  This
 will cause all text transfers  to  be  correct  with  the  exception  that  each
 computer sometimes uses special characters in text files.  On personal computers
 some word processors use 8-bit, non-printing characters to indicate underlining,
 etc.   These  files should be considered binary data files.  They may be sent to
 the DECsystem-10 for  transmission  to  a  computer  which  has  the  same  word
 processing software by following the rules for binary files given below.  Such a
 file will be unreadable on the DECsystem-10.  To  make  a  word  processor  file
 readable  on the DECsystem-10, the file must be converted to a "flat" ASCII file
 before  transferring.   Many  word  processors  have  an  option  to  make   the
 conversion.
-
-                                                Section 5 -- DECsystem-10 Kermit
166                                                  Kermit File Transfer Package
-
 The DECsystem-10 commonly inserts NULs into text  files.   The  length  of  each
 DECsystem-10  file  is  saved  as a word count in the RIB (Retrieval Information
 Block).  Because most text files  do  not  contain  an  even  multiple  of  five
 characters, the DECsystem-10 pads text files with NULs to fill in the last word.
 When downloading a file, Kermit-10 transmits the NULs.  When a DECsystem-10 text
 file  has  SOS line numbers, they are aligned on word boundaries.  SOS pads each
 line with NULs to fill in  partial  words  as  needed.   Again,  Kermit-10  will
 download  the  NULs.   On  a  personal  computer  the NULs may or may not make a
 difference.  For example, the DOS TYPE command turns NULs into spaces.  When the
 NULs  are at the end of a file they make no difference.  When they pad lines for
 line numbers, they follow the carriage return/line  feed  that  terminates  each
 line  and  indent  the  following  line.   The  EDLIN line editor makes the NULs
 visible, turning them to X@.
0In general, text files which are just being archived on a personal computer  can
 be  downloaded and uploaded without concern for embedded NULs.  Text files which
 are to be used on the PC should be downloaded with line  numbers  stripped  off.
 If  the trailing NULs interface with the intended use of the text file, they can
 be removed easily with EDLIN or another editor/word processor.
0Deciding what byte size to use when transferring binary data is  complicated  by
 differences  in computer word size.  Most computers other than DECsystem-10s and
 20s and Univacs store data in multiples of 8-bit bytes.  The table  below  shows
 what byte size to use when transferring files to or from the DECsystem-10 and an
 8-bit byte computer.  To use the table, find the row corresponding to the source
 computer  and  the column corresponding to the destination computer.  If you are
 using a computer merely to archive data, use the source computer as both  source
 and  destination in the table.  For example, when saving executable files from a
 PC on the DECsystem-10 for later retrieval, both the source and destination  are
 8-bit  computers  and  the  file  transfers,  both to and from the DECsystem-10,
 should be done with FILE BYTE-SIZE set to 8.
0     FILE BYTE-SIZE FOR BINARY FILE TRANSFER
0        from \ to |  DEC-10  |  8-bit  |
         ----------+----------+---------+
         DEC-10    |    7     |   (1)   |
         ----------+----------+---------+
         8-bit     |   (2)    |    8    |
         ----------+----------+---------+
-
-
-
-
-
 DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  67
-
 NOTES:
0  (1) Either 7 or 8-bit bytes may be used.  In the former case, the  arrangement
   of DECsystem-10 bits in 5 successive bytes will be as shown:
0               DECsystem-10 BITS IN 8-BIT BYTES
0                  +--+--+--+--+--+--+--+--+
           byte 1  | 0| 1| 2| 3| 4| 5| 6|  |
                   +--+--+--+--+--+--+--+--+
           byte 2  | 7| 8| 9|10|11|12|13|  |
                   +--+--+--+--+--+--+--+--+
           byte 3  |14|15|16|17|18|19|20|  |
                   +--+--+--+--+--+--+--+--+
           byte 4  |21|22|23|24|25|26|27|  |
                   +--+--+--+--+--+--+--+--+
           byte 5  |28|29|30|31|32|33|34|35|
                   +--+--+--+--+--+--+--+--+
0  If 8-bit bytes are used the first 32 bits (0-31) will fill 4 successive  bytes
   and the last 4 bits (32-35) will be discarded.
0  (2) Use 8-bit bytes, understanding that 4 successive bytes will be  stored  as
   bits 0-31 in DECsystem-10 words.
0The 36-bit byte option is for DECsystem-10 to DECsystem-10 transfers, so  it  is
 not  relevant at NIH.  There is also a FILE BYTE-SIZE AUTOMATIC option; it often
 makes an incorrect decision between 7-bit as 8-bit byte transfers and should  be
 avoided.
-5.1.3.  Files Kermit-10 Cannot Handle
0The Kermit protocol can only accommodate transfer  of  sequential  files,  files
 which are a linear sequence of bytes (or words).
0Some files on the DECsystem-10 are not sequential, and  cannot  be  successfully
 sent  or received by Kermit-10.  These include directory files, files with holes
 (missing pages), ISAM files,  and  RMS  files.   These  files  require  external
 information  (kept  in the DECsystem-10's RIB and/or index table) in order to be
 reconstructed; when sending files, Kermit-10 presently transmits only  the  file
 name  and  the  contents  of  the  file.   External control information and file
 attributes are not transmitted.
-
-
-
-
                                                 Section 5 -- DECsystem-10 Kermit
168                                                  Kermit File Transfer Package
-
 5.2.  Program Operation
0Note that in the examples  which  follow,  the  text  entered  by  the  user  is
 underlined  in  order  to  distinguish  it  from computer generated messages and
 prompts.
0Kermit-10's prompt is "Kermit-10>".  Kermit-10 will accept a single  command  on
 the Monitor command line, like this:
-  .Kermit send foo.bar
+   ___________________
0      ;the file is sent
-
 or you can run the program interactively to issue several commands, like this:
-  .Kermit
+   ______
0  TOPS-10 Kermit version 3(133)
0  Kermit-10>send foo.*
+            __________
0      ;files are sent
0  Kermit-10>stat
+            ____
0      ;performance statistics are printed
0  Kermit-10>receive
+            _______
0      ;files are received
0  Kermit-10>exit
+            ____
   .
-During interactive operation, you may use the help ("?") and  recognition  (ESC)
 features  freely while typing commands.  A question mark typed at any point in a
 command displays the options available at that point; typing  an  ESC  character
 causes  the  current  keyword to be completed (or default value to be supplied),
 and a "guide word" in parentheses to be typed, prompting you for the next field.
 If  you have not typed sufficient characters to uniquely specify the keyword (or
 if there is no default value) then a beep will be sounded and you  may  continue
 typing.   A  XW  will  delete  the  last word typed, and a XU deletes the entire
 command.
0Command keywords may be abbreviated to the shortest length that sets them  apart
 from any other keyword valid in that field.
-
0DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  69
-
 If you have a file called KERMIT.INI in your  login  directory,  Kermit-10  will
 execute  an  automatic  TAKE command on it upon initial startup.  KERMIT.INI may
 contain any Kermit-10 commands, for instance SET commands, or  DEFINEs  for  SET
 macros  to  configure Kermit-10 to various systems or communications media.  The
 default settings of Kermit-10 will generally be correct for most file transfers.
 If, after reviewing the various SET commands, you find other parameters that you
 would usually set differently, they should be placed in a KERMIT.INI file.
0Kermit-10 provides most of the commands possible for an "ideal" Kermit  program,
 as  described  in  the  main  part  of  the  Kermit  File Transfer Package.  The
 following sections will concentrate on system-dependent aspects of Kermit-10.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-                                                Section 5 -- DECsystem-10 Kermit
170                                                  Kermit File Transfer Package
-
 5.3.  Remote and Local Operation
0Kermit-10 normally runs in remote mode, with the user  sitting  at  a  PC.   But
 Kermit-10 can also run in local mode.  Local operation of Kermit-10 is useful if
 the DECsystem-10 has  an  autodialer,  or  a  hardwired  connection  to  another
 computer.   Because  the  NIH  DECsystem-10  has  no  facility  for dialing out,
 Kermit-10 cannot be used in local  mode  here.   Kermit-10  commands  which  are
 useful only for local mode have had their descriptions modified.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  71
-
 5.4.  Conditioning Your Job for Kermit
0Kermit-10 does as much as it can to condition your line for file  transfer.   It
 saves  all  your  terminal  and  link  settings,  and  restores  them after use.
 However, there are some sources of interference over which Kermit-10 can have no
 control.   In  particular, incoming messages to your terminal may become mingled
 with Kermit packets and slow things  down  or  stop  them  entirely.   For  this
 reason, before using Kermit-10 for any extended period, you may want to :
0     - Type the DECsystem-10 command, SET TERMINAL GAG
0     - Make sure you don't have any  print  or  batch  jobs  pending  that  were
        submitted with the /NOTIFY option.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
                                                 Section 5 -- DECsystem-10 Kermit
172                                                  Kermit File Transfer Package
-
 5.5.  Kermit-10 Commands
0This section describes the Kermit-10 commands -- in  detail  where  they  differ
 from  the  "ideal"  Kermit,  briefly  where  they  coincide.   Kermit-10 has the
 following commands:
0             BYE (This command is for local mode only)
        LOCAL CWD change DECsystem-10 working directory
          CONNECT (This command is for local mode only)
           DEFINE macros of Kermit-10 commands
     LOCAL DELETE delete DECsystem-10 files
        LOCAL DIR list directory of DECsystem-10 files
 LOCAL DISK-USAGE display statistics about DECsystem-10 disk utilization
      LOCAL ERASE delete DECsystem-10 files
             EXIT from Kermit-10
           FINISH (This command is for local mode only)
              GET (This command is for local mode only)
             HELP about Kermit-10
       LOCAL HELP about DECsystem-10 file management commands
            LOCAL prefix for DECsystem-10 file management commands
              LOG (This command is for local mode only)
           LOGOUT (This command is for local mode only)
             QUIT from Kermit-10
          RECEIVE files from another Kermit
           REMOTE (This command is for local mode only)
             SEND files to another Kermit
           SERVER mode of remote operation
              SET various parameters
   LOCAL SET-PATH set path (same as LOCAL CWD)
             SHOW various parameters
      LOCAL SPACE display statistics about DECsystem-10 disk utilization
           STATUS statistics about most recent file transfer
     LOCAL STATUS statistics about most recent file transfer
             TAKE commands from a file
       LOCAL TYPE type a DECsystem-10 file
0Section 3.3 of this manual contains the notation conventions used in the  syntax
 statements that follow.
-
-
-
-
-
-DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  73
-
 5.5.1.  Commands for File Transfer
0Kermit-10 provides the standard SEND, RECEIVE, and GET commands for transferring
 files  using  the  Kermit  protocol.   The  STATUS  command provides Kermit file
 transfer statistics.
-                                The SEND Command
0Syntax:  SEND filespec
-The SEND command causes a file or file group to be sent from the DECsystem-10 to
 the  other  system.   There  are  two forms of the command, depending on whether
 filespec contains wildcard characters  ("*"  or  "%").   If  filespec  does  not
 contain any wildcard characters, then the single file specified by filespec will
 be sent.  If filespec contains wildcard characters then all matching files  will
 be sent, in the order in which they are found in the directory.  If a file can't
 be opened for read access, it will be skipped.
0Files will be sent with their DECsystem-10 filename and extension (for  instance
 FOO.BAR,  no  device  or  directory field, and no protection attribute).  If you
 expect to be sending files whose names contain characters that would be  illegal
 in  filenames  on  the target system, and you know that the Kermit on the target
 system does not have the ability to convert incoming filenames,  you  can  issue
 the  SET  FILE  NAMING  NORMAL-FORM  command  to  have Kermit-10 replace suspect
 characters with X's , and create a new file name and attempt to use that name.
0By default five 7-bit bytes will be sent from each word in the  file,  with  the
 8th  bit  of  the 5th character set to the value of the remaining bit ("bit 35")
 from the word.  For information on sending binary files, refer to Section 5.1.2.
0If communication line parity is being used  (see  SET  PARITY),  Kermit-10  will
 request  that  the  other  Kermit  accept  a special kind of prefix notation for
 binary files ("eight-bit quoting").  This is an advanced feature,  and  not  all
 Kermits  have it; if the other Kermit does not agree to use this feature, binary
 files cannot  be  sent  correctly.   This  includes  executable  programs  (like
 DECsystem-10  .EXE  files,  PC DOS .COM files), relocatable object modules (.REL
 files), as well as text files with line sequence numbers.
0Kermit-10 will also ask the other Kermit whether it can handle a special  prefix
 encoding  for  repeated  characters.  If it can, then files with long strings of
 repeated characters will be transmitted very efficiently.  Columnar data, highly
 indented text, and binary files are the major beneficiaries of this technique.
-
-
-
-                                                Section 5 -- DECsystem-10 Kermit
174                                                  Kermit File Transfer Package
-
                               The RECEIVE Command
0Syntax:  RECEIVE [filespec]
0The RECEIVE command tells Kermit-10 to receive a file or  file  group  from  the
 other  system.  If only one file is being received, you may include the optional
 filespec as the name to store the incoming file under; otherwise,  the  name  is
 taken  from  the incoming file header.  If the name in the header is not a legal
 TOPS-10 file name, Kermit-10 will store it named in  accordance  with  the  FILE
 NAMING option in effect.
0If an incoming file has the same name as  an  existing  file,  Kermit-10  either
 creates  a  new  file name with an extension of three numeric digits or overlays
 the existing file depending on whether or not FILE WARNING has been  SET  ON  or
 OFF.
0Incoming files will all be stored with the prevailing bytesize,  7  by  default,
 which  is  appropriate  for  text files.  If you are asking Kermit-10 to receive
 binary files from a microcomputer or other 8-bit system, you must first type SET
 FILE  BYTESIZE 8.  Otherwise, the 8th bit of each byte will be lost and the file
 will be useless when sent back to the system of origin.
0If you have SET PARITY, then 8th-bit prefixing will be requested.  If the  other
 side  cannot  do  this,  binary  files  cannot be transferred correctly.  In all
 cases, Kermit-10 will request the other Kermit to compress repeated  characters;
 if  the  other  side  can  do  this  (not  all  Kermits know how) there may be a
 significant improvement in transmission speed.
0If an incoming file does not arrive in its  entirety,  Kermit-10  will  normally
 discard  it; it will not appear in your directory.  You may change this behavior
 by using the command SET INCOMPLETE KEEP, which will cause as much of  the  file
 as arrived to be saved in your directory.
0If a file arrives that you don't really want, you can attempt to  cancel  it  by
 typing  Control-X;  this  sends a cancellation request to the remote Kermit.  If
 the remote Kermit understands this request (not all  implementations  of  Kermit
 support this feature), it will comply; otherwise it will continue to send.  If a
 file group is being sent, you can request  the  entire  group  be  cancelled  by
 typing Control-Z.
-
                                 The GET Command
0Syntax:  GET [remote-filespec]
0This command is for local mode only.
-
-
-DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  75
-
                                The STATUS Command
0Syntax:  STATUS
0Gives statistics about the file transfers for the entire session  and  the  most
 recent  file  transfer.   The  following  example  shows  the  steps required to
 transfer a small binary file to the DECsystem-10 and display the statistics  for
 the transfer.  The example shows the effect of SET FILE BYTE-SIZE 8, the RECEIVE
 command, and the STAT command output.
-Kermit-10>SET FILE BYTE-SIZE 8
+          ____________________
 Kermit-10>RECEIVE
+          _______
0Kermit-10>STAT
+          ____
0Totals since Kermit was started
  Total transfer time 0:01:13.900 (73.900 seconds)
  Characters sent 360
  Characters received 3876
  Data characters sent 0
  Data characters received 3048
  NAKs sent 1
  NAKs received 0
  Total packets sent 56
  Total packets received 56
  Effective data rate: 411 baud
0Totals for the last transfer
  Last transfer time 0:00:34.100 (34.100 seconds)
  Characters sent 177
  Characters received 1938
  Data characters sent 0
  Data characters received 1524
  NAKs sent 0
  NAKs received 0
  Effective data rate: 448 baud
0Kermit-10>EXIT
+          ____
-
-
-
-
-
0                                                Section 5 -- DECsystem-10 Kermit
176                                                  Kermit File Transfer Package
-
 5.5.2.  Server Operation
-                              The SERVER Command
0Syntax:  SERVER
0The SERVER command puts a remote Kermit-10 in "server mode," so that it receives
 all  further commands in packets from the local Kermit.  The Kermit-10 server is
 capable of executing the following remote server commands:  SEND,  GET,  FINISH,
 BYE,  REMOTE  DIRECTORY,  REMOTE  CWD, REMOTE SPACE, REMOTE DELETE, REMOTE TYPE,
 REMOTE HELP, and REMOTE STATUS.
0Any non-standard parameters should be selected with SET commands before  putting
 Kermit-10  into  server mode, in particular the file bytesize.  The DECsystem-10
 Kermit server will send most files  in  the  correct  manner  with  its  default
 setting  FILE  BYTESIZE  7.  However, if you need to ask the DECsystem-10 Kermit
 server to receive binary files from an 8-bit-byte system (that is,  from  almost
 any  system  that's  not  a DECsystem-10 or DECsystem-20) you must issue the SET
 FILE BYTESIZE 8 command before putting it into server mode, and  then  you  must
 only send 8-bit binary files.  You cannot send a mixture of text files and 8-bit
 binary files to a Kermit-10 server except for archiving them on a DECsystem-10.
-
-
-
-
-
-
-
-
-
-
-
 DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  77
-
 5.5.3.  Commands for Local File Management
0Syntax:  LOCAL command
0Execute the specified command on the local system -- on the  DECsystem-10  where
 Kermit-10  is  running.   These  commands  provide  some  local  file management
 capability without having to leave the Kermit-10 program.  These commands can be
 used  on  a remote Kermit as long as that Kermit is running interactively, i.e.,
 not in server mode.
0CWD [directory] or SET-PATH [directory]
                   Change working directory,  or,  in  DECsystem-10  terminology,
                   define the path to the specified directory.
0DELETE filespec or ERASE [filespec]
                   Delete the specified file or files.
0DIRECTORY [filespec]
                   Provide a directory listing of the specified files.
0SPACE or DISK-USAGE [directory]
                   Show how much space is used in the specified directory.  If no
                   directory is given, data for the current directory are shown.
0TYPE filespec
                   Display the contents of the specified file or  files  at  your
                   terminal.   This  works  like  the  DECsystem-10 TYPE command,
                   except that if a file has a bytesize of 8, Kermit-10  will  do
                   8-bit  input  from  it if you have SET FILE BYTESIZE 8.  Also,
                   the DECsystem-10 Control-O command discards output  only  from
                   the  file  currently  being  displayed;  if multiple files are
                   being typed, then output will resume with the next file.
0HELP
                   List these commands.
0STATUS
                   Displays statistics about file transfers for the session.  The
                   STATUS  command,  used  without  the  "LOCAL" prefix, displays
                   statistics about the most recent file transfer as well as  all
                   the file transfers for the session.
-
-
-
-
-                                                Section 5 -- DECsystem-10 Kermit
178                                                  Kermit File Transfer Package
-
 5.5.4.  The SET, SHOW, and DEFINE Commands
0SET is used for establishing or  changing  parameters,  DEFINE  lets  you  group
 several  SET  commands together into a single "macro" command, and SHOW lets you
 examine current settings or macro definitions.
-                                The SET Command
0Syntax:  SET parameter option value
0Establish or modify various parameters for file transfer or terminal connection.
 You  can  examine  their values with the SHOW command.  The following parameters
 may be SET:
0         BLOCK-CHECK Packet transmission error detection method
                DEBUG (This command is for LOCAL mode only)
                DELAY How long to wait before starting to send
               ESCAPE (This command is for LOCAL mode only)
                 FILE For setting file parameters like byte size
                  IBM (This command is for LOCAL mode only)
           INCOMPLETE What to do with an incomplete file
                 LINE (This command is for LOCAL mode only)
           LOCAL-ECHO (This command is for LOCAL mode only)
              MESSAGE (This command is for LOCAL mode only)
               PARITY Character parity to use
               PROMPT Change KERMIT's prompt
              RECEIVE Various parameters for receiving files
               REPEAT Character for repeat sequences
                RETRY How many times to retry a packet before quitting
                 SEND Various parameters for sending files
0The DEFINE command may be used to compose "macros" by  combining  SET  commands.
 Those  SET  commands  which  differ from the "ideal" Kermit are now described in
 detail.
-
 SET DEBUG
0Syntax:  SET DEBUG options
0This command is for local mode only.
-SET ESCAPE
0Syntax:  SET ESCAPE octal-number
0This command is for local mode only.
-
-DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  79
-
 SET FILE
0Syntax:  SET FILE parameter keyword
0Establish file-related parameters:
0BYTESIZE keyword or number
0         Byte size for DECsystem-10 file input/output.  The  choices  are  SEVEN
          (7), EIGHT (8), THIRTY-SIX (36), and AUTO.
0         SEVEN (or 7)
               Always store or retrieve five 7-bit bytes per word.  When  sending
               a file, ignore the file bytesize and do 7-bit input from the file.
               This insures transmission of all 36 bits.  The default is SEVEN.
0         EIGHT (or 8)
               Always store or retrieve four 8-bit bytes per word.  When  sending
               a file, ignore the file bytesize and do 8-bit input from the file.
               This command is necessary  when  receiving  and  returning  binary
               files from/to 8-bit-byte systems, such as most microcomputers.
0         THIRTY-SIX (or 36)
               Always store or retrieve five 7-bit bytes per word.  When  sending
               a file, ignore the file bytesize and do 7-bit input from the file.
               This insures transmission of all 36 bits.
0         AUTO
               Equivalent to  SEVEN  for  incoming  files,  and  SEVEN  or  EIGHT
               depending on the mode for outgoing.
0         The DECsystem-10 will frequently use the wrong byte-size  when  set  to
          AUTO.    Refer  to  Section  5.1.2  for  proper  settings  for  various
          transfers.
-NAMING UNTRANSLATED or NORMAL-FORM
0         If NORMAL-FORM, the  names  of  incoming  or  outgoing  files  will  be
          converted  to  contain  only uppercase letters, digits, and at most one
          period; any other characters will be replaced by 'X'.  If UNTRANSLATED,
          filenames  will  be  sent  and  used  literally.   UNTRANSLATED  is the
          default.
-SET LINE
0Syntax:  SET LINE [octal-number]
0This command is for local mode only.
-
-                                                Section 5 -- DECsystem-10 Kermit
180                                                  Kermit File Transfer Package
-
 SET LOCAL-ECHO
0Syntax:  SET LOCAL-ECHO ON or OFF
0This command is for local mode only.
-SET MESSAGE
0Syntax:  SET MESSAGE type
0This command is for local mode only.
-SET RECEIVE
0Syntax:  SET RECEIVE parameter value
0In addition to the full complement of SET RECEIVE commands described in the main
 part  of the Kermit File Transfer Package, you may also SET RECEIVE TIMEOUT to a
 value between 0 and 94.  This specifies the number of seconds  between  timeouts
 during  server  command  wait,  0 specifies that no timeouts should occur during
 server command wait.  When a Kermit server times out, it  sends  a  NAK  packet.
 Some  systems  cannot  clear  piled-up  NAKs from their input buffers; if you're
 using such a system to communicate with a Kermit-10 server, and you expect to be
 leaving the server idle for long periods of time, you should use this command to
 turn off server command-wait timeouts.
-SET REPEAT
0Syntax:  SET REPEAT value
0This command sets the character to be used as the lead-in character for a repeat
 sequence  (a  string  of  characters  which represents some number of characters
 which are repeated in the data).  Both Kermits must support  repeat  compression
 for  this  to  be  in  effect.  The character set by this command must be in the
 range 41 ("1") to 76 (">") or 140 ("\") to 176 ("~").  The character  will  only
 be used on files which are being transmitted by Kermit-10.  The repeat character
 used for incoming files is determined by the other Kermit.  The default value is
 176 ("~").  A value of 40 (a space) will disable repeat compression.
0     Kermit-10>SET REPEAT nnn
+               ______________
0Where nnn is the ASCII value for the repeat quoting character in octal.
-
-
-
0DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  81
-
                                The DEFINE Command
0Syntax:  DEFINE macroname [set-option [, set-option [...]]]
0The DEFINE command is available  in  Kermit-10  for  building  "macros"  of  SET
 commands.  The macro name can be any keyword-style character string, and the set
 options are anything you would type after SET in  a  SET  command;  several  set
 options may be strung together, separated by commas.  Example:
0 define notimeout send timeout 0, receive timeout 0, receive server 0
0Macro definitions may not include macro names.  You can list all your macros and
 their definitions with the SHOW MACROS command.
-
                                 The SHOW Command
0Syntax:  SHOW [option]
0The SHOW command displays various information:
0DAYTIME     Current date, and time.
0DEBUGGING   Debugging mode in effect, if any.
0FILE-INFO   Byte size for DECsystem-10 file I/O, incomplete file disposition.
0LINE-INFO   TTY line, parity, local-echo, handshake, escape character, speed (if
             known), and session logging information.
0MACROS      Definitions for SET macros.
0PACKET-INFO For incoming and outbound packets.  Items under RECEIVE column  show
             parameters  for  packets  Kermit-10  expects  to receive, under SEND
             shows parameters for outgoing packets.
0TIMING-INFO Delays, retries, server NAK intervals.
0VERSION     Program version of Kermit-10.  This is also displayed when Kermit-10
             is initially started.
0ALL         (default) All of the above.
-
-
-
-
                                                 Section 5 -- DECsystem-10 Kermit
182                                                  Kermit File Transfer Package
-
 The following example shows the default  settings  as  displayed  via  the  SHOW
 command.
0Kermit-10> SHOW
+           ____
 TOPS-10 Kermit version 3(133)
  2-Apr-86 21:56:36
0Line being used is TTY14: (DOC(43):: line # 10)
   Handshake: X?
   Parity:      none
   Local echo:  off  Escape:      XY
   XON-XOFF-processing:  default
0File type is 7-bit
 File naming: Normal form file specifications
 File warning is off
 Disposition for incomplete received files: Discard
0File specification type out is on
 Packet number type out is off
 Debugging is off
0Packet parameters:
                     Receive        Send
   Size:                  80          80 chars
   Padding:                0           0
   Pad Character:         X@          X@
   End-Of-Line:           XM          XM
   Control Quote:          #           #
   Start-of-Packet:       XA          XA
0 8th-bit Quote character &
  Repeat Quote character  ~
  Block check type is 3 character CRC-CCITT
0Timing parameters:
                     Receive        Send
   Time out:              15          15 secs
0  Delay before sending first packet: 5 secs
   Packet retries before timeout: 16
   Number of retries for initial packet: 5
   Server NAKs every 75 seconds while waiting for commands
-  No defined macros
-
-
-
 DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  83
-
 5.5.5.  Program Management Commands
-                                The TAKE Command
0Syntax:  TAKE filespec
0Execute Kermit-10 commands from  the  specified  file.   The  file  may  contain
 contain  any  valid  Kermit-10  commands, including other TAKE commands; command
 files may be nested up to a depth of 20.  Default file type for the command file
 is .CMD.
-                                The HELP Command
0Syntax:  HELP [topic [subtopic]]
0Typing HELP alone prints a brief summary of Kermit-10 and its commands.  You can
 also type
0  HELP command
0for any Kermit-10 command, e.g., "help send" or "help set parity"  to  get  more
 detailed information about a specific command.
-
                            The EXIT and QUIT Commands
0Syntax:  EXIT or QUIT
0Exit from Kermit-10.  You can CONTINUE the program from  the  MONITOR,  provided
 you  haven't run another program on top of it.  You can also exit from Kermit-10
 by typing one or more control-C's, even if it's in the middle of transferring  a
 file.   Kermit-10  will  always restore your terminal to its original condition,
 and you will be able to CONTINUE the program to get back to "Kermit-10>" command
 level with current settings intact.
0QUIT is a synonym for EXIT.
-                                The LOG Command
0Syntax:  LOG [option [filespec]]
0This command is for local mode only.
-
-
-
                                                 Section 5 -- DECsystem-10 Kermit
184                                                  Kermit File Transfer Package
-
 5.6.  Raw Download
0This facility is for local mode only.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  85
-
 5.7.  Kermit-10 Examples
0Here are a few examples of the use of Kermit-10.  Text entered by  the  user  is
 underlined.
-                                Remote Operation
0The following example shows use of Kermit-10 as a server from  an  IBM  PC.   In
 this  example, the user runs Kermit on the PC, connects to the DECsystem-10, and
 starts Kermit-10 in server mode.  From  that  point  on,  the  user  need  never
 connect  to  the DECsystem-10 again.  In this example, the user gets a file from
 the DECsystem-10, works on it locally at the PC, and then sends the results back
 to  the DECsystem-10.  Note that the user can leave and restart Kermit on the PC
 as often as desired.
0 A>______
+   kermit
  Kermit-MS>connect
+           _______
  .
  .k_____
+  _ermit
  TOPS-10 Kermit version 3(133)
0 Kermit-10>server
+           ______
0     [Kermit Server running on  DECsystem-10  host.   Please  type  your  escape
      sequence  to  return to your local machine.  Shut down the server by typing
      the Kermit BYE command on your local machine.]
0 X]C
+ ___
  Kermit-MS>get foo.txt
+           ___________
0     ;The transfer takes place.
0 Kermit-MS>exit
+           ____
  A>
  A>edit foo.txt ; (or whatever...)
+   ____________
  A>
  A>k_____
+   _ermit
  Kermit-MS>send foo.txt
+           ____________
0     ;The transfer takes place.
0 Kermit-MS>bye
+           ___
  A>
-
-
-
-                                                Section 5 -- DECsystem-10 Kermit
186                                                  Kermit File Transfer Package
-
 The next example shows the special procedure you would have to use in  order  to
 send  a  mixture of text and binary files from a PC (or an 8-bit-byte system) to
 the DECsystem-10.  Note that in this case, it's more convenient to avoid  server
 mode.
0 Kermit-MS>connect
+           _______
  .
  .k_____
+  _ermit
  TOPS-10 Kermit version 3(133)
0 Kermit-10>receive
+           _______
  X]C
+ ___
  Kermit-MS>send *.txt
+           __________
0     ;Textual files are sent.
0 Kermit-MS>connect
+           _______
  Kermit-10>set file bytesize 8
+           ___________________
  Kermit-10>receive
+           _______
  X]C
+ ___
  Kermit-MS>send *.exe
+           __________
0     ;Binary files are sent.
0 Kermit-MS>connect
+           _______
  Kermit-10>exit
+           ____
  .logout
+  ______
  X]C
+ ___
  Kermit-MS>exit
+           ____
  A>
-
-
-
-
-
-
-
-
0DECsystem 10 Kermit -- Section 5
1Kermit File Transfer Package                                                  87
-
 6.  TSO Kermit
0TSO Kermit Capabilities At a Glance:
0      Local operation:  No
       Remote operation:  Yes
       Transfers text files:  Yes
       Transfers binary files:  Yes
       Wildcard send:  Yes
       XX/XY interruption:  Yes
       Filename collision avoidance:  No
       Timeouts:  Yes
       8th-bit prefixing:  Yes
       Repeat character compression:  Yes
       Alternate block check types:  Yes
       Communication settings:  No
       Transmit BREAK:  No
       IBM mainframe communication:  Yes
       Transaction logging:  No
       Session logging:  No
       Debug logging:  Yes
       Raw transmit:  No
       Login scripts: No
       Act as server:  Yes
       Talk to server: No
       Advanced commands for servers:  No
       Local file management:  Yes
       Command/init files:  Yes
       Handle file attributes:  No
0KERMIT is a set of programs that transfers files between computers  over  normal
 terminal  communication  lines.   Originally  designed  to  be  used  between  a
 microcomputer and the DEC-20 mainframe, the protocol will  also  transfer  files
 between a microcomputer and an IBM mainframe system running under MVS/TSO.  This
 version, called TSO Kermit, was developed at NIH based upon  the  University  of
 Chicago TSO version, which was in turn based upon a VM/CMS version from Columbia
 University.
0KERMIT transfers data by creating packets with information regarding the type of
 packet  being  sent,  its  length,  a packet number, and a checksum to determine
 whether the data has been modified during transmission.  If a packet is lost  or
 garbled, Kermit will attempt to resend it.
0MVS/TSO stores files as records rather than byte streams.  MVS/TSO Kermit has to
 assemble   incoming   data  packets  into  records  and  strip  CRLFs  (carriage
 return/line feed characters) from incoming  lines,  and  also  append  CRLFs  to
 outgoing records.
0You must be  emulating  an  ASCII  terminal  (rather  than  a  3270)  with  your
 microcomputer  to  run  TSO Kermit.  Kermits that do not support 8th-bit-quoting
 cannot do binary file transfers with TSO Kermit.
-
0                                                         Section 6 -- TSO Kermit
188                                                  Kermit File Transfer Package
-
 6.1.  The IBM MVS File System
0Since TSO Kermit runs under TSO, the user must be aware of the MVS TSO data  set
 naming  conventions.  Since data set names are specified differently in MVS than
 in MS-DOS or APPLE-DOS, care should be exercised in selecting the names for data
 sets  on  the  target  system  when  data sets are being transmitted between two
 unlike file systems.  The following discussion is to  help  with  this  planning
 process on the TSO Kermit side.
0Data sets on the online storage volumes are distinguished from  one  another  by
 associating  with  each  data  set  a unique name, known as the data set name or
 "dsname."  All data set names on the online storage volumes begin with a  prefix
 containing  the  user's  account  number,  followed by the user's initials and a
 period.  TSO automatically attaches this prefix to the data set  name  specified
 by  the  user.  Thus, if the user's account is AAAA and initials are III, a data
 set named PROGRAM will be stored by TSO as AAAAIII.PROGRAM.  Such  a  completely
 specified  data  set  name is referred to as "fully qualified."  Normally, fully
 qualified data set names are not used in TSO Kermit unless it  is  necessary  to
 refer to another user's data set.
0The SET PREFIX command may be used to specify a data set name prefix to be  used
 as  the  first part of all the data set names for the duration of the TSO Kermit
 session (e.g., if the prefix is "TASK1."  then the fully qualified data set name
 will start with "AAAAIII.TASK1."). The prefix may be overridden by enclosing the
 data set name in quotes.
0Data set names may be up to 44 characters long, but the user selected portion of
 the  dsname  is limited to 36 characters unless it is fully qualified, since the
 first eight characters are reserved for  the  account-initials  prefix.   Unless
 otherwise  stated, the term "dsname" will refer to the data set name without the
 prefix.  Alphanumeric characters (letters and digits), national  characters  (@,
 $,  #),  and  the  special  characters  period  (.)  and hyphen (-) are the only
 characters allowed to form a dsname.
0All data sets used with TSO Kermit must be cataloged.  The  first  character  of
 the  dsname  and  the  first character following a period in a dsname must be an
 alphabetic or national (@, $, #) character, and periods must be used  to  divide
 the  name  into  groups of eight or fewer characters (not counting the periods).
 The data set name is divided by the periods into levels.  A data set  cannot  be
 cataloged  if there is already a data set cataloged with a name that is the same
 through one of the levels.  For example, if AAAAIII.MEMO.COSTS is the name of  a
 cataloged   data   set,   it   is   valid   to   catalog   a   data   set  named
 AAAAIII.MEMO.FINANCE, but it is invalid to catalog AAAAIII.MEMO.COSTS.FINAL. The
 reverse  is  also  true.   For example, if a data set named AAAAIII.DATA.JULY is
 cataloged, the data set AAAAIII.DATA cannot be cataloged,  while  the  data  set
 AAAAIII.DAT can be cataloged.
0For data sets which have been created and not cataloged, the user  may  use  the
 TSO or WYLBUR CATALOG command to catalog the data set.
0TSO Kermit supports a full range of MVS RECFM (record  format),  LRECL  (logical
 record  length), and BLKSIZE (block size) options.  Note that the default format
-
 TSO Kermit -- Section 6
1Kermit File Transfer Package                                                  89
-
 for text data sets uploaded using TSO Kermit is WYLBUR edit  format.   The  user
 may  specify  which volume the file will be saved and catalogued on by using the
 TSO Kermit SET VOLUME command.  If no volume is set, TSO Kermit will select  any
 available TMP volume.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
                                                          Section 6 -- TSO Kermit
190                                                  Kermit File Transfer Package
-
 6.2.  Program Operation
0TSO Kermit is run interactively under TSO.  In the examples  that  follow,  user
 input is underlined (to distinguish it from prompts, etc.). Enter
+         __________
0KERMIT
+______
0in order to commence a TSO Kermit session, or alternatively,
0KERMIT <command>
+________________
0in order to initiate a TSO Kermit session and execute a TSO Kermit command.
0When TSO Kermit is communicating with the terminal directly it can be recognized
 by its prompt:
0KERMIT-TSO>
0The following example shows the default environment set up by TSO Kermit when it
 is  initially invoked from TSO.  The default parameter settings may be displayed
 at any time during your  Kermit  session  by  issuing  the  SHOW  command.   For
 example,
0KERMIT-TSO> SHOW
+            ____
0Data Set Attributes                     Protocol Attributes
 DATA: Text                              DELAY (after SEND): 20 seconds
 EDIT (WYLBUR edit format data set): on  TIMER (Timeout interval): on (8 seconds)
 NUMBERED (line nos.): off               BLOCK (Block check type): 3 (CRC)
 TABS: off                               PACKET (Receive packet size): 94
 RECFM (Record format): VB               CQUOTE (Control quote character): #
 LRECL (Logical record length): 504      BQUOTE (Binary quote character): &
 BLKSIZE (Block size): 6356              RQUOTE (Repeat quote character): ~
 SPACE (Space allocation): 5 tracks      SOH (Start of Header): 1 (SOH,XA)
 VOLUME: TMP                             SEOL (Send End-of-line): 13 (CR,XM)
 PREFIX: No prefix                       REOL (Receive End-of-line): 13 (CR,XM)
                                         DEBUG: off
0Values displayed by the SHOW command may be  modified  by  the  TSO  Kermit  SET
 command.
0KERMIT-TSO> SET <parameter> <value>
+            _______________________
-
-
-
-
0TSO Kermit -- Section 6
1Kermit File Transfer Package                                                  91
-
 In the example that follows, note that initially TSO Kermit is set up  for  text
 (rather  than  binary) data sets, with WYLBUR edit format as the default.  Since
 data sets stored in WYLBUR edit format are compressed,  they  will  appear  very
 strange  if  listed  with the TSO LIST command or processed by any other program
 that does not support edit format.
0TSO Kermit provides the user with the option  of  executing  most  TSO  commands
 without  exiting  from  TSO  Kermit  by  simply  prefixing  the command with the
 characters TSO.  For example,
0KERMIT-TSO> TSO LISTC
+            _________
0The TSO LISTC command will list all the data set names in the catalog under  the
 account and initials for the TSO session.
0If the user has a standard sequence of commands  to  be  issued  each  time  TSO
 Kermit  is  run,  these  commands  may  be saved in a data set and automatically
 executed by TSO Kermit.  KERMIT.PROFILE.CLIST is the name of the "profile"  data
 set  which  is  executed  automatically by TSO Kermit if it exists.  Note:  This
 data set must not be in WYLBUR edit format.
0Since it would be inconvenient to frequently logoff TSO  and  logon  to  WYLBUR,
 users  have  the  ability  to  execute WYLBUR under TSO.  This means that Kermit
 users can avail themselves of the facilities of TSO Kermit and  still  have  the
 capabilities of WYLBUR at their disposal as follows:
0KERMIT-TSO> TSO ______
+            ____WYLBUR
0As soon as WYLBUR is invoked, the prompt changes to the familiar WYLBUR prompt:
0?
0At this point the user may enter WYLBUR commands and use WYLBUR to process  data
 received  by Kermit or to do anything else.  When finished, the user simply uses
 the WYLBUR END command to return to the Kermit prompt:
0KERMIT-TSO>
0Likewise, it is possible to invoke TSO Kermit from within WYLBUR  under  TSO  by
 using  the  WYLBUR  TSO command.  The example that follows illustrates the above
 capabilities, and shows the desired  method  for  transmitting  a  file  from  a
 microcomputer  to  the  IBM  System  370  and  from  the  IBM  System  370  to a
 microcomputer.
-
-
-
-
                                                          Section 6 -- TSO Kermit
192                                                  Kermit File Transfer Package
-
 The  following  dialing  procedure  assumes  you  have  started  Kermit  on  the
 microcomputer and are using a Hayes compatible modem.
0___________
+ATDT4922223
 CONNECT
 logon
+_____
 INITIALS? iii
+          ___
 ACCOUNT? aaaa
+         ____
 KEYWORD? kkk
+         ___
 TERMINAL? none
+          ____
 BOX? nnn
+     ___
 AAAAIII LOGON IN PROGRESS AT 11:26:19 ON JUNE 11, 1986
  NIH/DCRT/CCB TSO
 TSO LINE 13B
 READY
 kermit
+______
 NIH TSO KERMIT VERSION 1.0
 KERMIT-TSO>
0Prior to transmitting the file from the microcomputer, the user must assure that
 no  file  naming  conflict  exists  on  the  IBM System 370.  In this example, a
 currently existing version of the file to  be  transferred,  TREE.TXT,  must  be
 deleted on the host prior to initiating the transfer.  The TSO DELETE command is
 issued.
0KERMIT-TSO> tso delete tree.txt
+            ___________________
0ENTRY (A) AAAAIII.TREE.TXT DELETED
0The only TSO Kermit command required is a SERVER command which puts  TSO  Kermit
 into a state to process commands issued from the microcomputer.
0KERMIT-TSO> server
+            ______
  Now entering SERVER mode - type FINISH or LOGOUT on micro to halt SERVER
0At this point, TSO Kermit is in server mode and is waiting for the commands from
 the remote Kermit.
-
-
-
-
-
-
 TSO Kermit -- Section 6
1Kermit File Transfer Package                                                  93
-
 Now we must issue commands to KERMIT on the microcomputer (this example  assumes
 an  IBM  PC  running  MS-DOS  Kermit),  without breaking the connection with TSO
 Kermit.  We do this by issuing the escape sequence:
0___
+X]C
0The notation above means:  press and hold the Ctrl Key,  then  press  the  right
 bracket, release both keys and press the 'C' key.
0This results in the microcomputer Kermit issuing its prompt:
0Kermit-MS> send tree.txt
+           _____________
0Issuing the SEND command starts up transfer of the PC-DOS file TREE.TXT from the
 microcomputer  to  TSO.   During  the  transfer, statistics are displayed at the
 microcomputer terminal until the  transfer  completes,  and  the  normal  Kermit
 command prompt is re-displayed:
0Kermit-MS> get log.dat
+           ___________
0Issuing the GET command starts up transfer of the data set LOG.DAT from  TSO  to
 the  microcomputer.   During  the  transfer,  statistics  are  displayed  at the
 microcomputer terminal until the  transfer  completes,  and  the  normal  Kermit
 command prompt is re-displayed:
0Kermit-MS> finish
+           ______
0After the file LOG.DAT has been  transferred  to  the  PC,  issuing  the  FINISH
 command  terminates  server  mode  on TSO Kermit.  At this point Kermit is still
 running on both the PC and TSO and the user has the option of issuing a  CONNECT
 command,  terminating  TSO Kermit, and logging off, or continuing the TSO Kermit
 session.
0Kermit-MS> connect
+           _______
0After receiving the TSO Kermit prompt, issue the QUIT command to return  to  the
 TSO prompt and then LOGOFF normally.
0KERMIT-TSO> quit
+            ____
 READY
 ______
+logoff
0Type the escape sequence to get back to the KERMIT prompt on the  PC,  and  then
 issue a QUIT command to return to the DOS prompt.
0X]C
+___
 Kermit-MS> quit
+           ____
 A>
-
-
0                                                         Section 6 -- TSO Kermit
194                                                  Kermit File Transfer Package
-
 6.2.1.  Starting TSO Kermit
0After the TSO session has been started, the KERMIT command  is  used  to  invoke
 Kermit.   The  user can simply type the KERMIT command, or can invoke TSO Kermit
 and execute a specified command in one step by following KERMIT with a valid TSO
 Kermit command.
0KERMIT
0      or
0KERMIT <TSO Kermit command>
0For example:
0KERMIT SERVER  (to initiate Kermit in server mode)
      or
 KERMIT EXEC xxx (where xxx is the name of a TSO CLIST containing Kermit commands)
-
-
-
-
-
-
-
-
-
-
-
-
0TSO Kermit -- Section 6
1Kermit File Transfer Package                                                  95
-
 6.2.2.  TSO Kermit Commands
0TSO Kermit includes the following commands.  Refer to the  detailed  explanation
 of each command as necessary.
0Command      Function
+_______      ________
0END          Terminate TSO Kermit and return to TSO  (a  synonym  for  EXIT  and
              QUIT)
0EXEC         Execute TSO Kermit commands from a CLIST data set
0EXIT         Terminate TSO Kermit and return to TSO (a synonym for END and QUIT)
0FINISH       Terminate server mode for file transfer  (normally  issued  to  the
              local Kermit, but accepted by TSO Kermit as well)
0HELP         Tell how to display list of Kermit commands or command operands
0KERMIT       Used in CLISTs to prefix Kermit SET commands to distinguish  Kermit
              SET from TSO SET commands
0QUIT         Terminate TSO Kermit and return to TSO (a synonym for END and EXIT)
0RECEIVE      Put TSO Kermit in RECEIVE mode for incoming files
0RESET        Reset initial default Kermit parameter settings
0SET          Change data and protocol options
0SEND         Start transmission of a file or files
0SERVER       Put TSO Kermit into server mode for file transfer
0SHOW         Display data and protocol parameter settings
0STATUS       Display status information for last file transfer
0STOP         Abort a RECEIVE or SEND command
0TSO          Invoke TSO commands under TSO Kermit
0?            Display a list of TSO Kermit commands
0TSO Kermit commands may be abbreviated as follows:
0END (E); EXEC (X, EX, EXEC, XEQ); RECEIVE (REC); SHOW (SH); STATUS (STAT)
-
-
-                                                         Section 6 -- TSO Kermit
196                                                  Kermit File Transfer Package
-
 6.3.  Conditioning Your Session for Kermit
0Prior to communicating with TSO Kermit,  a  remote  Kermit  must  establish  the
 appropriate protocol parameters for IBM MVS TSO.
0Do not use SET IBM or DO IBM commands on those Kermits that have these  commands
 as  they  are  usually  intended for use with the IBM VM/CMS system, rather than
 TSO.  The following discussion tells you what parameters must  be  set  and  the
 values to use.
0Parameters that must be SET on the microcomputer Kermit for  communication  with
 WYLBUR or TSO.
0APPLE ][ Kermit            IBM PC Kermit              "IDEAL" Kermit
 --------------------       -------------------------  --------------------
                            FLOW-CONTROL NONE          FLOW-CONTROL NONE
                            HANDSHAKE NONE             HANDSHAKE NONE
 LOCAL-ECHO ON              LOCAL-ECHO ON              DUPLEX HALF
 PARITY EVEN                PARITY EVEN                PARITY EVEN
 BAUD-RATE as desired       SPEED as desired           BAUD-RATE as desired
 LINEFEED OFF               TERMINAL NEWLINE-MODE OFF
 EIGHT-BIT-QUOTING ON
 --------------------------------------------------------------------------
0NIH provides an MSKERMIT.INI file for MS-DOS Kermit for the IBM PC that  defines
 a  DO  TSO  command  that  will  set appropriate options for TSO.  MS-DOS Kermit
 automatically executes the commands in this file each time  Kermit  is  started,
 but  the user must manually issue the DO TSO command unless it has been added to
 the MSKERMIT.INI file.
0TSO Kermit does as much as it can to condition your session for  file  transfer.
 It sets common defaults for data and protocol settings.  In addition, TSO Kermit
 can be set up to automatically establish data and  protocol  settings  different
 from  the  defaults if the user so desires.  This is done by executing a PROFILE
 of commands stored in a data set when TSO Kermit is initiated.  This is  how  it
 works:   the  user creates a cataloged data set named KERMIT.PROFILE.CLIST. This
 data set must have line numbers in the last 8 columns if it is RECFM=FB,  or  in
 columns 1/8 if it is RECFM=VB (it may not be WYLBUR edit format).  You may store
 any TSO Kermit COMMANDS you wish in this data set and they will be automatically
 executed every time you execute Kermit under TSO.
0Note that the KERMIT command is specifically provided under TSO Kermit to  allow
 users  to  specify that, in a CLIST, SET commands prefixed with Kermit are to be
 treated as Kermit SET commands instead of TSO CLIST SET commands.
-
-
-
-TSO Kermit -- Section 6
1Kermit File Transfer Package                                                  97
-
 6.4.  TSO Kermit Commands
06.4.1.  Server Operation
0The SERVER command puts a remote  TSO  Kermit  in  "server  mode,"  so  that  it
 receives all further commands in packets from the microcomputer Kermit.  The TSO
 Kermit server is capable (as of this writing) of executing the following  remote
 server commands:
0      GET remote-filespec
0               Transfer  the  TSO  file(s)  named  in  remote-filespec  to   the
                microcomputer.
0      SEND filespec1 [filespec2]
0               Transfer the microcomputer file(s) named in filespec1 to TSO.  If
                filespec1  is  a  single  file, filespec2 can be used to override
                filespec1 as the data set named used by TSO.
0      FINISH   Terminates server mode  and  returns  the  microcomputer  to  the
                Kermit prompt.
0      LOGOUT   Terminates server mode, terminates TSO session on the  host,  and
                returns the microcomputer to the Kermit prompt.
0      BYE      Terminates server mode, terminates the TSO session on  the  host,
                terminates   Kermit   on   the  microcomputer,  and  returns  the
                microcomputer to the DOS prompt.
0Any non-standard parameters should be selected with SET commands before  putting
 TSO Kermit into server mode.  If you forget to do this, issue the FINISH command
 to the local Kermit to exit server mode, issue  the  appropriate  SET  commands,
 then  issue  the SERVER command to get back into server mode.  The principal use
 of the SERVER command and server mode of TSO Kermit is to simplify the  commands
 that  must  be  issued  to effect file transfers.  When finished with the server
 mode,  the  user  must  issue  the  FINISH,  BYE,  or  LOGOUT  command  to   the
 microcomputer  Kermit  to  terminate  server mode on the TSO Kermit side.  After
 placing TSO Kermit in server mode, type the escape  sequence  (Control-]  C  for
 MS-DOS  Kermit)  and  then  issue  GET  or  SEND commands from the microcomputer
 Kermit.  Server mode simplifies the file transfer process in  that  you  do  not
 have  to  constantly  issue  the  Kermit escape sequence and CONNECT commands to
 switch which Kermit you are giving commands to.  When TSO KERMIT is operating in
 server mode, it receives its commands from the microcomputer Kermit.
0TSO Kermit will respond to FINISH entered in terminal mode, as well as a command
 to the microcomputer; this is especially useful if the microcomputer Kermit does
 not support server mode.
0TSO Kermit supports file transfer of members of a partitioned  data  set  (PDS).
 The  member  name is specified in parentheses immediately following the data set
 name for the PDS.
-
                                                          Section 6 -- TSO Kermit
198                                                  Kermit File Transfer Package
-
 When receiving files, if the record format is fixed, any record longer than  the
 logical  record  length  will be truncated.  The record length can be as high as
 32760.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0TSO Kermit -- Section 6
1Kermit File Transfer Package                                                  99
-
 6.4.2.  Commands for File Transfer
0The SEND and RECEIVE commands are used for file transfer when TSO Kermit is  not
 in server mode.
-RECEIVE [data set name]
0Receive one or more files sent from the microcomputer.  If the data set name  is
 not  specified,  TSO  Kermit will use the name passed from the microcomputer for
 the first file received.  If no data set previously exists with this name a file
 will  be  created  and cataloged.  The attributes for the data set will be taken
 from the DATA, EDIT, RECFM, LRECL, BLKSIZE and SPACE parameters.  If a data  set
 or  member  of  a partitioned data set (PDS) already exists, TSO Kermit will ask
 you if you want to delete the existing file.  If not, the transfer will stop.
0TSO Kermit supports file transfer of members of an existing partitioned data set
 (PDS).   The  member  name is specified in parentheses immediately following the
 data set name for the PDS.
0When receiving files, if the record format is fixed, any record longer than  the
 logical  record  length  will be truncated.  The record length can be as high as
 32760.
0STOP may be entered to abort the RECEIVE command at any time.
-SEND [data set name]
0Send the specified data set  or  data  sets.   If  the  data  set  name  is  not
 specified, TSO Kermit will prompt for one.  The data set must be cataloged.
0One wildcard character '*' (asterisk) is allowed in the  data  set  name.   This
 allows  specifying  that  a  group  of files is being sent, or that any one file
 meeting the wildcarded naming specification will be sent.  The '*'  matches  any
 character  or characters.  A data set name like "NAME.*" will result in all data
 sets being sent whose names  begin  with  "NAME."   A  data  set  name  such  as
 "ABC.*.XYZ"  will  result  in  all  data  sets being sent whose names begin with
 "ABC."  and end with ".XYZ". The "*" wild card cannot be used in  PDS  data  set
 names or in PDS member names.
0TSO Kermit supports file transfer of members of an existing partitioned data set
 (PDS).   The  member  name is specified in parentheses immediately following the
 data set name for the PDS.
0The file name that TSO Kermit  sends  to  the  other  Kermit  is  the  last  two
 qualifiers   (levels)   of   the   data  set  name,  but  always  excluding  the
 account/initials prefix.  For a PDS member, TSO Kermit sends  the  name  of  the
 member as the file name.
-
-
                                                          Section 6 -- TSO Kermit
1100                                                 Kermit File Transfer Package
-
 6.4.3.  Commands for Local Data Set Management
0TSO Kermit allows very flexible use of  TSO  commands  and  WYLBUR  commands  to
 effect  TSO  data set management tasks while running under TSO Kermit.  In order
 to use TSO commands, one merely invokes the following command:
0KERMIT-TSO> TSO <TSO command>
+            _________________
0For example, it is possible to use TSO to list  data  set  attributes  with  the
 following command:
0KERMIT-TSO> TSO LISTD <data set name>
+            _________________________
0It is possible to use TSO to list the names of  cataloged  data  sets  with  the
 following command:
0KERMIT-TSO> TSO LISTC
+            _________
0It is possible to use TSO to list contents of a non-edit format  data  set  with
 the following command:
0KERMIT-TSO> TSO LIST <data set name>
+            ________________________
0It is possible to invoke WYLBUR under TSO with the following command:
0KERMIT-TSO> TSO WYLBUR
+            __________
-
-
-
-
-
-
-
-
-
-TSO Kermit -- Section 6
1Kermit File Transfer Package                                                 101
-
 6.4.4.  The SET, RESET, and SHOW Commands
0The SET command establishes or modifies various parameters  for  file  transfer.
 The  RESET  command  changes  the  parameter  settings to the TSO Kermit default
 values.  You can examine the parameter values with the SHOW command.
0SET <parameter> <value>
0Set the parameter to the specified value.  Legal SET parameters are:
0DATA       Specifies if any transformation is to be performed  on  incoming  and
            outgoing   data.    TEXT  (ASCII-EBCDIC  conversion)  or  BINARY  (no
            conversion).  The default for DATA is TEXT.
0EDIT       ON or OFF (ON specifies received data sets will be stored  in  WYLBUR
            edit format).  The default for EDIT is ON.
0NUMBERED   Specifies line numbering options for non-edit format text data sets:
0           OFF - unnumbered (no line numbers in data set)
            WYLBUR - WYLBUR line numbers in default columns
            WYLBUR m/n - WYLBUR line numbers in columns m through n
            TSO - TSO line numbers in default columns
            TSO m/n - TSO line numbers in columns m through n
0           Default columns are the last eight for data sets with RECFM=F or  FB,
            and first eight for data sets with RECFM=V, VB, or U.
0           The default for NUMBERED is OFF.
0TABS       Controls TAB processing on upload and download of text files.
0           OFF  disables TAB processing.
            ON   assumes tabs are set every 8 positions on the  microcomputer and
                 changes  tabs to blanks in received data sets and blanks to tabs
                 in transmitted data sets.
0           Tab    positions    may    also    be    specified    as    "column",
            "column+interval*count", and/or "column + interval/max"
0           column+interval*count means tab at "column" plus every "interval" for
            "count" times for a total of count + 1 tabs.
0           column+interval/max means the same except tabs  are  set  up  to  the
            "max"  column  specified  instead  of  up to the number of tabs being
            specified by "count".
0           The default for TABS is OFF.
0RECFM      Record format for received non-edit format data sets.   Valid  record
            formats are F, FB, V, VB, VBS or U. The default for RECFM is VB.
-
0                                                         Section 6 -- TSO Kermit
1102                                                 Kermit File Transfer Package
-
 LRECL      Logical record length for received  non-edit  format  data  sets  The
            default for LRECL is 504, and the maximum is 32760.
0BLKSIZE    Block size for received non-edit format data sets.  The  default  for
            BLKSIZE is 6356, and the maximum is 32760.
0SPACE      Space allocation for received data sets  in  tracks,  used  for  both
            primary and secondary allocation values.  The default for SPACE is 5,
            and the maximum is 32767.
0VOLUME     Specifies which disk volume will be used for the received  data  set.
            VOLUME  requires  a  6 character volume serial number (e.g., FILE24),
            except that TMP means that any TMP volume may be used.   The  default
            for VOLUME is TMP.
0PREFIX     Like WYLBUR's SET PREFIX command, specifies characters to be prefixed
            to  the  front  of data set names.  Be sure to include the period (.)
            qualifier as needed.  The account-initials prefix (e.g., AAAAIII.) is
            assumed  to  precede  this prefix (unless the prefix is in quotes, in
            which case it is assumed to  be  fully  qualified).   A  PDS  can  be
            specified  as  a prefix by entering the PDS data set name followed by
            an open and close parenthesis, such  as,  PDSNAME();  all  subsequent
            data  set  names will be treated as the names of members of that PDS;
            part of the member name can also be  specified  (e.g.,  PDSNAME(AB)).
            The default is NO PREFIX.
0NOPREFIX   Nullifies previously set prefix.
0DELAY      Specifies the number of seconds that  TSO  Kermit  waits  before  the
            first packet is sent by the SEND command.  The default DELAY is 20.
0TIMER      Controls timeout processing for received packets.  TSO Kermit sends a
            NAK  (negative  acknowledgement)  packet  after  the timeout interval
            expires.  After 20 retries, TSO Kermit terminates the file  transfer.
            Valid  values  are OFF (turns off timeout), ON (turns on timeout), or
            the number of seconds to be  used  for  the  timeout  interval.   The
            default for TIMER is ON, with an interval of 8 seconds.
0BLOCK      Specifies which type of Kermit block checking will  be  used.   Valid
            options  are  1  (1-byte  checksum),  2  (2-byte checksum), 3 (3-byte
            cyclic redundancy check), or CRC (synonym for 3).   The  default  for
            BLOCK is 3.
0PACKET     Sets the maximum packet length.  Valid values are 26-94 decimal,  The
            default for PACKET is 94.
0CQUOTE     Specifies the character used for prefixing ASCII control  characters.
            Value  must  be between 33-62 or 96-126 decimal, indicating the ASCII
            code for the character.  The actual character may also be  specified,
            optionally in quotes.  The default for CQUOTE is #.
-
-TSO Kermit -- Section 6
1Kermit File Transfer Package                                                 103
-
 BQUOTE     Specifies the 8th bit quote character used for  prefixing  characters
            that  have  their  8th bit on.  Value must be between 33-62 or 96-126
            decimal, indicating the ASCII code for  the  character.   The  actual
            character  may  also be specified, optionally in quotes.  The default
            for BQUOTE is &.
0RQUOTE     Specifies the repeat quote  character  used  for  prefixing  repeated
            characters.  Value must be between 33-62 or 96-126 decimal indicating
            the ASCII character.  The actual character  may  also  be  specified,
            optionally in quotes.  The default for RQUOTE is ~.
0SOH        Sets  the  start-of-header  character  sent  at  the  start  of  each
            transmitted packet and expected at the start of each received packet.
            May be specified as decimal value of ASCII code (0-31), ASCII control
            character  name  (e.g.,  SOH), or in control key notation (e.g., XA).
            The default for SOH is 1, (SOH, XA).
0SEOL       Sets the end-of-line control  character  sent  at  the  end  of  each
            transmitted  packet.  May be specified as decimal value of ASCII code
            (0-31), ASCII control character name (e.g., CR), or  in  control  key
            notation (e.g., XM).  The default for SEOL is 13, (CR, XM).
0REOL       Sets the end-of-line control character expected at the  end  of  each
            received  packet.   May  be  specified as decimal value of ASCII code
            (0-31), ASCII control character name (e.g., CR), or  in  control  key
            notation (default XM).  The default for REOL is 13, (CR, XM).
0DEBUG      ON dumps all received and sent packets plus all data  set  I/O  to  a
            RECFM=VB  data  set.   The  user must allocate the DD name DEBUG to a
            sequential data set (e.g., TSO ALLOC  F(DEBUG)  DA(DEBUG.DATA)  NEW).
            OFF  closes  the  debug  data  set  (if open) and turns off debugging
            information.  The default for DEBUG is OFF.
0SET parameters may be abbreviated as follows:  BLOCK  (BLK);  NOPREFIX  (NOPRE);
 NUMBERED (NUMD); PREFIX (PRE); SPACE (SP); VOLUME (VOL)
-
-
-
-
-
-
-                                                         Section 6 -- TSO Kermit
1104                                                 Kermit File Transfer Package
-
 6.4.5.  Program Management Commands
0HELP     Displays a message that tells how to get  explanations  of  TSO  Kermit
          commands.
0?        Lists all legal TSO Kermit commands, along with brief descriptions.
0EXIT     Terminates TSO Kermit.
0QUIT     Same as EXIT.
0END      Same as EXIT.
0TSO <TSO command>
0         Executes the TSO command.
0EXEC <data set name>
0         Executes Kermit commands in a TSO CLIST data set.  The  data  set  must
          have  line  numbers  (columns  73/80  for  RECFM=FB,  columns  1/8  for
          RECFM=VB).
0KERMIT   Used in CLISTs, processes TSO Kermit SET commands.  Any TSO Kermit  SET
          command  in  an  EXEC  file  must  be prefixed by KERMIT.  SET commands
          without the KERMIT prefix will be interpreted as TSO SET commands.
0STATUS   Returns the status of the previous execution of KERMIT-TSO.  Therefore,
          STATUS will either display the message "Kermit completed successfully,"
          or the last error encountered prior  to  aborting.   STATUS  will  also
          display warning messages.
-
-
-
-
-
-
-
-
 TSO Kermit -- Section 6
1Kermit File Transfer Package                                                 105
-
 6.5.  TSO Kermit Examples
0Here is a brief example  of  how  to  use  the  IBM  PC  and  MS-DOS  Kermit  in
 conjunction  with  TSO  Kermit to send a file to the IBM PC.  This example shows
 how to use TSO Kermit to transfer a text file.
-A>kermit                      Run Kermit on the micro
+  ______
0Kermit-MS> do tso             Set up standard TSO settings
+           ______
 Kermit-MS>connect             Connect to communication port
+          _______
 ___________                   Dial the NIH TSO service (assumes Hayes compatible
+ATDT4922223
+___________
                               modem).  Local Echo may cause double characters to
                               be displayed depending upon modem settings.
 CONNECT
0   [The microcomputer will act as a regular terminal from now on.]
    [Logon here as you normally would, and run TSO Kermit.]
0logon                         Initiate logon sequence
+_____
 INITIALS? iii
+          ___
 ACCOUNT? aaaa
+         ____
 KEYWORD? kkk
+         ___
 TERMINAL? none
+          ____
 BOX? bbb
+     ___
 AAAAIII LOGON IN PROGRESS AT 11:58:55 ON MAY 15, 1986
  NIH/DCRT/CCB TSO
 TSO LINE 118
 READY
 kermit                        Invoke  TSO  Kermit  (also   executes  the   CLIST
+______
                               KERMIT.PROFILE.CLIST if you have created it)
0NIH TSO KERMIT VERSION 1.0
 KERMIT-TSO> set volume file39 Set default volume for data sets
+            _________________
-KERMIT-TSO> show              Display data and protocol settings
+            ____
0Data Set Attributes                     Protocol Attributes
 DATA: Text                              DELAY (after SEND): 20 seconds
 EDIT (WYLBUR edit format data set): on  TIMER (Timeout interval): on (8 seconds)
 NUMBERED (line nos.): off               BLOCK (Block check type): 3 (CRC)
 TABS: off                               PACKET (Receive packet size): 94
 RECFM (Record format): VB               CQUOTE (Control quote character): #
 LRECL (Logical record length): 504      BQUOTE (Binary quote character): &
 BLKSIZE (Block size): 6356              RQUOTE (Repeat quote character): ~
 SPACE (Space allocation): 5 tracks      SOH (Start of Header): 1 (SOH,XA)
 VOLUME: FILE39                          SEOL (Send End-of-line): 13 (CR,XM)
 PREFIX: No prefix                       REOL (Receive End-of-line): 13 (CR,XM)
                                         DEBUG: off
-
-                                                         Section 6 -- TSO Kermit
1106                                                 Kermit File Transfer Package
-
 KERMIT-TSO> ?                 Display list of commands available
+            _
0Legal commands are
0RECEIVE uploads a data set (file) from the microcomputer to the mainframe
    SEND downloads a data set (file) from the mainframe to the microcomputer
    STOP aborts a file transfer in progress (valid only during file transfer)
  STATUS displays the status of the last file transfer
  SERVER invokes TSO Kermit as a slave server
     END terminates TSO Kermit and returns user to TSO
    QUIT and EXIT are synonyms of END
     SET changes KERMIT protocol and data set options
    SHOW displays the current KERMIT option settings
   RESET reinitializes KERMIT to default settings
     TSO issues a command to TSO
    EXEC reads a data set of TSO Kermit commands (a TSO CLIST)
  KERMIT allows TSO Kermit EXEC files to process the TSO Kermit SET commands
           (must prefix each SET cmd)
0KERMIT-TSO> tso listc         List cataloged data sets
+            _________
0IN CATALOG:SYSCTLG.VNIHCT2
 AAAAIII.@WYLBUR.MAIL
 AAAAIII.@WYLBUR.TSO.RECOVERY
 AAAAIII.KERM.CON
 AAAAIII.KERM.LOG
 AAAAIII.KERMIT.INI
 AAAAIII.KERMIT.PROFILE.CLIST
 AAAAIII.MSKERMIT.INI
 AAAAIII.RCVBIN.CLIST
0KERMIT-TSO> server            Enter server mode
+            ______
0 Now entering SERVER mode - type FINISH or LOGOUT on micro to halt SERVER
0Now we must issue commands to KERMIT on the microcomputer (this example  assumes
 an  IBM  PC),  without  breaking  the  connection with TSO Kermit running on the
 mainframe.  We do this by issuing the escape sequence:
0___
+X]C
0The notation above means:  press and hold the Control (Ctrl) key, then press the
 right bracket, release both keys and press the 'C' key.
0Kermit-MS>get kermit.ini      Tell TSO Kermit to transfer the file KERMIT.INI
+          ______________
0    [the file is received -- MS-DOS Kermit displays status]
0Kermit-MS>finish              Terminate server mode on TSO Kermit
+          ______
0Kermit-MS>connect             Go back to TSO Kermit prompt
+          _______
-
0TSO Kermit -- Section 6
1Kermit File Transfer Package                                                 107
-
     [press carriage return to see TSO Kermit's prompt]
0KERMIT-TSO> status            Check status of completed transfer
+            ______
0                        TSO Kermit Status Report
 TSO KERMIT completed successfully
0KERMIT-TSO> end               Terminate TSO Kermit, return to TSO
+            ___
 READY
 logoff                        Logoff from TSO
+______
 CHARGE =       $.51
 TOTAL CPU TIME = 0.31 SECONDS (MODEL 3090  )
 VECTOR CPU TIME =      0.00 SECONDS
 ELAPSED TIME = 00:02:39
 I/O COUNT = 7
 REGION = 336K
 AAAAIII LOGGED OFF TSO AT 12:01:38 ON MAY 15, 1986
0X]C                           Return to the micro
+___
0Kermit-MS>quit                Terminate Kermit on the micro
+          ____
 A>
-
-
-
-
-
-
-
-
-
-
-
                                                          Section 6 -- TSO Kermit
1108                                                 Kermit File Transfer Package
-
 In order to send a file from the IBM  PC  to  TSO  repeat  the  above  procedure
 swapping  the  command  SEND  with  GET.  This is shown for a binary file in the
 example which follows.  (This example assumes the user has logged on to TSO  and
 issued the KERMIT command.)
0KERMIT-TSO> set data binary   Set up TSO Kermit for binary data
+            _______________
0KERMIT-TSO> server            Enter server mode
+            ______
0 Now entering SERVER mode - type FINISH or LOGOUT on micro to halt SERVER
0X]C                           Return to the micro
+___
0Kermit-MS>send tree.com       Microcomputer sends the file TREE.COM
+          _____________
0    [the file is sent .......]
0Kermit-MS>finish              Terminate server mode on TSO Kermit
+          ______
0Kermit-MS>connect             Go back to TSO Kermit prompt
+          _______
0    [press carriage return to see TSO Kermit's prompt]
0KERMIT-TSO> status            Check status of completed transfer
+            ______
0                        TSO Kermit Status Report
 TSO KERMIT completed successfully
0KERMIT-TSO> end               Terminate TSO Kermit, return to TSO
+            ___
 READY
 logoff                        Logoff from TSO
+______
 CHARGE =       $.51
 TOTAL CPU TIME = 0.31 SECONDS (MODEL 3090  )
 VECTOR CPU TIME =      0.00 SECONDS
 ELAPSED TIME = 00:02:39
 I/O COUNT = 7
 REGION = 336K
 AAAAIII LOGGED OFF TSO AT 12:01:38 ON MAY 15, 1986
0X]C                           Return to the micro
+___
0Kermit-MS>quit                Terminate Kermit on the micro
+          ____
 A>
-
-
-
-
 TSO Kermit -- Section 6
1Kermit File Transfer Package                                                 109
-
 6.6.  Additional Information
0The commands are supplied with a help option, so a question mark can be typed to
 get  the  appropriate  format or a list of options.  The question mark, however,
 must be followed by a carriage return; TSO Kermit will respond and  display  the
 prompt  again.   For  instance,  SET  ?  will list all valid options for the SET
 command.
0If the microcomputer Kermit does not send an error packet when  it  aborts,  TSO
 Kermit  does  not  know  the  microcomputer  has stopped sending it information.
 Therefore, when you connect back to the IBM, TSO Kermit  may  still  be  sending
 packets (they will appear on the screen).  The user must enter STOP to terminate
 the sending of packets.
0When the DATA parameter is set to TEXT, and TSO Kermit receives a text file that
 has characters with the eighth bit on, it ignores the eighth bit.  When the DATA
 parameter is set to BINARY, and TSO Kermit receives a binary  file,  the  eighth
 bit is preserved.
-6.7.  Error Messages
0TSO Kermit supplies the microcomputer and the user with numerous error messages.
 If  file  transfer must be aborted, an error packet is sent to the microcomputer
 before TSO Kermit stops.  The same message  can  be  retrieved  via  the  STATUS
 command  when TSO Kermit returns and displays the prompt.  If TSO Kermit aborted
 because the maximum amount of retries was exceeded (20) the error  message  will
 display  "Retry  Count  Exceeded."  If execution stops because the microcomputer
 aborted, the error message  will  convey  that  to  the  user,  but  it  is  the
 microcomputer's responsibility to pinpoint the error.
-
-
-
-
-
-
-
-
0                                                         Section 6 -- TSO Kermit
1110                                                 Kermit File Transfer Package
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0TSO Kermit -- Section 6
1Kermit File Transfer Package                                                 111
-
 7.  MS-DOS Kermit for the IBM-PC
0Program:        Daphne Tzoar and  Jeff  Damens  (Columbia  University),  Joe  R.
                 Doupnik  (Utah  State  University), James Harvey (Indiana/Purdue
                 University), contributions by many others.
 Language:       Microsoft Macro Assembler (MASM)
 Documentation:  Frank da Cruz and Christine Gianone (Columbia University)
 Version:        2.29
 Date:           May 26, 1986
-Kermit-MS Capabilities At A Glance:
0  Local operation:                   Yes
   Remote operation:                  Yes
   Transfers text files:              Yes
   Transfers binary files:            Yes
   Wildcard send:                     Yes
   XX/XY interruption:                Yes
   Filename collision avoidance:      Yes
   Can time out:                      Yes
   8th-bit prefixing:                 Yes
   Repeat count prefixing:            Yes
   Alternate block checks:            Yes
   Terminal emulation:                Yes
   Communication settings:            Yes
   Transmit BREAK:                    Yes
   IBM mainframe communication:       Yes
   Transaction logging:               No
   Session logging:                   Yes
   Raw transmit:                      No
   Act as server:                     Yes
   Talk to server:                    Yes
   Advanced server functions:         No
   Advanced commands for servers:     Yes
   Local file management:             Yes
   Command/init files:                Yes
   Command macros:                    Yes
   Attribute packets:                 No
   Extended-length packets:           No
   Sliding windows:                   No
0Kermit-MS is a program that implements the Kermit file transfer protocol for the
 IBM  PC family, IBM compatibles, and several other machines using the Intel 8086
 processor series (8088, 80286, etc.) and  operating  system  family  (PC-DOS  or
 MS-DOS,  henceforth  referred to collectively as MS-DOS or simply DOS).  The NIH
 Computer Center supports only the IBM PC version of Kermit-MS.
-
-
-                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1112                                                 Kermit File Transfer Package
-
 Kermit-MS  version  2.29  runs  in  as  little  as  60K  of  memory  (about  55K
 contiguous),  but  will  occupy up to 100K, if it can be found, for extra screen
 rollback memory.  It will also try to leave 24 Kbytes free for a second copy  of
 COMMAND.COM  which  is  needed  for  the SPACE command and others.  Versions not
 using screen rollback memory will not require the additional space.
0On the IBM PC, Kermit-MS 2.29 performs almost  complete  emulation  of  the  DEC
 VT-102  terminal  at speeds up to 19,200 bps (lacking only smooth scrolling, 132
 column mode, and ANSI printer control).  Much of the speed is  accomplished  via
 direct  writes to screen memory, but this is done in a "TopView" aware manner to
 allow successful operation in windowing environments like  TopView,  MS-Windows,
 and DesqView.  Speed is also due to direct access of the serial port UART (8250)
 chip, with buffered,  interrupt-driven  receipt  of  characters  and  selectable
 XON/XOFF  flow  control.   Full-speed  9600 bps operation is possible on 4.77Mhz
 systems without flow control, but flow control is required on these systems  for
 19,200 bps or higher rates.
0Kermit-MS 2.29 is capable of sending a break signal that is required  by  WYLBUR
 and  TSO.   This  can  be  accomplished  by  using  Ctrl-Break while in terminal
 emulation mode.
0As of version 2.28, MS-DOS Kermit requires version 2.0 or later of  DOS.   Older
 versions  of  MS-DOS  Kermit  are no longer distributed, but if you have version
 2.27 or earlier, it can run under version 1.0 or 1.1 of MS-DOS.
0Kermit-MS 2.29 runs on a wide variety of MS-DOS systems,  including  the  entire
 IBM  PC  family  (the  PC,  XT,  AT, PCjr, Portable PC, PC Convertible) and many
 compatibles.
0This document will describe the things you should know  about  the  MS-DOS  file
 system  in  order to make effective use of Kermit, and then it will describe the
 Kermit-MS program itself.  It is assumed  you  are  already  familiar  with  the
 general  ideas  of  Kermit  file transfer.  If you are not, consult Section 1 of
 this manual, or Kermit, A File Transfer Protocol,  by  Frank  da  Cruz,  Digital
 Press (1986).
0Note:  About the notation used in this section:  user  input  is  underlined  to
+                                                                  __________
        distinguish it from computer output.  When the "control" key is needed in
        conjunction with another key to generate a character, it  is  represented
        in  one  of these equivalent ways:  Control-Z, Ctrl-Z, and XZ all mean to
        depress and hold the "control" key, press the "Z" key, then release  both
        keys.
-
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 113
-
 7.1.  The MS-DOS File System
0The features of the MS-DOS file system of greatest interest to Kermit users  are
 the form of the file specifications, and the formats of the files themselves.
-
 7.1.1.  File Specifications
0MS-DOS file specifications (in version 2.0 or later of DOS) are of the form
0    DEVICE:\PATHNAME\NAME.TYPE
0where the DEVICE is a single character identifier (for instance, A for the first
 floppy disk, C for the first fixed disk, D for a RAM disk emulator), PATHNAME is
 up to 63 characters of identifier(s) (up to 8  characters  each)  surrounded  by
 reverse  slashes,  NAME  is  an identifier of up to 8 characters, and TYPE is an
 identifier of up to 3 characters in length.  Device and pathname may be omitted.
 The first backslash in the pathname is omitted if the specified path is relative
 to the current directory.  In the path field, "."  means the current  directory,
 ".."  means the parent directory.
0Pathname is normally omitted, but can be specified in all Kermit-MS commands (as
 of  version  2.29).   Device  and  directory pathnames, when omitted, default to
 either the user's current disk and directory, or to the current directory search
 path as specified in the DOS PATH environment variable, depending on the context
 in which the file name appears.
0    When this document says that a file is searched for "in the current
     path," it means that the PATH is searched first, and if the file is not
     found, then Kermit-MS looks on the current disk and directory.  If the
     PATH environment variable is empty, Kermit looks only at the current
     disk and directory.
0NAME.TYPE is normally sufficient to specify a file, and only this information is
 sent along by Kermit-MS with an outgoing file.
0The device, path, name, and type fields may contain uppercase  letters,  digits,
 and  the special characters "-" (dash), "_" (underscore), and "$" (dollar sign).
 When you type lowercase letters in filenames, they are  converted  automatically
 to  uppercase.   There are no imbedded or trailing spaces.  Other characters may
 not  be  included;  there  is  no  mechanism  for  "quoting"  otherwise  illegal
 characters  in filenames.  The fields of the file specification are set off from
 one another by the punctuation indicated above.
0The name field is the primary identifier for the file.  The  type,  also  called
 the  extension  or suffix, is an indicator which, by convention, tells what kind
 of file we have.  For instance FOO.BAS is the source of a  BASIC  program  named
 FOO;  FOO.OBJ  might  be  the  relocatable  object  module produced by compiling
 FOO.BAS; FOO.EXE could be an executable program produced by linking FOO.OBJ, and
 so forth.  .EXE and .COM are the normal suffixes for executable programs.
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1114                                                 Kermit File Transfer Package
-
 MS-DOS allows a group of files to be specified in a single file specification by
 including  the  special  "wildcard"  characters, "*" and "?."  A "*" matches any
 string of characters from  the  current  position  to  the  end  of  the  field,
 including no characters at all; a "?"  matches any single character.
0Here are some examples:
0  *.BAS   All files of  type  BAS  (all  BASIC  source  files)  in  the  current
           directory.
0  FOO.*   Files of all types with name FOO.
0  F*.*    All files whose names start with F.
0  F?X*.*  All files whose names  start  with  F  and  contain  X  in  the  third
           position, followed by zero or more characters.
0  ?.*     All files whose names are exactly one character long.
0Wildcard notation is used on many computer systems in similar ways,  and  it  is
 the mechanism most commonly used to instruct Kermit to send a group of files.
0    Note:  Kermit-MS uses the "?"  character for help while commands  are  being
            typed,  so the single-character wildcard in the first position of the
            file name in Kermit-MS commands is "#" rather than "?".  For example
0           Kermit-MS>send ________
+                     _____#b??ef.*
0           would send files such as abcdef.for and xbyzef.bas.
0Kermit-MS users should bear in mind that  other  (non-MS-DOS)  systems  may  use
 different  wildcard characters.  For instance the DEC-10 Kermit uses "%" instead
 of "?"  as the single character wildcard; when  using  Kermit-MS  to  request  a
 wildcard  file  group from a Kermit-10 server, the Kermit-MS "?"  or "#" must be
 replaced by the DEC-10 "%".
-
-
-
-
-
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 115
-
 7.1.2.  File Formats
0MS-DOS systems  store  files  as  bulk  collections  of  8-bit  bytes,  with  no
 particular differences between text, program code, and binary files.  ASCII text
 files consist of lines separated by carriage-return-linefeed sequences  (CRLFs),
 which   conforms  exactly  to  the  way  Kermit  represents  text  files  during
 transmission.   Since  a  non-MS-DOS  receiving  system  might  need   to   make
 distinctions  as  to file type, you may need to use various SET functions on the
 remote system to inform  it  that  the  incoming  file  is  of  some  particular
 (non-default)  type,  such  as  binary.  In transmitting files between Kermit-MS
 programs, regardless of file contents, the receiving MS-DOS  system  is  equally
 capable of processing text, code, and data, and in fact requires no knowledge of
 how the bytes in the file are to be used.  Unlike most  other  Kermit  programs,
 MS-DOS  Kermit  does  not  require a command like SET FILE TYPE BINARY to switch
 from text to binary file transfer.
0MS-DOS (unlike CP/M) is capable of pinpointing the end of file with precision by
 keeping  a  byte  count  in  the  directory,  so  one would expect no particular
 confusion in this regard.  However, most MS-DOS programs  continue  to  use  the
 CP/M convention of terminating a text file with a Control-Z character, and won't
 operate correctly unless this terminating byte is present.  Therefore, Kermit-MS
 users should be aware of a special SET EOF option for both incoming and outbound
 files, described later.
0Non-MS-DOS systems  may  well  be  confused  by  nonstandard  ASCII  files  from
 Kermit-MS:
0   - Files containing any of the 8-bit "extended ASCII" characters will probably
      need conversion (or translation) to 7-bit ASCII.
0   - Files produced by word processing programs like Easywriter or WordStar  may
      contain  special  binary  formatting  codes,  and  could need conversion to
      conventional 7-bit ASCII  format  prior  to  transmission,  using  commonly
      available "exporter" programs.
0   - Files created by word processors that store formatting data at the  end  of
      the  file, after the Control-Z and before physical end, may require special
      processing via SET EOF to strip the  formatting  data,  lest  they  confuse
      non-MS-DOS recipients.
0   - Spreadsheet or  database  files  usually  need  special  formatting  to  be
      meaningful to non-MS-DOS recipients (though they can be transmitted between
      MS-DOS systems with Kermit-MS).
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1116                                                 Kermit File Transfer Package
-
 7.2.  Program Operation
0Kermit-MS can be run interactively, from a batch file, or as an  "external"  DOS
 command.   Commands  consist of one or more fields, separated by "whitespace" --
 one or more spaces or tabs.
0Upon initial startup, the program  executes  any  commands  found  in  the  file
 MSKERMIT.INI  in the current path.  This initialization file may contain command
 macro definitions, communications settings for one or more ports, or  any  other
 Kermit-MS commands.  Here is a sample MSKERMIT.INI file:
0def wyl set parity even,set local echo on,set speed 1200
 def dec set parity none,set local echo off, set speed 1200
 def tso set parity even,set local echo on,set speed 1200
 do wyl
 connect
0Note that the above MSKERMIT.INI file executes the  WYL  macro  and  issues  the
 connect  command  for  the  user.  This is useful if you normally access WYLBUR.
 If, however you want to use TSO Kermit or DECsystem-10 Kermit,  the  appropriate
 macro to execute would be the TSO or DEC macro.
0The NIH Computer Center supplies a standard MSKERMIT.INI file on  the  Kermit-MS
 diskette distributed by the Technical Information Office.  This file defines the
 macros WYLBUR, DEC10, TSO, and 3270 to allow  easy  access  to  Computer  Center
 services.   If  you  only  use one of the services (e.g., TSO), you can have the
 initialization file automatically invoke  the  service  and  issue  the  CONNECT
 command by adding two lines to the end of the MSKERMIT.INI file:
0    DO TSO
     CONNECT
0To work with  your  configuration,  the  NIH-supplied  macros  may  need  to  be
 modified.   In these macros as distributed, SPEED is set to 2400 and PORT is set
 to 1.  If you have a 1200 bps modem, SPEED should be changed  to  1200,  and  if
 your  modem is connected through the COM2 serial port, PORT should be changed to
 2.
0Macros are described in detail in section 7.3.8.
-
-
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 117
-
 Interactive Operation:
0To run Kermit-MS interactively, invoke the program from  DOS  command  level  by
 typing its name.  When you see the command's prompt,
0  Kermit-MS>
0you may type Kermit commands repeatedly until you are ready to exit the program,
 for example:
0  A>
   A>kermit
+    ______
0  IBM PC Kermit-MS V2.29
   Type ? for help
0  Kermit-MS>send foo.*
+            __________
0    informational messages about the files being sent
0  Kermit-MS>get bar.*
+            _________
0    informational messages about the files being received
0  Kermit-MS>exit
+            ____
   A>
0During interactive operation, you may edit the command you're  currently  typing
 using BACKSPACE to erase the character most recently typed, Ctrl-W to delete the
 most recent field,  or  Ctrl-U  to  delete  the  entire  command.   The  editing
 characters  may  be used in any combination until the command is finally entered
 by typing ENTER (Carriage Return) or Ctrl-L.
0While typing commands, you may use the help ("?") and keyword  completion  (ESC)
 features  freely.   A  question  mark  typed  at  almost  any point in a command
 produces a brief description of what is expected or possible at that point  (for
 this  reason  Kermit-MS  uses "#" for the single-character match wildcard in the
 first position of the local filenames and "?"  thereafter,  and  ?-help  is  not
 available  from  within  a filename).  ESC typed at any point, except in a local
 filename, will cause the current field to be filled out if what you  have  typed
 so  far is sufficient to identify it, and will leave you in position to type the
 next field (or to type a "?"  to find out what the next  field  is);  otherwise,
 the program will beep at you and wait for you to type further characters.
0Some Kermit-MS commands, like GET, SHOW KEY, SET KEY, may prompt for  additional
 information  on  subsequent lines.  If you have reached one of these prompts and
 then wish to cancel the command, you may type Ctrl-C.
-
-
-                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1118                                                 Kermit File Transfer Package
-
 Summary of Kermit-MS Command Characters:
0  SPACE         Separates fields within the command.
0  TAB           Same as Space, and echoes as Space.  You may also use Ctrl-I for
                 Tab.
0  BACKSPACE     Deletes  the  character  most  recently  typed.   May  be  typed
                 repeatedly  to  delete  all the way back to the prompt.  You may
                 also use DELETE, RUBOUT, Ctrl-H, or equivalent keys.
0  Ctrl-W        Deletes the most recent "word", or field, on the  command  line.
                 May be typed repeatedly.
0  Ctrl-U        Deletes the entire command line, back to the prompt.
0  Ctrl-C        Cancels the current command  and  returns  to  the  "Kermit-MS>"
                 prompt.
0  ESC           If enough characters have been supplied in the  current  keyword
                 to  identify it uniquely, supply the remainder of the field, and
                 position to the next field of the command.  Otherwise,  sound  a
                 beep.  ESC does not provide filename completion in version 2.29.
0  ?             Displays a brief message describing what may  be  typed  in  the
                 current  command  field.   Also, wildcard character for matching
                 any single  character  in  all  but  the  first  position  of  a
                 filename.
0  #             Wildcard character for matching single characters in  filenames.
                 Equivalent  to  MS-DOS  "?", but used in the first position of a
                 filename only, so that "?"  may be  used  to  get  help  at  the
                 beginning of a filename field.
0  RETURN        Enters the command.  On most keyboards, you may also  use  ENTER
                 or Ctrl-M.
0  Ctrl-L        Clears the screen and enters the command.
0  Ctrl-Break    Equivalent to Ctrl-C.
0Liberal use of "?"  allows you to feel your way through the commands  and  their
 fields.   This  feature  is  sometimes called "menu on demand" -- unlike systems
 that force you to negotiate menus at every turn,  menu-on-demand  provides  help
 only when it is needed.
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 119
-
 Command Line Invocation:
0Kermit-MS may also be invoked with  command  line  arguments  from  DOS  command
 level, for instance:
0  A>kermit send foo.bar
+    ___________________
0or
0  A>kermit set port 1, set baud 1200, connect
+    _________________________________________
0In this case, help and recognition are not available (because the program  won't
 start  running until after you type the entire command line), and Kermit-MS will
 exit back to DOS after completing the specified command or commands.  Therefore,
 when invoked with command line arguments, Kermit-MS will behave as if it were an
 external DOS command, like MODE.  Note that several commands may be given on the
 command line, separated by commas.
-Batch Operation:
0Like other MS-DOS programs, Kermit-MS may be operated under batch  with  command
 line  arguments.   If  you invoke it without command line arguments, it will run
 interactively, reading commands from the keyboard and not the batch file.   When
 it exits, batch processing will continue to the end of the batch file.
-Remote Operation:
0The MS-DOS CTTY command allows a MS-DOS  system  to  be  used  from  a  terminal
 connected to its communication port.  Such sessions must be conducted with great
 care, since many programs assume that they are running on the real console,  and
 explicitly  reference  screen memory or keyboard scan codes.  Kermit can be used
 in this manner too, but before you give it any file transfer commands, you  must
 inform  it  that  it  is  running in "remote mode" rather than its normal "local
 mode."  Use the SET REMOTE ON command for this  purpose,  to  prevent  the  file
 transfer display from being sent out the port.
-
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1120                                                 Kermit File Transfer Package
-
 7.3.  Kermit-MS Commands
0MS-DOS Kermit implements a large subset  of  the  commands  of  "ideal"  Kermit.
 Here's a brief summary:
0          BYE  to remote server.
         CLEAR  key redefinitions.
         CLOSE  log file and stop logging remote session.
       COMMENT  a command file.
       CONNECT  as terminal to remote system.
           CWD  change local working directory.
        DEFINE  macros of Kermit-MS commands.
        DELETE  local files.
     DIRECTORY  listing of local files.
            DO  a macro expansion.
          EXIT  from Kermit-MS.
        FINISH  Shut down remote server.
           GET  files from remote server.
        HANGUP  the phone.
          HELP  about Kermit-MS.
         LOCAL  prefix for local file management commands.
           LOG  remote terminal session.
        LOGOUT  remote server.
          PUSH  to MS-DOS command level.
          QUIT  from Kermit-MS
       RECEIVE  files from remote Kermit.
        REMOTE  prefix for remote file management commands.
           RUN  a MS-DOS program.
          SEND  files to remote Kermit.
        SERVER  mode of remote operation.
           SET  various parameters.
          SHOW  various parameters.
         SPACE  inquiry (about disk space).
        STATUS  inquiry (about settings).
          TAKE  commands from file.
          TYPE  display a local file.
       VERSION  display Kermit-MS program version number.
0In general, commands and their parameters may be  abbreviated  to  the  shortest
 prefix  that  is  unique  (e.g., V for VERSION).  In addition, C can be used for
 CONNECT, and H can be used for HELP.
0The remainder of this section concentrates on the  commands  that  have  special
 form  or  meaning  for  MS-DOS  Kermit.   Not  all of the following commands are
 necessarily available on all MS-DOS systems, and some of the commands  may  work
 somewhat differently between DOS versions.
0The notation used is as follows:  Optional  fields  are  in  [square  brackets],
 lists  of alternatives are in $curly braces.  In dialog examples user typein is
 underlined to distinguish it from computer typeout.
+__________
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 121
-
 7.3.1.  Commands for Terminal Connection
0The CONNECT command connects your PC as a terminal to the remote system, so that
 you can start up Kermit there.
-                              The CONNECT Command
0Syntax:  CONNECT
0The CONNECT command establishes an interactive terminal connection to the system
 connected  to  the  currently  selected communications port (e.g., COM1 or COM2)
 using full duplex (remote) echoing and no parity unless otherwise  specified  in
 previous SET commands.  You can type the escape character followed by the letter
 C to get back to Kermit-MS.  The escape character is Ctrl-] by default.
0You can use the SET ESCAPE command to define a different escape  character,  SET
 SPEED (or BAUD) to change the speed, and SET PORT to switch between ports.  Read
 about the SET COMMAND in section 7.3.6 for more information on these  and  other
 settings.
0Terminal emulation is described in greater detail in section 7.4 below.
-                               The HANGUP Command
0Syntax:  HANGUP
0HANGUP command attempts to lower the modem signals DTR and RTS.  It may be  used
 to  hang up the phone when dialed up through a modem, or to get the attention of
 port contention units or terminal concentrators that operate in this manner.
-
-
-
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1122                                                 Kermit File Transfer Package
-
 7.3.2.  Commands for File Transfer
0The file transfer commands are SEND, GET, and RECEIVE.
-                                The SEND Command
0Syntax:  SEND filespec1 [filespec2]
0The SEND command causes a file or file group to be sent from  the  local  MS-DOS
 system  to the Kermit on the remote system.  The remote Kermit may be running in
 either server or interactive mode; in the latter case, you should  already  have
 given it a RECEIVE command and escaped back to your PC.
0filespec1 may contain  the  wildcard  characters  "*"  to  match  zero  or  more
 characters  within  a  field, and/or "#" (first position) or "?"  (elsewhere) to
 match any single character.  If filespec1 contains wildcard characters then  all
 matching  files will be sent, in the same order that MS-DOS would show them in a
 directory listing.  If  filespec1  specifies  a  single  file,  you  may  direct
 Kermit-MS  to  send  that  file  with a different name, given in filespec2.  For
 instance, in the command
0  Kermit-MS>send foo.bar framus.widget
+            __________________________
0filespec2 begins with the first nonblank character after filespec1 and ends with
 the carriage return; thus it may contain blanks or other unusual characters that
 may be appropriate on the target  machine.   The  alphabetic  case  of  text  in
 filespec2 is preserved in transmission.
0If the SEND command is specified by itself on the command line, then you will be
 prompted  separately  for  the name of the file to send, and the name to send it
 under:
0    Kermit-MS>send
+              ____
      Local Source File: c:\chris\xcom1.txt
+                        __________________
      Remote Destination File: com1.txt
+                              ________
0If a file can't be opened for read access, standard MS-DOS  recovery  procedures
 will take place.  For example:
0    Not ready error reading drive A
     Abort, Retry, Ignore?
0If you select "Abort," you will be returned to DOS.
0Files will be sent  with  their  MS-DOS  filename  and  filetype  (for  instance
 FOO.TXT,  no  device  or pathname).  If there is no filetype, then only the name
 will be sent, without the terminating dot.  Each file is sent  as  is,  with  no
 conversions  done  on  the  data,  except  for  possibly  adding  or  deleting a
 terminating Control-Z character (see the SET EOF command).
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 123
-
 Once you give Kermit-MS the  SEND  command,  the  name  of  each  file  will  be
 displayed on your screen as the transfer begins; packet, retry, and other counts
 will be displayed along with informational messages during the transfer.  If the
 file  is successfully transferred, you will see "Complete," otherwise there will
 be an error message.  When the specified operation is  done,  the  program  will
 sound a beep.
0Several single-character commands may be given  while  a  file  transfer  is  in
 progress:
0  XX  (Control-X) Stop sending the current file and go on to the  next  one,  if
       any.
0  XZ  Stop sending this file, and don't send any further files.
0  XC  Return to Kermit-MS command level immediately without sending any kind  of
       notification to the remote system.
0  XE  Like XC, but send an Error packet to the remote Kermit in  an  attempt  to
       bring it back to server or interactive command level.
0  CR  Simulate a timeout:  resend the current packet, or NAK the expected one.
0Control-X, Control-Z, and Control-E send the proper  protocol  messages  to  the
 remote Kermit to bring it gracefully to the desired state.  Control-C leaves the
 remote Kermit in whatever state it happens to be in, possibly retransmitting its
 last  packet  over and over, up to its retry limit.  You should only have to use
 Control-C in dire emergencies (the remote Kermit is  stuck,  the  remote  system
 crashed,  etc),  or  at  those times when you realize that you have given a file
 transfer command to Kermit-MS without first having told the remote Kermit  about
 it.
-
-
-
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1124                                                 Kermit File Transfer Package
-
                                 The GET Command
0Syntax:  GET remote-filespec
0The GET command requests a remote Kermit server to send the file or  file  group
 specified  by remote-filespec.  This command can be used only when Kermit-MS has
 a Kermit server active on the other end of the connection.  This means that  you
 must have CONNECTed to the other system, logged in, run Kermit there, issued the
 SERVER command, and escaped back (e.g., X]C) to the  local  Kermit-MS.   If  the
 remote  Kermit  does  not  have  a  SERVER command, then you should use SEND and
 RECEIVE as described below.
0You may use the GET command in a special way to specify  a  different  name  for
 storing  the  incoming  file.   Just  type  GET alone on a line, and you will be
 prompted separately for the remote filespec and the local filespec:
0  Kermit-MS>get
+            ___
    Remote Source File: com1.txt
+                       ________
    Local Destination File: xcom1.txt
+                           _________
0The local file name may contain a device designator, and/or  a  directory  path.
 If  more  than  one  file  arrives,  only the first will be renamed.  The device
 designator and directory path are described as follows:
0  Device designator
0      Store the file on the designated  device.   If  no  device  designator  is
       given, store it on the current default device.
0  Directory path
0      Store the file in the designated directory.  If no path given,  store  the
       file in the current directory.
0The remote filespec is any string that can be a legal file specification for the
 remote  system;  it is not parsed or validated locally.  It can contain whatever
 wildcard or file-group notation is valid on the remote system.  As files arrive,
 their  names  will  be  displayed  on  your  screen,  along  with packet traffic
 statistics and status messages.
0The same single-character commands are available as during SEND:
0  XX  Request that the remote Kermit stop sending the current file, and  proceed
       to  the  next  one  immediately.  Since this is an optional feature of the
       Kermit protocol, the remote Kermit might not honor the request.
0  XZ  Request that the remote Kermit terminate the entire transfer; this is also
       an optional feature that may or may not be supported by the remote Kermit.
0  XC, XE, and CR operate in the same way as they do during SEND.  In this  case,
       XE should always do what XZ is supposed to do.
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 125
-
                               The RECEIVE Command
0Syntax:  RECEIVE [filespec]
0The RECEIVE command tells Kermit-MS to receive a file or  file  group  from  the
 other system.  Kermit-MS passively waits for the file to arrive; this command is
 not to be used when talking to a Kermit server.  (Use GET for that).  You should
 already  have  issued  a  SEND  command to the remote Kermit and escaped back to
 Kermit-MS before issuing the RECEIVE command.
0If the optional filespec is provided, the first incoming  file  will  be  stored
 under  that  name.   The  filespec  may include any combination of the following
 fields:
0  Device designator
0      Store the file on the designated  device.   If  no  device  designator  is
       given, store it on the current default device.
0  Directory path
0      Store the file in the designated directory.  If no path given,  store  the
       file in the current directory.
0  File name
0      Store the file under the name given.  If no name is given, store it  under
       the  name  it  was  sent  under,  converted,  if  necessary,  to  suit DOS
       conventions, and modified, if desired, to avoid overwriting  any  file  of
       the same name in the same directory.
0If the optional filespec was provided, but more than one file arrives, the first
 file  will  be stored under the given filespec, and the remainder will be stored
 under their own names, but on the specified device and directory.
0If an incoming file does not arrive in its  entirety,  Kermit-MS  will  normally
 discard  it  and  it  will  not  appear  in your directory.  You may change this
 behavior by using the command SET INCOMPLETE KEEP, which will cause as  much  of
 the file as arrived to be saved on the disk.
0The same single-character commands are available as during SEND:
0  XX  Request that the remote Kermit stop sending the current file, and  proceed
       to  the  next  one  immediately.  Since this is an optional feature of the
       Kermit protocol, the remote Kermit might not honor the request.
0  XZ  Request that the remote Kermit terminate the entire transfer; this is also
       an optional feature that may or may not be supported by the remote Kermit.
0  XC, XE, and CR operate in the same way as they do during SEND.  In this  case,
       XE should always do what XZ is supposed to do.
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1126                                                 Kermit File Transfer Package
-
 If the incoming file has the same name  as  a  file  that  already  exists,  and
 WARNING  is  set ON, Kermit-MS will change the incoming name (and inform you how
 it renamed it) so as not to obliterate the pre-existing  file.   If  WARNING  is
 OFF,  the  original  file will be overwritten; if you type XX or XZ to interrupt
 the transfer, you'll either get a partial new file, or else both the old and the
 new  file  of that name will be lost, depending on SET INCOMPLETE.  In any case,
 when WARNING is off, files with  the  same  name  as  incoming  files  will  not
 survive.
0Caution:  If an incoming file's name (the part before the dot) corresponds to an
 MS-DOS device name, such as NUL, COM1, CON, AUX, LPT1, or PRN, output will go to
 that device, rather than to a file with that name.  This is a feature of MS-DOS.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 127
-
 7.3.3.  Commands Controlling Remote Kermit Servers
0The BYE, FINISH, and LOGOUT commands allow you to  shut  down  a  remote  Kermit
 server:
0BYE             When communicating with a remote  Kermit  server,  use  the  BYE
                 command  to  shut down the server, log out its session, and exit
                 locally from Kermit-MS to DOS.
0FINISH          Like BYE, FINISH shuts down the remote server.  However,  FINISH
                 does  not  log  out  the  server's  session.   You  are  left at
                 Kermit-MS prompt level so that  you  can  connect  back  to  the
                 session on the remote system.
0LOGOUT          The LOGOUT command is identical to the BYE command,  except  you
                 will  remain at Kermit-MS prompt level, rather than exit to DOS,
                 so that you can establish or use another connection.
0Other functions may be also requested of a server, described  under  the  REMOTE
 command, immediately below.
-
-
-
-
-
-
-
-
-
-
-
-                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1128                                                 Kermit File Transfer Package
-
 7.3.4.  Commands for File Management
0Kermit-MS provides commands for managing both local and remote files.
-                              The REMOTE Commands
0The REMOTE keyword is a prefix for a number of commands.  It indicates that  the
 command  is  to  be  performed  by the remote Kermit, which must be running as a
 server.  Note that not all Kermit servers are capable  of  executing  all  these
 commands,  and  some  Kermit  servers may be able to perform functions for which
 Kermit-MS does not yet have the corresponding commands.   In  case  you  send  a
 command  the server cannot execute, it will send back a message stating that the
 command is unknown to it.  If the remote server can execute the command, it will
 send  the  results to your screen (or whatever device you have specified in your
 most recent SET DESTINATION command).
0Here are the REMOTE commands that Kermit-MS may issue:
0REMOTE CWD [directory]
0        Ask the server to Change your Working Directory on the remote host, that
         is,  the  default  source  and  destination  area  for file transfer and
         management.  You will be prompted for a password, which will not echo as
         you  type  it.   If  you do not supply a password (i.e., you type only a
         carriage return), the  server  will  attempt  to  access  the  specified
         directory  without  a  password.  If you do not supply a directory name,
         your default or login directory on the remote system will be assumed and
         you will not be prompted for a password.
0REMOTE DELETE filespec
0        Ask the server to delete the specified  file  or  files  on  the  remote
         system.   In  response,  the server may display a list of the files that
         were or were not successfully deleted.
0REMOTE DIRECTORY [filespec]
0        Ask the server to display a directory listing of  the  specified  files.
         If no files are specified, then the list should include all files in the
         current working directory.
0REMOTE HELP
0        Ask the server to list the services it provides.
0REMOTE HOST [command]
0        Ask the server to send  the  command  to  the  remote  system's  command
         processor for execution.
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 129
-
 KERMIT command
0        Send the command to the remote Kermit for  interpretation  as  a  Kermit
         command  itself, in the remote Kermit server's own command syntax.  Most
         Kermit servers, including Kermit-MS, do not yet recognize such commands.
0REMOTE SPACE [directory]
0        Ask the server to provide a brief summary of disk usage in the specified
         area  on  the  remote host or, if none specified, the default or current
         area.
0REMOTE TYPE filespec
0        Ask the server to display the contents of the specified remote  file  or
         files on your screen.
-
-
-
-
-
-
-
-
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1130                                                 Kermit File Transfer Package
-
                                The LOCAL Command
0The LOCAL keyword is a prefix for a number of commands.  It indicates  that  the
 specified  command  is  to  be  executed  on the local MS-DOS system.  The LOCAL
 prefix may be omitted.   All  file  specifications  may  include  device  and/or
 directory fields.  The local commands are:
0CWD path
0        Changes the current working directory to the given path.  All references
         to local file names without explicit paths will refer to that path.
0DELETE filespec
0        Deletes the specified file or files.   As  in  DOS,  the  names  of  the
         deleted  files  are  not  listed,  only the message "file(s) deleted" or
         "file(s) not found", and if you give the command "delete *.*", Kermit-MS
         will prompt "Are you sure?", like DOS.
0DIRECTORY [filespec]
0        Lists the names, sizes, and creation dates of files that match the given
         file  specification.  If no filespec is given, the command is equivalent
         to DIR *.*.
0SPACE
0        Performs the MS-DOS CHKDSK function by running the CHKDSK  program  from
         the current path.
0RUN command
0        Passes the command line to COMMAND.COM for execution.  Thus,  any  legal
         DOS  operation  is  permitted:   running  a  program  (with command line
         arguments or i/o redirection), executing a DOS command, or  executing  a
         batch  file.   COMMAND.COM  should  be  in  the current path.  Kermit is
         suspended while  the  command  is  executed  and  automatically  resumes
         afterward.   Yes,  one  may  nest  RUN KERMIT several times if memory is
         available; but that just wastes memory.  If the command is a DOS command
         (like  DIR  or  REN)  it  will  be  executed  directly  by  COMMAND.COM.
         Otherwise, the specified file will be executed, which must be in .EXE or
         .COM  format, or a .BAT file containing DOS commands, from the specified
         path or according to the value of the  PATH  variable  if  no  path  was
         included in the filespec.  Example:
0            Kermit-MS>run more < foo.txt
+                      __________________
-
-
-
 MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 131
-
 TYPE filespec
0        Displays the specified local file on the screen.  Automatic pause is not
         available  at  the  end  of  a  page  (but  see above example for how to
         accomplish this).  Ctrl-S can be used to stop scrolling  and  Ctrl-Q  to
         continue scrolling.
0PUSH
0        Invokes  an  MS-DOS  command   processor   "under"   Kermit-MS,   either
         COMMAND.COM  or  whatever  shell you have specified with COMSPEC in your
         CONFIG.SYS file.  You can return to Kermit-MS by typing the MS-DOS  EXIT
         command,  and  you will find Kermit-MS as you left it, with all settings
         intact.  The same function is accomplished by the  CONNECT  escape-level
         command P.
0The local RUN command has various uses,  one  of  which  is  to  supplement  the
 features  of  Kermit-MS.   A  common complaint about Kermit-MS, for instance, is
 that it lacks login scripts, autodialer control, and phone  directories.   While
 waiting  for  these features to appear in a generally useful form in some future
 release, you might be able to provide the specific functions you need by writing
 a program in any compiled language (assembler, Pascal, C, etc) and then invoking
 from within Kermit-MS using the RUN  command.   For  instance,  if  you  have  a
 Hayes-like  modem, you could write a short program to operate the dialer with AT
 commands, accepting the phone number to dial  on  the  command  line.   If  this
 program were called DIAL, then you could "run dial 7654321" from within Kermit.
-
-
-
-
-
-
-
-
-
-                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1132                                                 Kermit File Transfer Package
-
                                 The TAKE Command
0Syntax:  TAKE filespec
0The TAKE command instructs Kermit-MS to  execute  commands  from  the  specified
 file,  which may include an explicit path; if no path is specified, the value of
 the PATH variable is used; if PATH has no  value,  then  the  current  disk  and
 directory  are  searched.   The  command  file  may  include any valid Kermit-MS
 commands, including TAKE, but it cannot include  characters  to  be  sent  to  a
 remote host during terminal emulation (i.e., after a CONNECT command).
0Commands within TAKE files, unlike interactive commands,  may  include  trailing
 comments, preceded by semicolons:
0    set port 2 ; Select the modem port
     set speed 1200 ; Set the speed for the modem
0Warning:  since TAKE  file  processing  discards  all  characters  from  a  line
 beginning  with the first semicolon, it is not possible to include semicolons in
 remote filespecs within TAKE files, e.g.,
0    get dska:foo.bar;6
0Commands from the TAKE file will normally not be displayed on your  screen.   If
 you want to see them as they are executing, you can SET TAKE-ECHO ON.
-
-
-
-
-
-
-
-
-
-
 MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 133
-
                            The LOG and CLOSE Commands
0Syntax:  LOG filespec
          CLOSE
0Specifies that your terminal session during CONNECT  will  be  recorded  in  the
 specified file; the filespec may include a device specification and/or directory
 path.  The LOG command allows you to "capture" files from a remote  system  that
 doesn't  have  Kermit, as well as to record remote command typescripts.  The log
 is closed when you EXIT from Kermit-MS or  when  you  issue  an  explicit  CLOSE
 command.
0During terminal emulation, the LOG  command  records  all  the  characters  that
 arrive  from  the remote host in the specified file, including escape sequences.
 If you have SET LOCAL-ECHO ON, it will also record the characters you type.  And
 if you have also SET DEBUG ON, then during file transfer it will also record the
 packets in the log.
0You may LOG PRN to cause the logging information to be printed directly on  your
 printer.   Note  that  any escape sequences that are sent to the screen are also
 sent to the printer.
0If you want to record information without imbedded  escape  sequences,  use  the
 screen  dump  feature,  invoked  by the CONNECT escape-level command F, which is
 described in more detail in the terminal emulation section.
-
-
-
-
-
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1134                                                 Kermit File Transfer Package
-
 7.3.5.  The SERVER Command
0Kermit-MS is capable of acting as a full-fledged Kermit server,  providing  file
 transfer  and  management  for  users coming in through one of the communication
 ports.  This is normally used when Kermit-MS is acting  as  a  remote  host  for
 another  microcomputer.   To  put  Kermit-MS  into  server mode, first issue any
 desired SET commands to select and configure the desired port, and then type the
 SERVER  command.   Kermit-MS  will  await all further instructions from the user
 Kermit on the other end of the connection, which may be hardwired  or  connected
 through an autoanswer modem.  For example:
0  Kermit-MS>set port 1
+            __________
   Kermit-MS>set speed 1200
+            ______________
   Kermit-MS>set timer on
+            ____________
   Kermit-MS>set warning on
+            ______________
   Kermit-MS>server
+            ______
0Kermit 2.29 server mode supports the following requests:
0    SEND           REMOTE DELETE       REMOTE CWD
     GET            REMOTE DIRECTORY    REMOTE HOST
     FINISH         REMOTE SPACE
     BYE            REMOTE TYPE
0The REMOTE HELP command is not implemented.  Remote CWD can be  used  to  change
 both directories and devices.
0    CAUTION:  The method used for most of the REMOTE commands  is  to  invoke  a
     task  with  the user's command line, redirect standard output to a temporary
     file, $KERMIT$.TMP, send that file back to the remote end, and  then  delete
     the  file.   Sufficient  space  must  be  available  to store this file.  To
     service DOS commands or user tasks the  boot  drive  must  hold  a  copy  of
     COMMAND.COM.  PATH  will not be searched (this can be disastrous on a floppy
     disk based system).
0    FURTHER CAUTION:  Any of these DOS tasks or programs may encounter an error,
     and  in  that  case,  DOS  will  generally  put  the familiar "Abort, Retry,
     Ignore?"  message on the screen, and  will  wait  for  an  answer  from  the
     keyboard.  This will hang the server until a human comes to the keyboard and
     gives a response.  The same thing will happen when any  program  is  invoked
     that  interacts  with the real console.  For instance, REMOTE SPACE works by
     running CHKDSK; if CHKDSK finds something wrong with the disk while tallying
     up  the  space,  it will ask (at the console) if you want to it to be fixed.
     This, too, will hang the server.
0    MORAL:  The MS-DOS Kermit server should probably  not  be  used  for  REMOTE
     commands unless someone is around to take care of it when it gets stuck.
-
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 135
-
 7.3.6.  The SET Command
0Syntax:  SET parameter value
     or:  SET parameter parameter value
0The SET command establishes or modifies various parameters for file transfer  or
 terminal  connection.   You  can  examine  their values with the STATUS and SHOW
 commands.  The following SET commands are available in Kermit-MS:
0                BAUD  Communications port line speed (synonym for SPEED)
                 BELL  Whether to beep at the end of a transaction
     BLOCK-CHECK-TYPE  Level of error checking for file transfer
                DEBUG  Display packet contents during file transfer
         DEFAULT-DISK  Default disk drive for file i/o
          DESTINATION  Default destination device for incoming files
              DISPLAY  For selecting the type of file transfer display
                 DUMP  Screen dump file (or device) name
          END-OF-LINE  Packet termination character
                  EOF  Method for determining or marking end of file
               ESCAPE  Escape character for CONNECT
         FLOW-CONTROL  Enable or disable XON/XOFF
            HANDSHAKE  Half-duplex line turnaround option
           INCOMPLETE  What to do with an incompletely received file
                  KEY  Specify key redefinitions, or "keystroke macros"
           LOCAL-ECHO  Specify which computer does the echoing during CONNECT
            MODE-LINE  Whether to display a mode line during terminal emulation
               PARITY  Character parity to use
                 PORT  Select a communications port
               PROMPT  Change the "Kermit-MS>" prompt to something else
              RECEIVE  Request remote Kermit to use specified parameters
               REMOTE  For running Kermit-MS interactively from back port
                RETRY  Packet retransmission threshold
                 SEND  Use the specified parameters during file transfer
                SPEED  Communications port line speed (synonym for BAUD)
            TAKE-ECHO  Control echoing of commands from TAKE files
             TERMINAL  Emulation and parameters
                TIMER  Enable/disable timeouts during file transfer
              WARNING  Specify how to handle filename collisions
0Next, the SET commands will be described in greater detail.
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1136                                                 Kermit File Transfer Package
-
 SET BAUD
0Syntax:  SET BAUD rate
0Set the speed of the currently selected terminal communications  port  (COM1  by
 default)  to 300, 1200, 1800, 2400, 4800, 9600, 19200 bps, or other common speed
 Kermit-MS leaves the current communication port settings alone unless you  issue
 explicit  SET  commands  to change them.  SET SPEED is an acceptable synonym for
 SET BAUD.  Note that on  certain  systems,  when  you  first  run  Kermit  after
 powering  the  system  up, you may get a message "Unrecognized baud rate".  This
 means that Kermit tried to read the speed  from  the  port  and  none  was  set.
 Simply  use  SET BAUD or the DOS MODE command to set the desired speed.  The NIH
 Computer Center MSKERMIT.INI file sets this parameter to 2400.
-SET BELL
0Syntax:  SET BELL $ON, OFF
0Specifies whether bell (beeper) should sound upon completion of a file  transfer
 operation.  Normally ON.
-SET BLOCK-CHECK
0Syntax:  SET BLOCK-CHECK $1, 2, 3
0Selects the error detection  method:   a  1-character  checksum,  a  2-character
 checksum,  or  a 3-character 16-bit cyclic redundancy check (CRC).  If the other
 Kermit program is not capable  of  type  2  or  3  checking  methods,  automatic
 fallback  to type 1 will occur.  NIH recommends use of type 3 whenever the other
 Kermit supports it.   The  NIH  Computer  Center  MSKERMIT.INI  file  sets  this
 parameter to 3.
-SET DEBUG
0Syntax:  SET DEBUG $ON, OFF
0When debugging is ON, Kermit will display packet traffic on your  screen  during
 file  transfer.   If  the  debugger is loaded, control will be transferred to it
 when Ctrl-C is typed.  During terminal emulation (on the IBM PC  only),  control
 characters  are  displayed  in uparrow notation.  If logging is being done, file
 transfer packets are included in the log.   When  OFF  (this  is  the  default),
 debugging information is not displayed, and packets are not logged.
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 137
-
 SET DEFAULT-DISK
0Syntax:  SET DEFAULT-DISK x:
0Specify the default disk drive to use for file transfer, directory listings, and
 so  forth.   Equivalent  to  typing  the DOS command for changing disks (A:, B:,
 etc).  Affects Kermit and all inferior processes, but when you exit from Kermit,
 you will still have the same default disk as when you entered.
-SET DESTINATION
0Syntax:  SET DESTINATION device
0Specify the device for incoming files during file transfer:  DISK,  PRINTER,  or
 SCREEN.   SET  DESTINATION  PRINTER  will  cause  incoming  files  to be spooled
 directly to the printer; SCREEN will send output normally destined for the  disk
 to  the  screen.   The normal destination is DISK.  SET DESTINATION affects only
 files transferred with SEND, GET, or RECEIVE; it cannot be used to  reroute  the
 output from REMOTE server commands.
-
-
-
-
-
-
-
-
-
-
-
-                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1138                                                 Kermit File Transfer Package
-
 SET DISPLAY
0Syntax:  SET DISPLAY $QUIET, REGULAR, SERIAL
0During file transfer, MS-DOS Kermit's regular  display  is  a  formatted  screen
 whose fields are randomly updated with file names, packet numbers, error counts,
 percent done, error messages, and so forth:
0               File name:  FOO
       KBytes transferred:  7
0                 Sending:  In progress
             Percent done:  52%
0       Number of packets:  74
        Number of retries:  2
               Last error:  None
             Last warning:  None
0The items in the right-hand column are updated more or less at random.
0If you wish to run Kermit-MS interactively through the back port,  for  instance
 after  the  operator has done CTTY COM1, you must give the command SET REMOTE ON
 (which, currently at least, is equivalent to SET DISPLAY QUIET); this suppresses
 the  file  transfer display screen, so that the display won't interfere with the
 file transfer itself.  You can also use this command to suppress the display  in
 local  mode,  in  case  you  are using a system that allows you to do other work
 while file transfer proceeds in the background.
0If you have your PC connected to  a  speaking  device  (a  common  practice  for
 visually  impaired  people),  or you are logging the display screen to a printer
 (using DOS XPrtSc or kermit > prn), the random nature  of  the  regular  display
 will  make  the  results of little use.  SET DISPLAY SERIAL is provided for this
 purpose; it causes the program to report progress "serially" on the screen.   In
 serial  mode,  error  messages  are  preceded  with  the word "Error" and repeat
 messages with the word "Retry".  Packets are numbered as dots with  every  tenth
 being  a  plus sign.  The packet display is automatically broken across lines at
 every 70th packet.  The serial display makes much more sense  when  spoken  than
 does the regular display.
0The serial display does not show the percent and kilobytes transferred.  REGULAR
 is the default.
-SET DUMP
0Syntax:  SET DUMP path
0Changes the file or device name of the screen dump file.  The normal  file  name
 is  KERMIT.SCN.  See  the section on terminal emulation for details about screen
 dumps.
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 139
-
 SET END-OF-LINE
0Syntax:  SET END-OF-LINE number
0If the remote system needs packets to  be  terminated  by  anything  other  than
 carriage  return, specify the decimal value of the desired ASCII character.  The
 NIH MSKERMIT.INI file sets this parameter to 13 (carriage return).
-SET EOF
0Syntax:  SET EOF $CTRL-Z, NOCTRL-Z
0Controls how the end of file is handled.  CTRL-Z specifies a Control-Z character
 should be appended to the end of an incoming file, unless it already ends with a
 Control-Z.  Certain MS-DOS text editors and other applications require files  to
 be  in this format.  For outbound files, treat the first Control-Z as the end of
 the local file, and do not send it or any subsequent  characters.   NOCTRL-Z  is
 the  default;  incoming  files are stored, and MS-DOS files are sent, exactly as
 is, in their entirety.  The NIH Computer  Center  MSKERMIT.INI  file  sets  this
 parameter to CTRL-Z.
-SET ESCAPE
0Syntax:  SET ESCAPE character
0Specify  the  control  character  you  want  to  use  to  "escape"  from  remote
 connections    back    to    Kermit-MS.     The    default    is   normally   X]
 (Control-Rightbracket).  The character is entered literally, and should normally
 be  chosen  from  the  ASCII control range.  It is not possible to use non-ASCII
 characters (e.g., function keys) for this purpose.
-SET FLOW-CONTROL
0Syntax:  SET FLOW-CONTROL $XON/XOFF, NONE
0Specify the full duplex flow control to be done on the currently selected  port.
 The  options  are XON/XOFF and NONE.  The specified type of flow control will be
 done during both terminal emulation and file  transfer.   By  default,  XON/XOFF
 flow  control  is  selected.   XON/XOFF should not be used on half-duplex (local
 echo) connections.  If XON/XOFF is used, HANDSHAKE should be set to  NONE.   The
 NIH  MSKERMIT.INI file sets this parameter to XON/XOFF for the DECsystem-10, and
 to NONE for TSO and WYLBUR.
-
-
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1140                                                 Kermit File Transfer Package
-
 SET HANDSHAKE
0Syntax:  SET HANDSHAKE $CODE number, BELL, CR, LF, NONE, XOFF, XON
0Specify any half-duplex line turnaround handshake character  for  the  currently
 selected  port.  The CODE number form allows any ASCII character to be specified
 by its decimal ASCII code.   The  specified  handshaking  is  done  during  file
 transfer  only.   Handshake  is NONE by default; if set to other than NONE, then
 FLOW-CONTROL should be set  to  NONE.   The  NIH  MSKERMIT.INI  file  sets  this
 parameter to NONE for the DECsystem-10 and TSO, and to XON for WYLBUR.
-SET INCOMPLETE
0Syntax:  SET INCOMPLETE $DISCARD, KEEP
0Specifies what to do with files that arrive incompletely:  discard them or  keep
 them.  They are normally discarded.
-SET KEY
0Syntax:  SET KEY key-specifier
0Specifies that when the designated key is struck during terminal emulation,  the
 associated  character  string is sent.  The key-specifier is one of the keywords
 BACKSPACE, F1, F2, ..., or else SCAN followed by a scan code.
0If SCAN is used, it is followed by a decimal number to indicate the scan code of
 the key, which you would ascertain from your system reference manual, or else by
 using the Kermit-MS SHOW KEY command.  SET KEY prompts you on a new line for the
 definition  string.   Certain  characters,  like  ESC and CR, may not be entered
 literally into the string, but can be included by inserting escape codes of  the
 form \ooo, a backslash followed by a 2- or 3-digit octal number corresponding to
 the ASCII value of the  desired  character.   If  some  other  key  redefinition
 package,  like  ProKey,  has  been  loaded,  then  its  redefinitions  will take
 precedence over Kermit's.
0The SET KEY command is illustrated in the terminal emulation section 7.4.   Note
 that  key  redefinitions  occur  only  during  terminal  emulation,  and  not at
 Kermit-MS command level, or outside of Kermit.
-
-
-
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 141
-
 SET LOCAL-ECHO
0Syntax:  SET LOCAL-ECHO $ON, OFF
0Specify how characters are echoed during terminal  emulation  on  the  currently
 selected  port.   ON  specifies  that  characters  are to be echoed by Kermit-MS
 (because neither the remote computer nor the communications circuitry  has  been
 requested  to echo), and is appropriate for half-duplex connections.  LOCAL-ECHO
 is OFF by default, for full-duplex, remote echo operation.
0When using Kermit to connect two PCs "back to back," use local echo so that when
 you  CONNECT  to the other PC to send messages to its operator, you can see what
 you are typing.  Depending on the system, you may have to type a carriage return
 and  a linefeed at the end of each line in order to make the display look right.
 The NIH Computer Center MSKERMIT.INI file sets this parameter  to  OFF  for  the
 DECsystem-10, and to ON for TSO and WYLBUR.
-SET MODE-LINE
0Syntax:  SET MODE-LINE $ON, OFF
0Turn the status, or "mode" line (the 25th line during terminal connection) on or
 off.   When  the  mode  line  is  enabled, it may be turned on and off using the
 CONNECT escape-level command M. Refer to the terminal  emulation  section,  7.4,
 for further details.
-
-
-
-
-
-
-
-
-
-                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1142                                                 Kermit File Transfer Package
-
 SET PARITY
0Syntax:  SET PARITY $EVEN, ODD, MARK, SPACE, NONE
0Specify the character parity to be used on the currently  selected  port.   NONE
 means  no  parity  processing  is done, and the 8th bit of each character can be
 used for data when transmitting binary files.  This is the normal case.
0You will need to  SET  PARITY  to  ODD,  EVEN,  MARK,  or  possibly  SPACE  when
 communicating   with   a   system,   or  over  a  network,  or  through  modems,
 concentrators, multiplexers, or front ends  that  require  or  impose  character
 parity  on the communication line.  For instance, GTE Telenet normally uses MARK
 parity.  If you neglect to SET PARITY when the communications equipment requires
 it,  the  symptom  may  be  that  terminal  emulation  works (well or maybe only
 partially), but file transfer does not work at all.
0If you have set parity to ODD, EVEN, MARK, or SPACE, then Kermit-MS will request
 that  binary  files  will  be transferred using 8th-bit-prefixing.  If the other
 Kermit knows how to do 8th-bit-prefixing (this is an  optional  feature  of  the
 Kermit  protocol,  and  not  all implementations of Kermit have it), then binary
 files can be transmitted successfully.  If NONE is specified,  8th-bit-prefixing
 will  not  be  requested.   Note  that there is no advantage to using parity; it
 reduces Kermit's file transfer efficiency without providing any additional error
 detection.   The SET PARITY command is provided only to allow Kermit to adapt to
 conditions  where  parity  is  required,  or  8-bit  transmission  is  otherwise
 thwarted.   The  NIH  MSKERMIT.INI  file sets this parameter to EVEN for TSO and
 WYLBUR, and to NONE for the DECsystem-10.
-SET PORT
0Syntax:  SET PORT $number, COM1, COM2
0On machines with more than one communications port, select the port to  use  for
 file  transfer  and CONNECT.  This command lets you use a different asynchronous
 adapter, or switch between two or more simultaneous remote sessions.  Subsequent
 SET  SPEED,  PARITY, HANDSHAKE, FLOW, and LOCAL-ECHO commands will apply to this
 port only.  SET PORT 1 selects COM1, SET PORT 2 selects COM2.   Kermit  defaults
 to port 1.  The NIH Computer Center MSKERMIT.INI file sets this parameter to 1.
-SET PROMPT
0Syntax:  SET PROMPT string
0This command allows you to change the MS-DOS Kermit program's prompt.
-
-
-
 MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 143
-
 SET RECEIVE
0Syntax:  SET RECEIVE parameter value
0At the beginning of a protocol operation, request the remote Kermit to  use  the
 given value specified parameter, or inform Kermit-MS that the remote Kermit will
 be using it.
0PACKET-LENGTH number
0        Ask the remote Kermit to use the specified maximum  length  for  packets
         that it sends to Kermit-MS.  The normal (and maximum) length is 94.  Use
         this command to shorten packets if the communication line is noisy; this
         will   decrease  the  probability  that  a  particular  packet  will  be
         corrupted, and will reduce the retransmission overhead  when  corruption
         occurs, but it will increase the protocol overhead.
0PADCHAR number
0        Ask the remote Kermit to use the given control character (expressed as a
         decimal  number 0-31, or 127) for interpacket padding.  Kermit-MS should
         never require any padding.
0PADDING number
0        Ask the remote Kermit to insert the given number of  padding  characters
         before each packet it sends.  This should never be necessary.
0START-OF-PACKET number
0        If the remote Kermit will be marking the beginning  of  packets  with  a
         control  character  other  than  Control-A,  use  this  command  to tell
         Kermit-MS about it (the number should be the decimal ASCII  value  of  a
         control  character).   This  will  be  necessary  only  if  the hosts or
         communication equipment involved cannot  pass  a  Control-A  through  as
         data,  or  if  some  piece of communication equipment is echoing packets
         back at you.
0TIMEOUT number
0        Ask the remote Kermit to time out after the given number of seconds if a
         packet  expected  from  Kermit-MS  has not arrived.  Use this command to
         change the normal timeout interval.
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1144                                                 Kermit File Transfer Package
-
 SET REMOTE
0Syntax:  SET REMOTE $ON, OFF
0SET REMOTE ON removes the file transfer display (as if you had given the command
 SET  DISPLAY QUIET).  It should be used when you are running Kermit-MS in remote
 mode (i.e., when coming in from another PC through the Kermit-MS's "back  port",
 to  which  the  console  has been reassigned using the DOS CTTY command).  It is
 necessary to issue this command because (a) Kermit-MS has no way of knowing that
 its  console  has  been  redirected, and (b) when the console is the same as the
 port, the file transfer display will interfere with the  file  transfer  itself.
 SET REMOTE OFF returns the file transfer display to its preferred style (REGULAR
 or SERIAL).
-SET RETRY
0Syntax:  SET RETRY number
0Sets the number of times a packet is retransmitted before the protocol gives up.
 The  number of retries can be between 1 and 63, and is 5 by default.  This is an
 especially useful parameter when the communications line is noisy or the  remote
 host is very busy.
-
-
-
-
-
-
-
-
-
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 145
-
 SET SEND
0Syntax:  SET SEND parameter value
0PACKET-LENGTH number
0        Use the  specified  maximum  length  for  outbound  packets.   Normally,
         Kermit-MS uses whatever length the other Kermit requests.
0PADCHAR number
0        Use the specified control character for interpacket padding.  Some hosts
         may  require  some  padding  characters  (normally  NUL or DEL) before a
         packet, and certain front ends or other communication equipment may need
         certain control characters to put them in the right modes.
0PADDING number
0        How many copies of  the  pad  character  to  send  before  each  packet,
         normally zero.
0PAUSE number
0        How many milliseconds to pause between sending the next  packet,  0-127,
         normally  zero.  This helps half-duplex systems prepare for reception of
         our packet.  Padding characters are  sent  only  after  the  time  limit
         expires.
0QUOTE number
0        Use the indicated printable character for  prefixing  (quoting)  control
         characters  and other prefix characters.  The only reason to change this
         would be for sending a very  long  file  that  contains  very  many  "#"
         characters (the normal control prefix) as data.
0START-OF-PACKET number
0        Mark the beginning of outbound packets with some control character other
         than  Control-A.   This  will  be  necessary  if  the remote host or the
         communication channel involved cannot accept a Control-A as data, or  if
         it  echoes  back your packets.  The remote host must have been given the
         corresponding SET RECEIVE START-OF-PACKET command.
0TIMEOUT number
0        Change Kermit-MS's normal timeout interval; this  command  is  effective
         only  if  TIMER  is  set to be ON; it is normally OFF so that the remote
         Kermit can control timeouts.  When the timer is ON, the default  timeout
         interval is 13 seconds.
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1146                                                 Kermit File Transfer Package
-
 SET SPEED
0Syntax:  SET SPEED rate
0Set the speed of the currently selected terminal communications  port  (COM1  by
 default) to 300, 1200, 1800, 2400, 4800, 9600, 19200 bps, or other common speed.
 The  NIH  Computer  Center  MSKERMIT.INI  file  sets  this  parameter  to  2400.
 Kermit-MS  leaves the current communication port settings alone unless you issue
 explicit SET commands to change them.  SET BAUD is an acceptable synonym for SET
 SPEED.   Note  that on certain systems, when you first run Kermit after powering
 the system up, you may get a message "Unrecognized baud rate".  This means  that
 Kermit  tried  to read the baud rate from the port and none was set.  Simply use
 SET SPEED or the DOS MODE command to set the desired speed.   The  NIH  Computer
 Center MSKERMIT.INI file sets this parameter to 2400.
-SET TAKE-ECHO
0Syntax:  SET TAKE-ECHO ON or OFF
0Specifies whether screen display should occur during implicit or  explicit  TAKE
 operations  on  MSKERMIT.INI  or  other  Kermit-MS  command  files,  and  during
 evaluation of macro definitions.  Handy for finding errors.   The  NIH  Computer
 Center MSKERMIT.INI file sets this parameter to ON.
-
-
-
-
-
-
-
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 147
-
 SET TERMINAL
0Syntax:  SET TERMINAL parameter [value]
0This  command  controls  most  aspects  of  terminal  emulation.   Most  of  the
 parameters  are  only  settable  (or  meaningful)  on  the  IBM  PC  family  and
 compatibles.
0The first group of parameters tells which kind of  terminal  to  emulate.   When
 Kermit-MS  uses  its  built-in  software  for emulation, incoming characters are
 examined for  screen  control  commands  (escape  sequences)  specific  to  that
 terminal, and if encountered, the commands are executed on the PC screen.
0NONE    Act as a dumb terminal.  All incoming characters will  be  sent  to  the
         screen  "bare",  as-is, through DOS.  If you have loaded a device driver
         into DOS for the CON device, such as ANSI.SYS, then that driver will  be
         able to interpret the codes itself.  Many non-IBM systems have their own
         screen control code interpreter built into DOS or firmware, or available
         as a loadable device driver.
0VT52    The DEC VT-52 terminal.
0HEATH   The  Heath/Zenith-19  terminal  (H19),  which  supports  all  the   VT52
         commands, plus line and character insert/delete editing functions, and a
         25th line.
0VT102   The DEC VT102 (ANSI) terminal, which is the same as  a  VT100  but  also
         supports  line/character  insert/delete editing functions.  VT102 is the
         default value set by the NIH MSKERMIT.INI file.
0TEKTRONIX
0        A Tektronix 4010 graphics terminal.  Available on TI and Victor PCs; not
         available on IBM PCs.
0The specific escape sequences supported by Kermit for  each  of  these  terminal
 types are listed in section 7.5.
-
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1148                                                 Kermit File Transfer Package
-
 The remaining SET TERMINAL commands  specify  setup  options  for  the  selected
 terminal:
0 CHARACTER-SET $UK, US
0         UK displays # as a pound sterling sign, US displays # as #.
0 COLOR number [, number [, number]]
0        Several numbers, applied in left to right sequence, separated by  commas
         or spaces:
0           0   Reset the colors to normal intensity white characters on a black
                background  and use the "no-snow" mode on the IBM Color Graphics
                Adapter (CGA).
            1   High intensity foreground
            10  Request fast screen updating for use on the IBM EGA or PGA,  and
                some non-IBM CGAs.
            3x  Foreground color
            4x  Background color
0         where x is a single digit from 0 to 7, which is the sum of the desired
          colors:
0           1   Red
            2   Green
            4   Blue
0        Example:  0, 1, 34, 40 on an IBM CGA would produce  blue  characters  on
         black  field  with  no  snow.   The snow removal business has to do with
         whether the  program  should  synchronize  with  vertical  retrace  when
         updating  screen  memory.  This is necessary with certain color adaptors
         (like the CGA) and unnecessary for others (like the EGA).
0 CURSOR-STYLE $BLOCK, UNDERLINE
0        Sets the cursor rendition to your preference.  Note that on  some  early
         IBM  PCs and compatibles, the cursor may not be restored correctly after
         escape back from CONNECT because of a bug in the early IBM BIOS.
0 KEYCLICK $ON, OFF
0        Turns electronic keyclick ON or OFF.  If your keyboard has a  mechanical
         clicker  (as  IBM  boards  do),  you  may  not notice the effect of this
         command.
0 MARGIN-BELL $ON, OFF
0        Controls whether the bell should  be  sounded  when  the  cursor  passes
         column 72 near the right screen margin.
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 149
-
  NEWLINE-MODE $ON, OFF
0        ON sends a carriage-return-linefeed combination  (CRLF)  when  you  type
         carriage return (CR) during terminal emulation; OFF (default) just sends
         a CR when you type CR.  The NIH Computer Center MSKERMIT.INI  file  sets
         this parameter to OFF.
0 SCREEN-BACKROUND $NORMAL, REVERSE
0        NORMAL means dark background, light  characters.   REVERSE  means  light
         background, dark characters.
0 TAB $AT n, CLEAR AT n, CLEAR ALL
0        Sets tab stops or clears one  or  all  tab  stops.   n  is  the  numeric
         position  of the tab to be set or cleared.  By default, tabs are every 8
         spaces, at positions 9, 17, 25, etc.  Only meaningful when  emulating  a
         terminal  that  has  settable  tabs  (the  VT52 doesn't).  More than one
         tabstop may be specified  by  separating  column  numbers  with  commas,
         spaces, or tabs.  The NIH Computer Center MSKERMIT.INI file sets tabs at
         9, 17, 25, 33, 41, 49, 57, 65, and 73.
0 WRAP $ON, OFF
0        ON automatically breaks screen lines (by inserting  a  CRLF)  when  they
         reach  the  the  right margin; OFF disables wrapping -- if a line is too
         long, the excess characters go off the  screen.   The  NIH  MSKERMIT.INI
         file  sets this parameter to OFF for the DECsystem-10, and to ON for TSO
         and WYLBUR.
-SET TIMER
0Syntax:  SET TIMER $ON, OFF
0This command enables or disables the timer that is used during file transfer  to
 break deadlocks that occur when expected packets do not arrive.  By default, the
 timer is ON.  The NIH Computer Center MSKERMIT.INI file sets this  parameter  to
 OFF.
-
-
-
-
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1150                                                 Kermit File Transfer Package
-
 SET WARNING
0Syntax:  SET WARNING $ON, OFF
0Specify what to do when an incoming file has the same name as an  existing  file
 in  the  default  directory  of the default device.  If ON, Kermit will warn you
 when an incoming file has the same name as an existing file,  and  automatically
 rename  the  incoming  file  (as  indicated in the warning message) so as not to
 destroy (overwrite)  any  existing  one.   If  OFF,  the  pre-existing  file  is
 destroyed,  even if the incoming file does not arrive completely.  WARNING is ON
 by default.
0The new name is formed by adding numbers to the part of the name before the dot.
 For instance, ABC.TXT becomes ABC00001.TXT, then ABC00002.TXT, etc.
-7.3.7.  The SHOW Command
0Syntax:  SHOW option
0Most parameters that may be altered with  SET  commands  are  displayed  by  the
 STATUS  command.   The SHOW command is used for displaying macro definitions and
 key redefinitions.
0The SHOW MACROS command  displays  the  definitions  of  all  currently  defined
 macros, as well as the amount of space left for new macro definitions.
0The SHOW KEY command allows you to determine the scan code produced by  pressing
 a  given  key,  so that you can construct a SET KEY SCAN command to redefine the
 key.  If the key already  has  a  redefinition  in  effect,  that  too  will  be
 displayed.   This can be done either interactively or in a macro command.  Refer
 to the terminal emulation section for examples.
-
-
-
-
-
-
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 151
-
 7.3.8.  Command Macros
0Kermit-MS provides a facility for combining  commands  into  "macros."   Command
 macro  definitions  may  be included in your MSKERMIT.INI file, TAKEn explicitly
 from a specified file, or typed interactively.  Macros are invoked with  the  DO
 command.
-                               The DEFINE Command
0Syntax:  DEFINE macro-name [command [, command [, ...]]]
0Kermit-MS command macros are constructed with the DEFINE command.  Any Kermit-MS
 commands may be included.  Example:
0    define tso set parity even, set speed 2400, connect
0A macro can be undefined by typing an empty DEFINE command for it, like
0    define tso
0A macro definition may be no longer than 128 characters.  Longer definitions can
 be accomplished by "chaining."  Example:
0    define setup set port 1, set speed 19200, set parity even, do setup2
     define setup2 set port 2, set speed 1200, set parity none, do setup3
     define setup3 set warning on, set incomplete keep, connect
0The SHOW MACROS command displays the value of all currently defined macros,  and
 tells how much space is left for further definitions.
-
-
-
-
-
-
-
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1152                                                 Kermit File Transfer Package
-
                                  The DO Command
0A Kermit-MS command macro is invoked using the DO command.   For  instance,  the
 NIH  supplied MSKERMIT.INI file defines the macros WYLBUR, DEC10, TSO, and 3270.
 To setup the emulation for WYLBUR, you would type
0    do wylbur
+    _________
0The WYLBUR macro contains SET commands for speed, parity, local echo, etc.   You
 can  use  the  DEFINE  command  to  redefine  the  macro or to nullify the macro
 definition altogether.  The latter is accomplished by creating an  empty  macro,
 e.g.
0    define ______
+    _______wylbur
0There is no automatic way to undo (negate) the effect of DOing a macro.  If  you
 need  to  accomplish this effect, you should use another macro for that purpose.
 For instance, to undo the effect of "do wylbur" so that you  could  connect  to,
 say, the DECsystem-10, you could:
0    do dec10
+    ________
0using another of the predefined macros in the MSKERMIT.INI file supplied by  the
 NIH Computer Center.
0If you wish to view the macro expansion whenever you issue a DO command, you can
 SET TAKE-ECHO ON.
-
-
-
-
-
-
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 153
-
 7.4.  Terminal Emulation
0When you issue the CONNECT command, your PC acts as a terminal  connected  to  a
 remote  computer  through  the currently selected port.  The characters you type
 are sent out the port, and characters that arrive at the port are  displayed  on
 your  screen,  or  interpreted  according  to whatever type of terminal is being
 emulated.
0If you have not previously issued a SET PORT command, COM1 is used.  If you have
 SET  LOCAL-ECHO ON for the selected port, then Kermit-MS will display characters
 on the screen as you type them, otherwise it will rely on the remote  system  to
 echo  them.  XON/XOFF flow control will be done unless you have SET FLOW-CONTROL
 OFF.  If you have SET PARITY to anything other than NONE, Kermit-MS will add the
 appropriate  parity  to  each outbound character.  While CONNECTed, you can also
 communicate directly  with  an  autodialer  or  "smart  modem"  to  control  the
 communications  line,  hang  it  up,  and  the  like, for instance, by typing AT
 commands to a Hayes-compatible modem.
0When you CONNECT, the program attempts to raise the DTR and RTS RS-232  signals,
 and  it  takes  no specific action to lower them unless you explicitly issue the
 HANGUP command.
0The IBM PC version of Kermit-MS emulates the DEC VT102 terminal by default,  and
 may  also  be  instructed  to  emulate  the DEC VT52, the Heath/Zenith-19, or no
 terminal at all, via the SET TERMINAL  command.   Emulation  of  each  of  these
 terminals  is  nearly  complete.   VT102 emulation lacks only smooth scroll, 132
 column mode, and ANSI printer control.  Double-height,  double-width  characters
 are  supported, but simulated using ordinary characters.  On color monitors, the
 foreground and background colors may  be  set  using  SET  TERMINAL  COLOR,  and
 inverse/normal  video  display  may  also  be  selected,  along  with many other
 terminal  parameters.   A  complete  list   of   the   commands,   default   key
 configurations,  and  escape  sequences  accepted  by the IBM PC Kermit terminal
 emulator is given in section 7.5.
-
-
-
-
-
-
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1154                                                 Kermit File Transfer Package
-
 The Escape Character
0The escape character is  used  to  regain  the  attention  of  Kermit-MS  during
 CONNECT,  i.e.,  terminal  emulation.   When  you  type  the  escape  character,
 Kermit-MS waits for you to follow it  with  a  single  character  command.   For
 instance,  the single character command "?"  produces a list of available single
 character commands.  This command is executed immediately; it may not be edited,
 and the program does not wait for a carriage return to confirm it.  Here are the
 CONNECT escape-level commands available in Kermit-MS:
0  ?   Help -- prints the available single-character commands.
   0   (the digit zero) Transmit a NUL (ASCII 0).
   B   Transmit a BREAK signal.
   C   Close the connection and return to Kermit-MS prompt level.
   F   File the current screen in the screen dump file.
   M   Toggle the mode line, i.e., turn it off if it is on & vice versa.
   P   Push to DOS; get back to CONNECT by typing EXIT.
   Q   Temporarily quit logging the remote session.
   R   Resume logging the remote session.
   S   Show the status of the connection.
   X]  (or whatever you have set the escape character to be)
       Typing  the  escape character twice sends one copy of it to the connected
       host.
0Typing any other character (except the space bar, which is the  "null  command")
 after  the  escape  character will cause Kermit-MS to beep, but will do no harm.
 The escape character can be changed to something other than Control-Rightbracket
 by using the SET ESCAPE command.
0Note:  Ctrl-Break can be used to transmit a BREAK signal.   You  may  find  this
 more  convenient  to use than typing the escape character followed by the letter
 B.
-
-
-
-
-
-
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 155
-
 The Mode Line
0When you first issue the CONNECT command, an  inverse  video  "mode  line"  will
 display  the  most important facts about the connection you've just established,
 so that you can quickly diagnose any problems.  Here's what the IBM PC mode line
 looks like:
0+---------------------------------------------------------------------------+
 | Esc-chr:X] help:X]? port:1 speed:2400 parity:even echo:rem VT102 .... PRN |
 +---------------------------------------------------------------------------+
0This shows that the escape character is Ctrl-Rightbracket, that you  would  type
 Ctrl-rightbracket  followed  by  question mark (X]?) to get help during CONNECT,
 that you are connected on port 1 at 2400 baud with even parity and remote  echo,
 and that a VT102 terminal is being emulated.  The four dots represent the VT102s
 LEDs (they turn into the digits 1,2,3,4 when "lit") and PRN will show up if  the
 printer is activated (e.g., by Ctrl-PrintScreen).
0The mode line occupies the 25th line of the  screen,  and  is  not  affected  by
 scrolling.   When  emulating  a VT102 or Heath-19, Kermit will allow the host to
 address the 25th line directly  using  cursor  positioning  commands.   If  this
 happens,  Kermit  will  remove  its mode line and relinquish control of the 25th
 line to the host (as if you had typed SET MODE OFF).  When no terminal is  being
 emulated,  the  25th line (if any) is available for scrolling.  If the mode line
 is disabled by an application or by the command SET MODE OFF then the  only  way
 to revive Kermit's mode line display is to give the command SET MODE ON.
-7.4.1.  Screen Scroll
0On certain systems, Kermit-MS provides several pages of screen memory, which may
 be scrolled up and down using keys as shown in Table 1-1.
0-------------------------------------------------------------------------------
-      Screen Forward  Line Forward        Screen Backward   Line Backward
0      PgDn            Ctrl-PgDn           PgUp              Ctrl-PgUp
0                   Table 7-1:   Kermit-MS Screen Scroll Keys
0-------------------------------------------------------------------------------
0There is no way to assign these functions to other keys.
0The IBM PC also allows use of the Home key to get to  the  top  of  its  display
 memory  and  End key to get to the bottom, and the keypad plus (+) key to toggle
 the mode line on and off.
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1156                                                 Kermit File Transfer Package
-
 7.4.2.  Screen Dump
0The screen dump feature writes the contents of the screen to a file  (KERMIT.SCN
 unless  another  file  was  selected  by  the SET DUMP command) when the CONNECT
 escape-level command F is typed.  The screen dump file is appended  to  on  each
 successive screen dump, with each screen separated by a formfeed (Ctrl-L).  This
 feature may be used in conjunction with  screen  rollback  --  a  handy  way  to
 recapture  screenfuls  of  laboriously  typed-in  text  after  a remote host has
 crashed without saving your work.
0A screen dump differs from a session log  in  two  ways.   First,  each  desired
 screen  must  be  manually  filed,  and  second,  the  screen dump file has been
 stripped of any escape sequences, whereas the session log records them.
-7.4.3.  Printer Control
0During terminal emulation, a locally attached printer may be controlled  in  the
 normal  manner.   Pushing  the "Print Screen" key shifted will cause the current
 contents of the screen to  be  printed  or  spooled;  holding  down  CTRL  while
 depressing  Print  Screen will start or stop the spooling of incoming characters
 to the printer.  On the IBM PC, the mode line will show PRN when the printer  is
 activated  in  this  manner.   XP  or  XN  are  sent to the host during terminal
 emulation, and do not toggle printing, as they do when you're  talking  directly
 to DOS.
0CTRL-Print-Screen can  be  simulated  with  the  Kermit-MS  LOG  PRN  and  CLOSE
 commands.
-7.4.4.  Key Redefinitions
0Key redefinitions are useful for defining "keystroke macros" of login sequences,
 frequently  issued  commands,  and so forth, and for setting up the terminal for
 use with host resident software  designed  to  work  with  terminals  that  send
 predefined  sequences  from  their  function  keys.   For instance, here's a key
 redefinition file for arranging the DEC Rainbow keyboard into the  normal  ASCII
 keyboard layout:
0    ; Make shift-comma send a left angle bracket
     set key scan 556
     <
     ; Shift-period sends a right angle bracket
     set key scan 558
     >
     ; Accent grave is where ESC is supposed to be
     set key scan 96
     \33
     ; Put accent grave on the ESC function key
     set key f11
     `
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 157
-
 More Examples:
0    ; set AT&T 2224B autodial sequence for access to TSO in F9 key.
     SET KEY F9
     AT4922223\15
     ; set F10 key to TSO LOGON command.
     SET KEY F10
     LOGON AAAAIII/NONE/BBB\15
0Since SET KEY is a two-line command, a special trick is necessary  in  order  to
 include  it in a single-line macro definition:  just use a comma where you would
 have typed carriage return after the first line, for instance:
0    define bar set key scan 261,foo
0The CLEAR command may be used to eliminate all key redefinitions.  The  SET  KEY
 facility  may be used provide the PC with a "meta" key for use with editors like
 EMACS or TVEDIT that can use "meta characters" as commands.  Note:  No  Computer
 Center  supported  software  offered  on  the  IBM  System 370 uses meta keys as
 described here.  A meta key is a shift key whose effect is to turn  on  the  8th
 (parity)  bit  of  the  character.   For  instance, on the IBM PC the scan codes
 produced by holding down ALT together with other keys can  be  determined  using
 SHOW  KEY,  and  then  8-bit ASCII equivalents with the 8th bit turned on can be
 defined using SET KEY; if the scan code produced  by  typing  ALT-a,  i.e.,  the
 letter "a" (ASCII 141, octal) with the ALT key held down, is 2078 (decimal), you
 would set the META equivalent to 141+200=341 (octal), or "\341" in octal SET KEY
 notation:
0    Kermit-MS>show key
     Press a key: ALT-a
       Scan Code: 2078
       Definition:
     Kermit-MS>set key scan 2078
     Definition String: \341
0Whenever you type ALT-a with this definition in effect, Kermit-MS will  transmit
 octal 341, rather than 141.
-
-
-
-
-
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1158                                                 Kermit File Transfer Package
-
 7.5.  IBM-PC MS Kermit Terminal Emulator Summary
0                     By Joe Doupnik, Utah State University
0This section summarizes the IBM  PC  Kermit-MS  keyboard  and  screen  operation
 during  emulation  of  H19,  VT52,  and VT102 terminals.  Note that spaces shown
 between characters of escape sequences are there for ease of reading; the actual
 sequences contain no spaces.
-7.5.1.  Keyboard Layout and Characters Sent
0Here is how the keypad functions are assigned to the IBM keyboard function keys:
0---------------------------------------------------------------------------
        Heath-19 and VT52 Keypads                     VT102 keypad
               IBM Keys                                 IBM keys
    +------+------+-------+----------+       +------+------+------+------+
    | Blue |  Red |  Grey | up arrow |       |  PF1 |  PF2 |  PF3 |  PF4 |
    |  F1  |  F2  |  F3   | up arrow |       |  F1  |  F2  |  F3  |  F4  |
    +------+------+-------+----------+       +------+------+------+------+
    |  7   |  8   |  9    |down arrow|       |  7   |  8   |  9   |  -   |
    |  F5  |  F6  |  F7   |down arrow|       |  F5  |  F6  |  F7  |  F8  |
    +------+------+-------+----------+       +------+------+------+------+
    |  4   |  5   |  6    | rgt arrow|       |  4   |  5   |  6   |  ,   |
    |  F9  |  F10 |  SF1  | rgt arrow|       |  F9  |  F10 |  SF1 |  SF2 |
    +------+------+-------+----------+       +------+------+------+------+
    |  1   |  2   |  3    |left arrow|       |  1   |  2   |  3   |  E   |
    |  SF3 |  SF4 |  SF5  |left arrow|       |  SF3 |  SF4 |  SF5 |  n  S|
    +------+------+-------+----------+       +------+------+------+  t  F|
    |  0------0   |  .    |  Enter   |       |  0------0   |  .   |  e  6|
    |  SF7        |  SF8  |  SF6     |       |   SF7       |  SF8 |  r   |
    +-------------+-------+----------+       +-------------+------+------+
-                SF1 means push Shift and F1 keys simultaneously
0---------------------------------------------------------------------------
-Cursor Keys
-                              H-19 & VT52           VT102
 VT52/H19 key   IBM key        All Modes      Numeric   Application
 up arrow       up arrow       ESC A          ESC [ A   ESC O A
 down arrow     down arrow     ESC B          ESC [ B   ESC O B
 right arrow    right arrow    ESC C          ESC [ C   ESC O C
 left arrow     left arrow     ESC D          ESC [ D   ESC O D
-
-
 MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 159
-
 Auxiliary Keypad
0                              Heath-19 & VT52             VT102
 VT52/H19 key   IBM key        Numeric Applic.   Numeric   Applic.
0PF1/HF7/Blue   F1             ESC P   ESC P     ESC O P   ESC O P
 PF2/HF8/Red    F2             ESC Q   ESC Q     ESC O Q   ESC O Q
 PF3/HF9/Grey   F3             ESC R   ESC R     ESC O R   ESC O R
 PF4/HF1        F4             ESC S   ESC S     ESC O S   ESC O S
 0              SF7            ESC ? p           ESC O p
 1              SF3            ESC ? q           ESC O q
 2              SF4            ESC ? r           ESC O r
 3              SF5            ESC ? s           ESC O s
 4              F9             ESC ? t           ESC O t
 5              F10            ESC ? u           ESC O u
 6              SF1            ESC ? v           ESC O v
 7              F5             ESC ? w           ESC O w
 8              F6             ESC ? x           ESC O x
 9              F7             ESC ? y           ESC O y
 - (minus)      F8             ESC ? m           ESC O m
 , (comma)      SF2            ESC ? l           ESC O l (ell)
 . (period)     SF8            ESC ? n           ESC O n
 Enter          SF6            ESC ? M           ESC O M
-        (SFn means hold down Shift key while pressing Function key n.)
-Other IBM keys operational in Connect mode:
0Del (White key) Send ASCII Del code (rubout).
 Backspace       Send ASCII Del code (rubout).
 Shift BackSpace Send ASCII BS code (backspace).
 Keypad (Grey)+  Toggle mode line on/off (only if Mode Line is enabled).
 Alt -           Toggle among Heath-19, VT52, and VT100 emulation.
 Alt =           Clear screen and reset terminal emulator  to  starting  (setup)
                 state.
 Home            Roll screen up (text down) to beginning of storage.
 End             Roll screen down (text up) to end of storage.
 PgUp            Roll screen up (back, earlier) one screen full.
 PgDn            Roll screen down (forward, later) one screen full.
 Ctrl-PgUp       Roll screen up one line.
 Ctrl-PdDn       Roll screen down one line.
0Control-PrtSc   Toggle  on/off copying of received text to printer, "PRN" shows
                 on far right of mode line when activated.
0Control-End     Dump image of screen  to  a  disk  file  or  device.    Default
                 filename  is  KERMIT.SCN  in the current directory. Use command
                 SET DUMP to change the filename.  Screen images are appended to
                 the file, separated by formfeeds.
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1160                                                 Kermit File Transfer Package
-
 Shift-PrtSc     Standard Print-screen, dump screen image to printer.
0"Alt -" means hold down Alt and type minus.  This  switches  among  the  various
 kinds  of  emulation,  but  does  not  change  most  operating parameters of the
 emulator.
-CONNECT Escape Commands
0Type Kermit escape character (normally "X]"), then one of the keys below:
0    ?   display this short list.
     0   send a null character.
     B   send a BREAK signal.
     C   close connect session & return to Kermit prompt.
     F   dump screen to filespec, default is Kermit.scn.
     M   toggle mode line on/off.
     P   push to DOS.
     Q   quit (suspend) logging.
     R   resume logging.
     S   show status.
     Kermit escape character itself: send it to the host.
-
-
-
-
-
-
-
-
-
-
-
 MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 161
-
 7.5.2.  Responses to Characters Received by the Terminal Emulator
0Unknown escape sequences of the form "ESC char" are  absorbed  by  the  emulator
 without further effect.
0DEC VT102 functions while in ANSI (VT102) mode, unsupported features  marked  by
 asterisk (*):
0Escape Seq     Mnemonic       Description of Action
 ESC D          IND            Index, moves cursor down one line, can scroll
 ESC E          NEL            Move cursor to start of line below, can scroll
 ESC H          HTS            Set one horizontal tab at current position
 ESC M          RI             Reverse Index, cursor up one line, can scroll
 ESC Z          DECID          Identify terminal (response is ESC [ ? 6 c)
 ESC c          RIS            Reset terminal to initial state
 ESC =          DECKPAM        Enter keypad application mode
 ESC >          DECKNPNM       Enter keypad numeric mode
 ESC 7          DECSC          Save cursor position and attributes
 ESC 8          DECRC          Restore cursor from previously saved position
 ESC # 3        DECDHL         Double height and width line, top half
 ESC # 4        DECDHL         Double height and width line, bottom half
 ESC # 5        DECSWL         Single height and width line
 ESC # 6        DECDWL         Double width single height line
 ESC # 8        DECALN         Screen alignment diagnostic - not supported
 ESC [ Pn A     CUU            Cursor up Pn lines, does not scroll
 ESC [ Pn B     CUD            Cursor down Pn lines, does not scroll
 ESC [ Pn C     CUF            Cursor forward, stays on same line
 ESC [ Pn D     CUB            Cursor backward, stays on same line
 ESC [ Pn; Pn H CUP            Set cursor to row, column (same as HVP)
 ESC [ Ps J     ED             Erase in display:
                                0 = cursor to end of screen, inclusive
                                1 = start of screen to cursor, inclusive
                                2 = entire screen, reset lines to single
                                    width, cursor does not move.
 ESC [ Ps K     EL             Erase in line:
                                0 = cursor to end of line, inclusive
                                1 = start of line to cursor, inclusive
                                2 = entire line
 ESC [ Pn L     (VT102)        Insert Pn lines preceding current line.
 ESC [ Pn M     (VT102)        Delete Pn lines from current downward, incl.
 ESC [ Pn P     (VT102)        Delete Pn chars from cursor to left, incl.
 ESC [ Pn; Pn R CPR            Cursor report (row, column), sent by terminal
                               Example: home position yields ESC [ 1; 1 R
 ESC [ Pn c     DA             Device attributes (reports ESC [ ? 6 c)
 ESC [ Pn; Pn f HVP            Set cursor to row, column (same as CUP)
 ESC [ Ps g     TBC            Tabs clear, 0 = at this position, 3 = all
 ESC [ 20 h     LNM            Set newline mode (lf = cr/lf)
 ESC [ 20 l     LNM            Reset newline mode (lf = lf)
 ESC [ ? Ps;...;Ps h  SM       Set mode, see table below
 ESC [ ? Ps;...;Ps l  RM       Reset mode, see table below
         Ps     mnemonic       mode           set            reset
         0                     error (ignored)
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1162                                                 Kermit File Transfer Package
-
         1      DECCKM         cursor keys    application    cursor/numeric
         2      DECANM         ANSI/VT52      ANSI/VT102     VT52
         3      DECCOLM        Columns        *132 col       80 col
         4      DECSCLM        *Scrolling     smooth         jump
         4      (VT102)        Insert/Replace insert         replace
         5      DECSCNM        Screen         reverse video  normal
         6      DECOM          Origin         relative       absolute
         7      DECAWM         Autowrap       on             off
         8      DECARM         *Autorepeat    on             off
         9      DECINLM        *Interlace     on             off
         18     (VT102)        *Printer termination character
         19     (VT102)        *Printer extent
 ESC [ Pn i     (VT102)        *Printer controls
 ESC [ ? Pn i   (VT102)        *Printer controls
 ESC [ Ps;...;Ps m  SGR        Select graphic rendition
                                0 = all attributes off (#'s 1, 4, 5, 7)
                                1 = bold, intensify foreground
                                4 = underscore (reverse video on IBM CGA)
                                5 = blink
                                7 = reverse video
                non-DEC extensions: 30-37 = foreground color = 30 + colors
                                    40-47 = background color = 40 + colors
                                    colors: 1 = red, 2 = green, 4 = blue
 ESC [ Ps n     DSR            Device Status Report.
                               Response from VT100: 0 = ready, 3=malfunction.
                               Command to VT100: 5 = report status with DSR,
                               6 = report cursor position using CPR sequence.
 ESC [ Ps;...;Ps q  DECLL      Load LEDs, Ps=0 means clear LED#1-4
                               Ps = 1,2,3,4 sets LED # 1,2,3,4
 ESC [ Pn; Pn r DECSTBM        Set top and bottom scrolling margins
 ESC [ sol x    DECREQTPARM    Request terminal parameters, see table below
 ESC [ sol; par; nbits; xspeed; rspeed; clkmul; flags x
                DECREPTPARM    Reports terminal parameters
                               *sol = 0  request; term can send unsolicited
                                 reports - not supported
                               sol = 1, request; term reports only on request
                               sol = 2, this is a report (DECREPTPARM)
                               sol = 3, terminal reporting only on request
                               par = 1 none, 2 space, 3 mark, 4 odd, 5 even
                               nbits = 1 (8 bits/char), 2 (7 bits/char)
                               xspeed,rspeed = transmit & receive speed index
  0,8,16,24,32,40,48,56,64,72,80,88,96,104,112,120 correspond to speeds of
  50,75,110,134.5,150,200,300,600,1200,1800,2000,2400,3600,4800,9600,19200 baud
                               clkmul = 1 (clock rate multiplier is 16)
                               flags = 0-15 (Setup Block #5), always 0 here
 ESC [ 2; Ps y  DECST          *Confidence tests - not supported
                SCS            Select character sets.
 ESC ( A        SCS            G0 points to UK symbols
 ESC ) A        SCS            G1 points to UK symbols
 ESC ( B        SCS            G0 points to ASCII symbols
 ESC ) B        SCS            G1 points to ASCII symbols
 ESC ( 0        SCS            G0 points to special (line drawing) graphics
-
 MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 163
-
 ESC ) 0        SCS            G1 points to special (line drawing) graphics
 ESC ( 1        SCS            *G0 points to alt char ROM - not supported
 ESC ) 1        SCS            *G1 points to alt char ROM - not supported
 ESC ( 2        SCS            *G0 points to alt graphics ROM - not supported
 ESC ) 2        SCS            *G1 points to alt graphics ROM - not supported
0XG             BELL           Sound VT102 style beep
 XH             BS             Backspace, move cursor left one character
 XI             HT             Horizontal tab, move cursor to next tabstop
 XJ             LF             Linefeed, move cursor down one line
 XL             FF             Formfeed, treated as a line feed
 XM             CR             Carriage return, move cursor to col 1
 XN             SO             Invoke usage of G1 character set
 XO             SI             Invoke usage of G0 character set
0Other extensions:
 ESC [ ? 6 h  ESC [ 25; Pc f   VT52/VT100 move cursor to 25th line.
 ESC [ ? 6 h  ESC [ 25; Pc H   VT52/VT100 move cursor to 25th line.
                               (These will disable Kermit's own status line.)
 ESC * char                    VT200 series graphics command, ignored.
-
-
-
-
-
-
-
-
-
-
-
-                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1164                                                 Kermit File Transfer Package
-
 7.5.3.  DEC VT102 Functions while in VT52 Mode
0Escape seq                    Description of action
 ESC A                         Cursor up
 ESC B                         Cursor down
 ESC C                         Cursor right
 ESC D                         Cursor left
 ESC F                         Enter graphics mode
 ESC G                         Exit graphics mode
 ESC H                         Cursor home
 ESC I                         Reverse line feed
 ESC J                         Erase to end of screen
 ESC K                         Erase to end of line
 ESC Y row column              Direct cursor address, offset from space
 ESC Z                         Identify (response is ESC / Z)
 ESC =                         Enter alternate keypad mode
 ESC >                         Exit alternate keypad mode
 ESC <                         Enter ANSI mode (changes to VT102)
-
-
-
-
-
-
-
-
-
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 165
-
 7.5.4.  Heath-19 Functions
-Heath-19 Functions while in Non-ANSI Mode
0Escape seq     Mnemonic       Description of action
 ESC A          HCUU           Cursor Up
 ESC B          HCUD           Cursor Down
 ESC C          HCUF           Cursor Forward, can jump to next line
 ESC D          HCUB           Cursor Backward, can jump to previous line
 ESC E          HCD            Clear display
 ESC F          HEGM           Enter Graphics mode
 ESC G          HXGM           Exit Graphic mode
 ESC H          HCUH           Cursor Home
 ESC I          HRI            Reverse Index
 ESC J          HEOP           Erase to end of page
 ESC K          HEOL           Erase to end of line
 ESC L          HIL            Insert line
 ESC M          HDL            Delete line
 ESC N          HDCH           Delete character
 ESC O          HERM           Exit Insert Char mode
 ESC Y row col  HDCA           Direct cursor addressing, offset from space
 ESC Z          HID            Identify (responds ESC / K  which is a VT52)
 ESC b          HBD            Erase Beginning of display
 ESC j          HSCP           Save cursor position
 ESC k          HRCP           Set cursor to saved position
 ESC l          HEL            Erase entire line
 ESC n          HCPR           Cursor Position Report request
 ESC o          HEBL           Erase beginning of line
 ESC p          HERV           Enter Reverse Video mode
 ESC q          HXRV           Exit Reverse Video mode
 ESC r Bn       HMBR           *Modify baud rate - not supported
 ESC t          HEKS           *Enter Keypad shifted mode, not supported
 ESC u          HXKS           *Exit Keypad shifted mode, not supported
 ESC v          HEWA           Wrap around at end of line
 ESC w          HXWA           Discard at end of line
 ESC x Ps       HSM            Set Mode. See table below
 ESC y Ps       HRM            Reset Mode. See table below
0        Ps     Mnemonic       Mode           Set            Reset
         1      HSM/HRM        25th line      enabled        disabled
         2                     *keyclick      off            on
         3                     *holdscreen    enabled        disabled
         4                     cursor type    block          underl.
         5                     *cursor on/off on             off
         6                     *keypad shifted  shifted      unshifted
         7                     alt app keypad  enabled       disabled
         8                     *linefeed      CR=CRLF        just CR
         9                     newline mode   enabled        disabled
0ESC z          HRAM           Reset to power-up configuration
 ESC =          HAKM           Enter Alternate Keypad mode
-
                                        Section 7 -- MS-DOS Kermit for the IBM-PC
1166                                                 Kermit File Transfer Package
-
 ESC >          HXAM           Exit Alternate Keypad mode
 ESC <          HEAM           Enter ANSI mode (ESC [ stuff)
 ESC @          HEIM           Enter Insert Char mode
 ESC [          HEHS           *Enter Hold Screen mode, not supported
 ESC \          HXHS           *Exit Hold Screen mode, not supported
 ESC $ and     HEK, HDK       *Keyboard enable/disable, not supported
 ESC ]          HX25           *Transmit 25th line, not supported
 ESC #          HXMP           *Transmit page, not supported
-Heath-19 Functions while in ANSI Mode
0Escape Seq     Mnemonic       Description of Action
 ESC [ s        PSCP           Save cursor position & attributes
 ESC [ u        PRCP           Restore cursor position & attributes
 ESC [ z        PRAM           Reset to power-up configuration
 ESC [ 2 J      ED             Erase entire screen but do not move cursor;
                               regular Heath-19 moves cursor to Home.
 ESC [ ? 2 h    PEHM           Revert to normal Heath-19 non-ANSI mode
 ESC [ > Ps h   SM             Same as ESC x Ps
 ESC [ > Ps l   RM             Same as ESC y Ps
0Plus most of the ANSI escape sequences listed for the VT102.
-
-
-
-
-
-
-
-
-
-
-MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 167
-
 7.6.  Installing MS-DOS Kermit on a Fixed Disk
-The NIH Computer Center supplied diskette contains a file (named  READ.ME)  with
 instructions  for  installing  MS-DOS  Kermit  on  a fixed disk.  To display the
 instructions, issue the DOS command:  TYPE A:READ.ME.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0                                       Section 7 -- MS-DOS Kermit for the IBM-PC
1168                                                 Kermit File Transfer Package
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0MS-DOS Kermit for the IBM-PC-- Section 7
1Kermit File Transfer Package                                                 169
-
 8.  APPLE-DOS Kermit
-Kermit-A2 Capabilities At A Glance:
0  Local operation:                   Yes
   Remote operation:                  Yes
   Transfers text files:              Yes
   Transfers binary files:            Yes
   Wildcard send:                     No
   XX/XY interruption:                Yes
   Filename collision avoidance:      Yes
   Can time out:                      Yes
   8th-bit prefixing:                 Yes
   Repeat count prefixing:            No
   Alternate block checks:            No
   Terminal emulation:                Yes (VT52)
   Communication settings:            Yes; local echo, parity
   Transmit BREAK:                    Yes
   IBM communication:                 Yes
   Transaction logging:               No
   Session logging (raw download):    No
   Raw upload:                        No
   Act as server:                     No
   Talk to server:                    Yes
   Advanced commands for servers:     No
   Local file management:             Yes
   Handle file attributes:            No
   Command/init files:                No
   Printer control:                   No
0KERMIT-A2 is a program that implements the Kermit file transfer protocol for the
 Apple  ][  microcomputer  system.   It  is written in 6502 assembly language and
 should run on any Apple ][, Apple ][ Plus, Apple //e,  enhanced  Apple  //e,  or
 Apple  //c  system  running  DOS 3.3.  This section will describe the things you
 should know about the DOS 3.3 file system in order  to  make  effective  use  of
 KERMIT, and then it will describe the special features of the KERMIT-A2 program.
-
-
-
-
-
-
                                   Section 8 -- APPLE-DOS Kermit for the Apple ][
1170                                                 Kermit File Transfer Package
-
 8.1.  The DOS 3.3 File System
0Items of importance which will be discussed in this  section  include  Filenames
 and File Characteristics.
0Apple DOS Filenames
0Filenames under Apple DOS may contain  almost  any  ASCII  character  (including
 space).    It  is  not  recommended  that  special  characters,  (i.e.,  control
 characters or spaces) be used in a filename to be transferred by Kermit-A2 since
 they may cause problems when parsing the filename.
0Filenames may be up to 30 characters in length and must begin with a letter.  No
 wildcarding of any kind can be done in KERMIT-A2.
-Apple DOS File Characteristics
0All files in Apple DOS have a file type associated with them which is  contained
 in  the  directory  entry  for  the file but is not part of the filename itself.
 There are four types of files in DOS 3.3.  They are:
0   - APPLESOFT BASIC
0   - INTEGER BASIC
0   - BINARY
0   - TEXT
0All file types have their data stored in eight-bit bytes  although  not  all  of
 them need the eighth bit.  The two file types containing BASIC programs required
 the eighth bit due to the nature of the data being  stored.   BINARY  files  are
 images  of  memory  copied into a file.  Often, these are machine code programs.
 These files require all eight bits.  TEXT files normally contain only  printable
 or  carriage control characters.  They are stored in the form of seven-bit ASCII
 characters but the eighth bit should always be set since Apples  manipulate  all
 text internally as 'NEGATIVE ASCII'.
0When transmitting text files, the byte size should be set  to  seven-bit.   When
 transmitting  anything else, the user must insure that both Kermits are handling
 eight bit data so that no information is lost.  If an eight-bit data path is not
 available  (i.e.,  the  remote Kermit needs to do parity checking with the eigth
 bit), then eight-bit quoting should be used.  Of course, BINARY files as well as
 Apple BASIC files will not have much meaning on a different system.  If the user
 desires to edit a BASIC file on a mainframe, for instance, he must convert it to
 a TEXT file before sending it over.  After receiving the file back on the Apple,
 the user may convert it back to BASIC once again.  The reason BASIC files  would
 be meaningless to a different machine is that the Apple stores BASIC keywords as
 single character tokens to save space and processing time.  To convert  a  BASIC
 program to and from a TEXT file, consult the Apple DOS 3.3 Manual.
-
0APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 171
-
 File information can be obtained by issuing the CATALOG command.  For example:
0  ]CATALOG
0   DISK VOLUME 010
      *A 002 HELLO
       B 078 KERMIT
       A 002 READER
       T 005 TESTFILE
0  ]
0When KERMIT-A2 is receiving a file, the file it creates on the diskette will  be
 of  the type indicated by the FILE-TYPE parameter.  The file will always be left
 in an unlocked state after it is closed by  KERMIT-A2.   When  sending  a  file,
 KERMIT-A2  will  use  the  FILE-TYPE  parameter  to  determine  how to detect an
 End-of-file condition.  Thus, it is important to have this set properly  in  all
 cases.
-Recommendations for Archiving Files
0When using a large system for archiving purposes, there is no reason to  convert
 Apple  Basic programs into text files before sending them since there is no need
 to edit them on the mainframe.
0The FILE-TYPE parameter must always be set correctly when sending and  receiving
 files.   Also,  when  sending  files  which  require  eight-bit BYTE-SIZEs, this
 parameter must  also  be  set  properly  since  KERMIT-A2  does  not  change  it
 automatically based on FILE-TYPE.
0The procedure for archiving TEXT files is:
0   - Run Kermit on remote system
0   - SET BYTE-SIZE 7-BIT ! On KERMIT-A2
0   - SET FILE-TYPE TEXT ! On KERMIT-A2
0   - Send files
0The procedure for archiving APPLESOFT, INTEGER, and BINARY files is:
0   - Run Kermit on remote system
0   - Set File-byte-size to Eight-bit (On Remote Kermit)
0   - SET BYTE-SIZE 8-BIT (On KERMIT-A2)
0   - SET FILE-TYPE APPLESOFT (or INTEGER, or BINARY) On KERMIT-A2
0   - Send files
-
                                   Section 8 -- APPLE-DOS Kermit for the Apple ][
1172                                                 Kermit File Transfer Package
-
 8.2.  Program Operation
-                            Hardware Considerations
0Computer
0KERMIT-A2 is designed to be used with the Apple ][ series of computers  with  at
 least  64k  of  memory.   It  has  been  tested  on  an  Apple //e with a normal
 (non-extended) 80-column card, an enhanced Apple //e, an Apple  //c,  and  on  a
 Apple  ][+  with  a language card.  It may work on Franklin computers, though it
 has not been tested on them.
0Operating System
0KERMIT-A2 reads and writes standard DOS 3.3 files  to  and  from  disk.   ProDOS
 files  must be converted to DOS 3.3 before they can be transferred.  It will NOT
 work under Apple CPM.  KERMIT-A2 is  distributed  on  a  disk  that  contains  a
 high-speed  operating  system  called Diversi-DOS(tm), which is licensed for use
 with this program only.  To legally use Diversi-DOS with other programs, you may
 send $30.00 directly to :
0                  DSR, Inc.,
                   34880 Bunker Hill,
                   Farmington, MI  48018.
0You will receive a Diversi-DOS utility disk with documentation.
080 Column Cards
0The only 80-column card supported is the Apple card that  comes  with  the  //e.
 Very  little  of  the  80-column programming in KERMIT-A2 is card-dependent, but
 other cards have not been tested.
0Serial Interface Cards for Modem Connection
0KERMIT-A2 will support the following serial interface cards:
01. D.C. Hayes MICROMODEM ][ (also works for SSM, should work for
    D.C. Hayes MICROMODEM //e)
02. Apple Super Serial card (also works for Practical Peripherals
    SERIALL)
0Most switch settings on these cards are irrelevant to Kermit.  However,  if  you
 plan  to  SET  INTERRUPT-USAGE  ON (a must above 300 bits per second) you should
 make sure that any  switch  governing  interrupts  is  set  ON  (the  Micromodem
 requires a solder joint or jumper to make interrupts possible).
0It is possible that  other  cards  may  have  operational  characteristics  very
 similar  or  identical to one of the devices above.  If this is the case, it may
-
0APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 173
-
 work using one of the currently available device drivers.  The user may want  to
 try each of the above options to see if any of them work.
0KERMIT-A2 must be told which device is being used so that it may  run  with  the
 correct  device  driver.   It  also must be told in which slot the card resides.
 This may be done with the 'SET SLOT' command (documented below).
0General Configuration
0It is assumed that you have at least one disk drive (used for booting the Kermit
 disk)  connected  to a disk-controller card mounted in slot 6 (the usual).  Your
 serial interface (or modem) card can be in any slot.
-                           Conversing with Kermit-A2
0KERMIT-A2's prompt is "KERMIT-A2>."
0To run KERMIT-A2 and issue commands to it, type the following:
-  ]BRUN KERMIT
0      APPLE-II KERMIT (VERSION 1.0)
0  KERMIT-A2>SEND TESTFILE
0  file is sent
0  KERMIT-A2>STATUS
0  performance statistics are printed
0  KERMIT-A2>Other commands
                   .
                   .
                   .
0  KERMIT-A2>EXIT
   ]
0KERMIT-A2 uses a TOPS-20 style command parser.
0During interactive operation, you may use the ?-prompting help feature ("?") and
 recognition  (ESC) features while typing commands.  A question mark typed at any
 point in a command displays the options available at that point; typing  an  ESC
 character  causes  the  current  keyword to be completed (or default value to be
 supplied).  If you have not typed sufficient characters to uniquely specify  the
 keyword  or  filename  (or  if  there  is  no default value) then a beep will be
 sounded and you may continue typing.  Keywords may be abbreviated to any  prefix
 that  is  unique.   Control-W  erases  the  last word you have typed.  Control-U
 erases the entire line that you have typed.
-
                                   Section 8 -- APPLE-DOS Kermit for the Apple ][
1174                                                 Kermit File Transfer Package
-
 8.3.  Remote and Local Operation
0KERMIT-A2 is normally run in local mode.  It may be run as a  remote  Kermit  as
 well  although  there  is  no  advantage  to  doing  things that way.  KERMIT-A2
 supports User-mode commands for talking to a  Server.   It  does  not  currently
 operate as a remote server.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 175
-
 8.4.  KERMIT-A2 Commands
-                            The SEND Command
0Syntax:  SEND filespec
0The SEND command causes a file to be sent from the Apple to the  remote  system.
 The  filespec  is  the  name  of the file on the Apple diskette to be sent.  The
 parser will not accept control characters and certain special  characters  in  a
 filename  (i.e.,  a comma), so the user may have to rename the file before it is
 sent.  The user may also have problems in  filename  compatibility  with  remote
 Kermits.  If the remote Kermit does not have the facilities to beat the filename
 into a format that its system likes, the user may have to rename the file before
 sending it.  The default disk drive used for file transfers is the drive used to
 boot the system or the last drive accessed with a  DOS  command.   This  can  be
 changed  with the 'SET DEFAULT-DISK' command (explained below).  Either the slot
 or the drive or both may be altered.
0As a file is being sent, the screen  displays  either  'SENDING  PACKET...'   or
 'WAITING  PACKET...'   followed  by  the  absolute  packet number since start of
 transmission.  If a packet must be transmitted several times and it reaches  the
 maximum  retry  count,  the  transfer will fail and the 'KERMIT-A2>' prompt will
 return.  If the remote Kermit sends an error packet, the text of the packet will
 be displayed on the screen and the prompt will return.
0Currently, a packet can be retransmitted manually  by  typing  anything  on  the
 keyboard.  If a 'Q' is typed, the entire transmission will be aborted.
-                              The RECEIVE Command
0Syntax:  RECEIVE [filespec]
0The RECEIVE command tells KERMIT-A2 to receive a file or  file  group  from  the
 other  system.  If only one file is being received, you may include the optional
 filespec as the name to store the incoming file under; otherwise,  the  name  is
 taken  from  the incoming file header.  If the name in the header is not a legal
 filename in DOS 3.3, KERMIT-A2 will attempt to change it into  something  legal.
 There  are very few things that are illegal in DOS 3.3.  If WARNING is on and an
 incoming file has a name identical to a file already existing on  the  diskette,
 KERMIT-A2 will issue a warning to the user and attempt to modify the filename to
 make it unique.
-                                The GET Command
0Syntax:  GET remote-filespec
0The GET command requests a remote Kermit server to send the file or  file  group
 specified  by remote-filespec.  This command can be used with a Kermit server on
 the other end.
-
                                   Section 8 -- APPLE-DOS Kermit for the Apple ][
1176                                                 Kermit File Transfer Package
-
 The remote filespec is any string that can be a legal file specification for the
 remote system; it is not parsed or validated locally.
0If the remote Kermit is not capable of server functions, then you will  probably
 get an error message back from it like "Illegal packet type."  In this case, you
 must connect to the other Kermit, give a SEND command, escape back, and  give  a
 RECEIVE command.
-                          The CONNECT Command
0Syntax:  CONNECT
0Establish a terminal connection to the remote system.  Get back to KERMIT-A2  by
 typing  the  escape  character followed by the letter C. The escape character is
 Control-E  by  default.   When  you   type   the   escape   character,   several
 single-character commands are possible:
0  B   Send a BREAK Signal.
   C   Close the connection and return to KERMIT-A2.
   H   Hang up the communications interface (drops phone connection)
   S   Show status of the connection.
   0   Send a null.
   Connect-escape
       Send the Connect-escape character itself.
   ?   List all the possible single-character arguments.
0You can use the SET ESCAPE-CHARACTER to define a different escape character.
0When 'CONNECTED', KERMIT-A2 will be passing characters entered on  the  keyboard
 to the remote system, and passing characters from the remote system to the Apple
 screen.  If VT52-EMULATION is turned on,  Kermit  will  trap  escape  codes  and
 simulate the appropriate functions of a VT52 terminal.
-                            The HELP Command
0Syntax:  HELP
0Displays a brief summary of KERMIT-A2 and its commands.
-                       The EXIT and QUIT Commands
0Syntax:  EXIT
0Exit from KERMIT-A2.  You can restart the  program,  provided  you  haven't  run
 anything else, by typing 'CALL 2049'.
0Syntax:  QUIT
0This is merely a synonym for EXIT.
-
 APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 177
-
                                 The SET Command
0Syntax:  SET parameter [option] [value]
0Establish or modify various parameters for file transfer or terminal connection.
 You  can  examine  their values with the SHOW command.  The following parameters
 may be SET:
0         BAUD-RATE  Communications interface line speed.
          BYTE-SIZE  SEVEN or EIGHT significant bits in a byte.
          DEBUGGING  TERSE or VERBOSE packet information.
       DEFAULT-DISK  Disk drive and slot used for file transfer?
      DEVICE-DRIVER  Which communication device is being used?
  EIGHT-BIT-QUOTING  Should eight-bit-quoting be used?
          EMULATION  Should Apple emulate full-screen terminal?
   ESCAPE-CHARACTER  Character for terminal connection.
          FILE-TYPE  Of Apple DOS file being sent/received.
           IBM-LINE  Should Apple wait for IBM turnaround character?
    INTERRUPT-USAGE  Can serial interface card handle interrupts?
             KBOARD  Type of Apple keyboard.
     KEY-SUBSTITUTE  Used to translate individual characters.
           LINEFEED  Should Apple send linefeed with carriage return?
         LOCAL-ECHO  Specify which host does echoing during CONNECT.
 LOWER-CASE-DISPLAY  How lower case characters are displayed on Apple.
             PARITY  Character parity to use.
            RECEIVE  Various parameters for receiving files.
            RETRIES  Specify maximum number of retries allowed.
             SCREEN  Specify width of screen.
               SEND  Various parameters for sending files.
               SLOT  Which slot # is communication device in?
              SOUND  Should Kermit ring the bell?
      TERMINAL-TYPE  Type of full-screen terminal to emulate.
            WARNING  Warn users if incoming file exists.
-SET BAUD-RATE
0Syntax:  SET BAUD-RATE rate
0Set the line speed of the serial interface card to 300,  1200,  2400,  4800,  or
 9600 bits per second.
-
-
-
-
-                                  Section 8 -- APPLE-DOS Kermit for the Apple ][
1178                                                 Kermit File Transfer Package
-
 SET BYTE-SIZE
0Syntax:  SET BYTE-SIZE parameter
0Byte size for Apple DOS file I/O.  The choices are 7-bit or 8-bit.
07-BIT    When sending a file, shut the H.O. bit.  When receiving, turn the  H.O.
          bit  on.  This is done since text files are the only files which should
          be sent as SEVEN-BIT files and text files only make sense to the  Apple
          if they are encoded in 'negative ascii' values.
08-BIT    Always send and receive the bytes intact.  All 8 bits are significant.
-SET DEBUGGING
0Syntax:  SET DEBUGGING options
0Record the packet traffic on your terminal.  Options are:
0TERSE            Show packet info only (brief).
0VERBOSE          Display packet field descriptions with packet info (lengthy).
0OFF              Don't display debugging information (this is the default).
-SET DEFAULT-DISK
0Syntax:  SET DEFAULT-DISK parameter value
0This command will tell KERMIT-A2 which  disk  drive  should  be  used  for  file
 transfers.   The  two parameters which may be set separately are SLOT and DRIVE.
 The value for SLOT ranges from 1 to 7.  The value for DRIVE is either 1 or 2.
-
-
-
-
-
-
-
 APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 179
-
 SET DEVICE-DRIVER
0Syntax:  SET DEVICE-DRIVER keyword
0This command will tell KERMIT-A2 what type  of  communication  device  is  being
 used.  Currently, four different cards are supported, however, other unsupported
 cards may work similar enough to one of the  three  available  that  it  may  be
 possible  to  use  them.   KERMIT-A2  must also be told where the card is in the
 machine (see the SET SLOT command).  The options for this set command are:
0APPLE-COM        The old Apple communication card (300 bits per second).   Note:
                  This  device  driver  has  not  been  tested  and  may not work
                  properly.
0MICROMODEM       The  D.C.  Hayes  Micromodem  ][  (300  bits  per  second)  and
                  Micromodem //e (300 and 1200 bits per second).
0SSM              SSM A10 serial interface card.
0SUPER-SERIAL     The Apple Super Serial Card (300-19.2 bits per  second).   Also
                  works for Practical Peripherals SERIALL.
0NOVATION-CAT     Novation Apple Cat ][ (300 and 1200 bits  per  second).   Note:
                  This  device  driver  has  not  been  tested  and  may not work
                  properly.
-SET EIGHT-BIT-QUOTING
0Syntax:  SET EIGHT-BIT-QUOTING ON or OFF
0This command will turn on or turn off the eight-bit-quoting feature.  If set ON,
 it  forces  KERMIT-A2  to  use  eight-bit-quoting  which may be handy if it must
 receive a text file in which some or all of the characters are not  in  negative
 ASCII.  The command takes ON or OFF as options.
-SET EMULATION
0Syntax:  SET EMULATION ON or OFF
0Specify  whether  KERMIT-A2  should  use  its  built-in  software  facility  for
 emulating a full-screen terminal.  If EMULATION is ON, the type of terminal must
 be specified by the SET TERMINAL-TYPE command.
-
-
-
-                                  Section 8 -- APPLE-DOS Kermit for the Apple ][
1180                                                 Kermit File Transfer Package
-
 SET ESCAPE-CHARACTER
0Syntax:  SET ESCAPE-CHARACTER hexadecimal-number
0Specify  the  control  character  you  want  to  use  to  "escape"  from  remote
 connections back to KERMIT-A2.  The default is 5 (Control-E).  The number is the
 hex value of the ASCII control character, 1 to 37, for instance 2 is Control-B.
-SET FILE-TYPE
0Syntax:  SET FILE-TYPE keyword
0This will inform KERMIT-A2 what type of DOS file is being sent or received.   It
 is  important  that  this is set correctly since KERMIT-A2 must create a file of
 the appropriate type when receiving (and it has no way of knowing what  kind  of
 file  it  is).   When  KERMIT-A2  is sending, it must also know the type of file
 since that tells it how to detect the actual end-of-file.  The options for  this
 parameter are APPLESOFT, INTEGER, TEXT and BINARY.
0APPLESOFT The file being sent/received is an Applesoft Basic program.
0  INTEGER The file being sent/received is an Integer Basic program.
0     TEXT The file being sent/received is an ASCII Text file.
0   BINARY The file being sent/received is a Binary image.
-
 SET IBM-LINE
0Syntax:  SET IBM-LINE ON or OFF
0When set to ON, KERMIT-A2 will wait  for  the  IBM  turnaround  character  (XON,
 CTRL-Q)  before  sending any characters to the other Kermit.  Note:  This option
 must be set to OFF when used with either TSO Kermit or DECsystem-10 Kermit.
-SET INTERRUPT-USAGE
0Syntax:  SET INTERRUPT-USAGE ON or OFF
0When set to  ON,  it  indicates  that  the  serial  interface  card  can  handle
 interrupts (a must above 300 bits per second).  Before setting it ON, you should
 make sure that any  switch  governing  interrupts  is  enabled  (the  Micromodem
 requires a solder joint or jumper to make interrupts possible).
-SET KBOARD
0Syntax:  SET KBOARD parameter keyword
-
 APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 181
-
 This command will tell KERMIT-A2 what type  of  keyboard  is  being  used.   The
 allowable options are:
02P   Apple ][+ or Apple ][.
02S   Apple ][ or ][+ with shift-key modification.
02E   Apple //e.
02C   Apple //c or enhanced Apple //e.
0On an Apple ][ or ][+ with an incomplete keyboard,  special  characters  can  be
 obtained by prefixing regular characters with a right-arrow.  Also, uppercase is
 shown in inverse and lowercase characters  are  displayed  as  normal  uppercase
 characters.
0Here are the rules for using the special Apple ][  or  ][+  input,  to  get  all
 printable ASCII characters, and how they appear on the screen:
0Special meanings are applied in various contexts  to  certain  characters.   The
 left  and  right arrow keys do special things, and sometimes the escape key does
 as well.
0For letters, the keyboard is always in either default UPPERCASE mode or  default
 lowercase mode.  When in UPPERCASE, all letters typed are sent out as uppercase.
 In lowercase, all letters are sent out as lowercase.  To reverse  the  case  for
 the  next  character  only,  hit  the right-arrow ("prefix") key.  To switch the
 default case, hit the prefix-key twice in a row.
0For funny characters, the prefix key is also used to get the unusual punctuation
 characters  which  are not on the Apple keyboard.  Here they are:  (To represent
 the right-arrow prefix character, we are using the letter p).
0To get                   Type        Appearance
0Left Square Bracket      p(          [
 Right Square             p)          ]
 Left Curly Bracket       p<          $
 Right Curly Bracket      p>          
 Underline                p-          _
 Backslash                p/          \
 Tilde (wiggle)           pX          ~
 Vertical Line            p.          |
 At-sign                  p"          @
0The left-arrow key sends a rubout.
0With left-arrow and right arrow doing special things, it is  a  little  hard  to
 enter  their  characters  (Control-H  and  Control-U  respectively).   There  is
 therefore an escape from prefix mode sequence.  If you type prefix-ESC, the next
 character is sent without any interpretation.
-
0                                  Section 8 -- APPLE-DOS Kermit for the Apple ][
1182                                                 Kermit File Transfer Package
-
 SET KEY-SUBSTITUTE
0Syntax:  SET KEY-SUBSTITUTE old-number new-number
0This command may be used to tell KERMIT-A2 to  transmit  a  different  character
 each  time  a particular key is pressed.  For example, the command could be used
 to transmit the letter "B" each time the "A" key was pressed.  The first  number
 in the command (i.e., "old number") , specifies the decimal value (between 0 and
 127) of the ASCII character to be translated.  The second number in the command,
 (i.e., "new number"), specifies the decimal value of the ASCII character that is
 to be transmitted.  If the second number does not have the high  order  bit  set
 (i.e.,  the  number  is  less  than 128), then the character transmitted will be
 prefixed by an escape.  For example, the command:
0    SET KEY-SUBSTITUTE 65 194
0would send "B" (decimal 194) whenever the "A"  (decimal  65)  key  was  pressed.
 Similarly, the command:
0    SET KEY-SUBSTITUTE 35 36
0would send ESCAPE "$" (decimal  36)  whenever  the  "#"  (decimal  35)  key  was
 pressed.
-SET LINEFEED
0Syntax:  SET LINEFEED ON or OFF
0When set to ON, KERMIT-A2 will send a linefeed after each carriage return.
-SET LOCAL-ECHO
0Syntax:  SET LOCAL-ECHO ON or OFF
0Specify how characters are echoed  while  CONNECTed  to  a  remote  system.   ON
 specifies  that  characters  are  to be echoed by KERMIT-A2 (because neither the
 remote computer nor the communications circuitry has been  requested  to  echo),
 and is appropriate for half-duplex connections.
-
-
-
-
-
 APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 183
-
 SET LOWER-CASE-DISPLAY
0Syntax:  SET LOWER-CASE-DISPLAY keyword
0Specify how lower case characters are to  be  displayed  while  CONNECTED  to  a
 remote system.  The allowable options are:
0INVERSE-UPPER  Upper case letters are displayed in  normal  upper  case.   Lower
                case  letters  are  displayed in inverse upper case.  By default,
                the keyboard is in the lower case mode.
0LOWER-CASE     All characters are displayed in  the  proper  case.   Upper  case
                letters  are  displayed  in normal upper case, lower case letters
                are displayed in normal lower case.  On an Apple ][ or ][+,  this
                option  requires  a lower case adaptor.  By default, the keyboard
                is in the lower case mode.
0NORMAL-UPPER   Upper case letters are displayed in inverse  upper  case.   Lower
                case letters are displayed in normal upper case.  By default, the
                keyboard is in the lower case mode.
0SAME-AS-UPPER  Both upper and lower case letters are displayed in  normal  upper
                case.  By default, the keyboard is in the lower case mode.
-SET PARITY
0Syntax:  SET PARITY keyword
0This command determines the type of parity to use on the transmission line.  The
 options for this parameter are EVEN, MARK, NONE, ODD, or SPACE.
-
-
-
-
-
-
-
-
                                   Section 8 -- APPLE-DOS Kermit for the Apple ][
1184                                                 Kermit File Transfer Package
-
 SET RECEIVE
0Syntax:  SET RECEIVE parameter value
0Parameters to request or expect for incoming packets, as follows:
0EIGHT-BIT-QUOTE-CHAR hexadecimal-number
0          Sets the character to be used  to  quote  characters  which  have  the
           eighth bit (parity bit) set.  This is used to transfer eight-bit bytes
           on a transmission medium which only supports  seven  data  bits.   The
           default value is 26 (ASCII "&").
0END-OF-LINE hexadecimal-number
0          Carriage return (ASCII 0D hex) by default.
0PACKET-LENGTH number
0          Maximum length packet for the other  side  to  send,  decimal  number,
           between 10 and 94, decimal.
0PADDING number, PAD-CHAR hexadecimal-number
0          How many padding characters to request before  each  incoming  packet,
           and  what  the  padding  character should be.  No Kermits are known to
           need padding; and if one did, it would request it without your  having
           to tell it to do so.  This command would only be necessary, therefore,
           under very unusual circumstances.
0QUOTE-CHAR hexadecimal-number
0          What printable character to use for quoting of control characters, "#"
           (ASCII 23 hex) by default.  There should be no reason to change this.
0TIMEOUT number
0          How many seconds the other Kermit should  wait  for  a  packet  before
           asking for re-transmission.
-SET RETRIES
0Syntax:  SET RETRIES number
0How many times to try sending a particular packet before giving up.  If  a  line
 is very noisy, you might want to increase this number.
-
-
-APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 185
-
 SET SCREEN
0Syntax:  SET SCREEN keyword
0This command determines if the screen display is to be in 40 column mode  or  80
 column mode.  The options for this parameter are 40 or 80.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0                                  Section 8 -- APPLE-DOS Kermit for the Apple ][
1186                                                 Kermit File Transfer Package
-
 SET SEND
0Syntax:  SET SEND parameter value
0Parameters for outgoing packets, as follows:
0EIGHT-BIT-QUOTE-CHAR hexadecimal-number
0          Sets the character to be used  to  quote  characters  which  have  the
           eighth bit (parity bit) set.  This is used to transfer eight-bit bytes
           on a transmission medium which only supports  seven  data  bits.   The
           default value is 26 (ASCII "&").
0END-OF-LINE hexadecimal-number
0          The ASCII character to be used  as  a  line  terminator  for  outbound
           packets,  if  one  is required by the other system, carriage return by
           default.  You will only have to use  this  command  for  systems  that
           require a line terminator other than carriage return.
0PACKET-LENGTH number
0          Maximum  packet  length  to  send,  between  10  and   94   (decimal).
           Shortening the packets might allow more of them to get through without
           error on noisy communication lines.  Lengthening the packets increases
           the throughput on clean lines.
0PADDING number, PAD-CHAR hexadecimal-number
0          How much padding to send before a packet,  if  the  other  side  needs
           padding,  and  what  character  to  use  for padding.  Defaults are no
           padding, and NUL (0) for the padding character.  This command is  also
           handy  for  inserting  special  characters  that  may  be  required by
           communications equipment.
0QUOTE-CHAR hexadecimal-number
0          What printable character to use for  quoting  of  control  characters,
           "#,"  (ASCII  23 hex) by default.  There should be no reason to change
           this.
0TIMEOUT number
0          How many seconds to wait for a packet before trying again.  A value of
           zero means don't time out -- wait forever.
-SET SOUND
0Syntax:  SET SOUND ON or OFF
0Specify whether KERMIT-A2 should ring the bell to get users attention.
-
 APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 187
-
 SET TERMINAL-TYPE
0Syntax:  SET TERMINAL-TYPE keyword
0This command determines the  type  of  full-screen  terminal  to  emulate.   The
 allowable options are:
0    VCA    Emulate Volker-Craig 4404 terminal in its ADM-3A
            operating mode.
0    VT52   Emulate DEC VT52 terminal.
-SET SLOT
0Syntax:  SET SLOT parameter
0This option tells KERMIT-A2 in which slot the communication device  is  located.
 The range for the parameter is 1-9.
-SET WARNING
0Syntax:  SET WARNING ON or OFF
0This  tells  KERMIT-A2  whether  to  warn  the  user  about  incoming  filenames
 conflicting with existing files or not.
-
                             The SHOW Command
0Syntax:  SHOW option
0The SHOW command displays the values of  the  parameters  settable  by  the  SET
 command.  In addition, if ALL is specified, a complete display of all parameters
 will be provided.
-                           The STATUS Command
0Syntax:  STATUS
0Give statistics about the most recent file transfer.  This includes  information
 such   as   number  of  characters  sent/received,  number  of  data  characters
 sent/received, and last error encountered.
-
-
-
                                   Section 8 -- APPLE-DOS Kermit for the Apple ][
1188                                                 Kermit File Transfer Package
-
                            The BYE Command
0Syntax:  BYE
0Shut down the remote server and exit from KERMIT-A2.
-                         The CATALOG Command
0Syntax:  CATALOG
0Ask DOS to show a list of files on the disk in the DEFAULT-DISK
-                         The COMPARE Command
0Syntax:  COMPARE filespec1 filespec2
0Compares two files on the disk in the DEFAULT-DISK  drive.   If  the  files  are
 different, it gives the number and some text of the first different line and the
 first different character.
-                          The DELETE Command
0Syntax:  DELETE filespec
0Ask DOS to erase a file on the disk in the DEFAULT-DISK drive.
-
                           The FINISH Command
0Syntax:  FINISH
0Shut down the remote server, but do not exit from KERMIT-A2.
-                         The INSTALL Command
0Syntax:  INSTALL
0Writes your customized version of the KERMIT-A2 program out to a disk file named
 "KERMIT."  Ignore the FILE-NOT-FOUND message.
-                         The MONITOR Command
0Syntax:  MONITOR
0Exit from KERMIT-A2 to the Apple's System Monitor.  You can restart the  program
 by typing '801G'.
-
 APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 189
-
                           The RENAME Command
0Syntax:  RENAME old-filespec,new-filespec
0Ask DOS to rename a file on the disk in the DEFAULT-DISK drive.
-                           The TYPE Command
0Syntax:  TYPE filespec
0Displays a text file.  KERMIT-A2 pauses  after  the  first  line  is  displayed.
 Pressing carriage return will start a continuous scroll.  Pressing any key other
 than carriage return will stop scroll and display one line per key press.
-
-
-
-
-
-
-
-
-
-
-
-
-
-                                  Section 8 -- APPLE-DOS Kermit for the Apple ][
1190                                                 Kermit File Transfer Package
-
 8.5.  Matching KERMIT-A2 to Your System
0Changing a few settings in the program  will  probably  be  necessary  to  match
 KERMIT-A2  to  your  particular  system.  It is unlikely that all of the default
 settings (those available when you first load KERMIT-A2) are the ones  you  will
 be  wanting to use on a regular basis.  This process of customizing KERMIT-A2 to
 your needs, which eliminates the need for typing in the settings every time  you
 load the program, is known as INSTALLATION.
0The settings of all of the parameters may be displayed by typing:
0    SHOW ALL
0You will most likely  want  to  make  changes  in  parameters  related  to  your
 hardware; the commands which do this are:
0    SET BAUD-RATE
     SET DEVICE-DRIVER
     SET INTERRUPT-USAGE
     SET KBOARD
     SET LOWER-CASE-DISPLAY
     SET SCREEN
     SET SLOT
0There are many other parameters, changes in some of which may add greatly to the
 convenience  of using KERMIT-A2 in your particular situation.  These do NOT have
 to be done now.  You can make such changes whenever it becomes clear to you that
 they  would  be helpful.  If you want to have these changes available each time
 you run KERMIT-A2, then you must issue the INSTALL command  again  as  described
 below.
-
-
-
-
-
-
-
-
0APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 191
-
 When you think you have everything the way you want it, review the  settings  by
 typing:
0    SHOW ALL
0If everything looks  correct,  you  can  now  save  the  customized  version  of
 KERMIT-A2 to disk by typing:
0    INSTALL
0While the disk drives whirs, ignore the  FILE-NOT-FOUND  message.   The  INSTALL
 command writes your new version into a file named KERMIT.  If there is already a
 file named KERMIT on the disk, INSTALL will warn you and refuse to write on  the
 disk.   If this happens, you can simply rename the old file and retry INSTALL by
 typing:
0    RENAME KERMIT,OLDKERMIT
     INSTALL
0To make sure that the new KERMIT-A2 is properly configured and saved, type:
0    EXIT
0and then:
0    BRUN KERMIT
0When you get the "KERMIT-A2>" prompt again, check the settings you made above by
 typing:
0    SHOW ALL
-
-
-
-
-
-
-
-
                                   Section 8 -- APPLE-DOS Kermit for the Apple ][
1192                                                 Kermit File Transfer Package
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0APPLE-DOS Kermit for the Apple ][-- Section 8
1Kermit File Transfer Package                                                 193
-
 Appendix A -- When Things Go Wrong
0Connecting two computers can be a tricky business, and many things can go wrong.
 Before  you  can  transfer  files  at  all,  you  must  first establish terminal
 communication.  But successful terminal connection  does  not  necessarily  mean
 that  file  transfer  will  also  work.  And even when file transfer seems to be
 working, things can happen to ruin it.
-A.1.  Basic Connection Problems
0If you have a version of Kermit on your microcomputer, but the  CONNECT  command
 doesn't seem to work at all, please:
0-     Make sure all the required physical connections have been  made  and  have
       not  wiggled loose.  If you are using a modem, make sure the carrier light
       is on.
0-     If you have more than one connector on your microcomputer, make  sure  you
       are using the right one.
0-     Make sure that the port is set to the right communication speed,  or  baud
       rate.   Some  versions  of  Kermit  have  a  builtin SET BAUD or SET SPEED
       command, others require that you set the baud rate using a system  command
       or  setup  mode  before  you  start  the Kermit program.  Some versions of
       Kermit have SHOW or STATUS commands that will tell you  what  the  current
       baud rate is.
0-     Make sure that the other communication line parameters, like parity,  bits
       per character, handshake, and flow control are set correctly.
0You may have to consult the appropriate manuals for the systems and equipment in
 question.
0If all settings and connections appear to be correct,  and  communication  still
 does  not  take  place,  the fault may be in your modem.  Internal modems (i.e.,
 those that plug  in  to  a  slot  inside  the  microcomputer  chassis)  are  not
 recommended  for  use  with  Kermit  unless  they totally mimic the asynchronous
 serial port  hardware  they  purport  to  replace.   Many  microcomputer  Kermit
 programs  are written to control the communication hardware explicitly; internal
 modems can interfere with that control.
0Even external modems can cause trouble --  the  "smarter"  they  are,  the  more
 potential  danger  of disagreement between the modem and the microcomputer about
 settings of baud rate, character framing, echo, and so forth.   Make  sure  your
 modem is set up correctly.
-
-
-
                                               Appendix A -- When Things Go Wrong
1194                                                 Kermit File Transfer Package
-
 A.2.  Terminal Connection Works But The Transfer Won't Start
0Once you've made a terminal connection to the remote system, you will  generally
 also be able to transfer files.  But not always.  If Kermit's terminal emulation
 seems to work correctly, but a  file  transfer  will  not  start  at  all,  then
 something  in  the  communication  path  is probably interfering with the packet
 data.
0Kermit normally  expects  to  have  full  control  of  the  communication  port.
 However,  it  is  sometimes the case that some communications equipment controls
 the line between the two computers  on  either  end.   In  addition  to  modems,
 examples  include  port  contention  or  selection  units,  multiplexers,  local
 networks, and wide-area networks.  Such equipment can interfere with the  Kermit
 file transfer protocol in various ways:
0Parity:
0A device can impose parity upon the communication line.  This means that the 8th
 bit   of  each  character  is  used  by  the  equipment  to  check  for  correct
 transmission.  Use of parity when Kermit is not expecting it will:
0- Cause packet CHECKSUMs to appear  incorrect  to  the  receiver  and  foil  any
   attempt  at  file transfer.  In most cases, not even the first packet will get
   through.
0- Prevent the use of the 8th bit for binary file data.
0If terminal connection works but file transfer does  not,  parity  is  the  most
 likely culprit.  To overcome this impediment, you should find out what parity is
 being used, and inform the Kermits on each side (using the SET  PARITY  command)
 so that they can:
0- Compose and interpret the CHECKSUMs correctly.
0- Employ a special encoding to allow  8-bit  data  to  pass  through  the  7-bit
   communication channel.
0Many packet-switched networks, such as GTE TELENET, require parity to be set.
-
-
-
-
-
-When Things Go Wrong -- Appendix A
1Kermit File Transfer Package                                                 195
-
 Echoing:
0Some communication processors, typically front ends,  echo  their  input.   When
 this  happens,  every  Kermit  packet that is sent to it will bounce right back,
 causing no end of confusion.  Some Kermit programs have been designed to  ignore
 echoed  packets,  but  most  have not.  If you encounter this problem, there are
 several possible solutions:
0-  Disable the front end echoing by typing  some  special  command,  if  such  a
    command is provided by the system.
0-  Some front ends respond to certain escape or control sequences as commands to
    turn off echoing, either from that point onward, or else on a per-line basis.
    In this case, the  appropriate  control  sequence  can  be  inserted  between
    packets  by  Kermit  programs instructed to do so, for instance using the SET
    PAD command.
0-  If the echoing cannot be disabled, then the two  Kermit  programs  should  be
    instructed   to   use   differing   packet   start  markers,  using  the  SET
    START-OF-PACKET command -- for instance, one Kermit uses Control-A as  usual,
    and  the  other  uses  Control-B.  This can only be done if both Kermits have
    this SET command.
-
-
-
-
-
-
-
-
-
-
-
                                               Appendix A -- When Things Go Wrong
1196                                                 Kermit File Transfer Package
-
 A.3.  Special Characters
0There is one problem that can prevent a file transfer from starting at  all,  or
 may  crop  up  after the file transfer is underway.  For instance, during a file
 transfer operation you might find your smart  modem  suddenly  hanging  up  your
 current  connection  and  placing  a  call  to Tasmania.  Or you might find that
 packets  containing  a  certain  character  like  "@"  cannot   be   transmitted
 successfully.
0This is the problem of "special characters."  Some device in  the  communication
 path  --  a  front  end,  a  port  switcher,  a  multiplexer, a "smart" modem --
 interprets certain characters in the data stream as commands rather than as data
 to  be  passed  them along to the other side.  Usually such equipment interferes
 only with the transmission of ASCII control characters; so long as Control-A and
 Carriage  Return  --  Kermit's normal packet start and end delimiters -- are not
 molested, then Kermit can operate.  However, equipment may exist which  swallows
 even  printable  characters.   Since  Kermit  assumes  that  ALL printable ASCII
 characters (ASCII 40 through 176, octal) can be transmitted without interference
 or  modification,  such  equipment  will prevent Kermit file transfer unless its
 printable-character-swallowing features can be disabled.
-A.4.  3270 Protocol Emulators
0Connections to IBM  mainframes  through  3270  protocol  emulation  hardware  or
 software  cannot  be  used for file transfer with Kermit or any similar program.
 Kermit requires an asynchronous  stream  ASCII  telecommunications  environment.
 3270-style  terminals  operate in a block-mode bisynchronous EBCDIC environment.
 Protocol converters change the EBCDIC screen data blocks into streams  of  ASCII
 characters  with  imbedded terminal control sequences.  Packetized file transfer
 is impossible under these circumstances because the data  is  modified  and  the
 packet block check invalidated.
0The only exception to this rule occurs on IBM mainframes with protocol emulators
 that  can  be  put  into  transparent mode by a command from the host, and whose
 Kermit programs have been coded explicitly to do this.  For instance, as of this
 writing there are IBM mainframe Kermit programs that allow file transfer through
 the Series/1 or 7171 front ends.
0The 3270 macro that the NIH Computer Center has supplied  (in  the  MSKERMIT.INI
 file) helps users access the NIH protocol conversion facility with the Kermit-MS
 terminal emulator.  However, Kermit file transfers  are  not  possible  via  the
 protocol conversion facility.
-
-
-
-
 When Things Go Wrong -- Appendix A
1Kermit File Transfer Package                                                 197
-
 A.5.  The Transfer Starts But Then Gets Stuck
0Once a Kermit file transfer has begun, there are certain conditions under  which
 it  can  become  stuck.   Since  many  hosts  are  capable of generating timeout
 interrupts when input doesn't appear within  a  reasonable  interval,  they  can
 resend  unacknowledged packets or request that missing packets be retransmitted.
 But since not all Kermit programs are capable of timing out, a means for  manual
 intervention  is  provided in the local Kermit -- you can type a carriage return
 on the keyboard of most microcomputers to wake up and continue the transfer.
0The following sections discuss various reasons why a transfer in progress  could
 become  stuck.   Before  examining these, first make sure that you really have a
 Kermit on the other end of  the  line,  and  you  have  issued  the  appropriate
 command:   SEND,  RECEIVE,  or  SERVER.   If  the  remote  side is not a server,
 remember that you must connect back between each transfer and issue a  new  SEND
 or RECEIVE command.
-A.5.1.  The Microcomputer is Hung
0The microcomputer itself sometimes becomes  hung  for  reasons  beyond  Kermit's
 control, such as power fluctuations.  If the microcomputer's screen has not been
 updated for a long time, then the microcomputer may be hung.   Try  these  steps
 (in the following order):
0-  Press RETURN to wake the microcomputer up.  This should clear up any protocol
    deadlock.  Several RETURNs might be necessary.
0-  If the problem was not a deadlock, restart Kermit, CONNECT back to the  host,
    get  back to your job or login again, and restart the transfer.  You may have
    to exit and reenter Kermit on the remote host.
-A.5.2.  The Connection is Broken
0Check the connection.  Make sure no connectors have  wiggled  loose  from  their
 sockets.   If  you're  using a modem, make sure you still have a carrier signal.
 Reestablish your connection if you have to.
0If upon reconnection you get no response, maybe the remote host  or  the  remote
 Kermit  program  crashed.   Get  back  to  command level on the local Kermit (on
 microcomputer implementations, you may be able to do this by typing  about  five
 RETURNs, or one or more Control-C's).  Issue the CONNECT command so that you can
 see what happened.  If the remote system has crashed then you will have to  wait
 for it to come back, and restart whatever file that was being transferred at the
 time.
-
-
-
                                               Appendix A -- When Things Go Wrong
1198                                                 Kermit File Transfer Package
-
-A.5.3.  The Disk is Full
0If your local floppy disk fills up or if files cannot be stored at the host, the
 Kermit  on  the machine where this occurs will inform you and then terminate the
 transfer.  You can continue the transfer by repeating the whole procedure either
 with  a  fresh floppy or after cleaning up your directory.  Some Kermit programs
 allow you to continue the sequence where it left off.  Some Kermits also have  a
 feature  that  allows  you to keep incompletely received files; this would allow
 you go back to the sending system, extract the unsent portion of the  file,  and
 send  it,  and then append the two received portions together using an editor or
 other system utility.  Kermit does not  provide  the  ability  to  switch  disks
 during a file transfer.
-A.5.4.  Message Interference
0You may find that  file  transfers  fail  occasionally  and  upredictably.   One
 explanation  could  be  that  terminal  messages  are being mixed with your file
 packet data.  These could include system broadcast  messages  (like  "System  is
 going  down  in  30  minutes"), messages from other users ("Hi Fred, what's that
 Kermit program you're always running?"), notifications that you  have  requested
 ("It's  7:30,  go  home!"   or  "You  have  mail from..."). Most Kermit programs
 attempt to  disable  intrusive  messages  automatically,  but  not  all  can  be
 guaranteed  to  do  so.  It may be necessary for you to "turn off" such messages
 before starting Kermit.
-A.5.5.  Transmission Delays
0Packet transmission can be delayed by  various  agents:   congested  timesharing
 systems or networks, earth satellites, etc.  When transmission delay exceeds the
 per-packet timeout interval for a significant length of time, the transfer could
 fail.   Most  Kermit  programs  provide  commands  that  allow you to adjust the
 timeout interval  or  the  packet  transmission  retry  threshold  in  order  to
 accommodate to severe transmission delays.
-A.5.6.  Noise Corruption
0If your connection is extremely noisy, packets  will  become  corrupted  --  and
 require   retransmission   --  more  often.   The  probability  that  successive
 retransmissions will fail because of corruption rises with the noise level until
 it  exceeds  the retry threshold, at which point the file transfer fails.  There
 are several recourses.  First, try to establish a new connection.   If  that  is
 impractical,  then use SET commands (when available) to reduce the packet length
 and increase the retry threshold.  Shorter packets reduce both  the  probability
 that  a particular packet will be corrupted and the retransmission overhead when
 corruption does occur, but they also increase the overall protocol overhead.  In
 a noisy environment, you should also request a higher level of error checking.
-
0When Things Go Wrong -- Appendix A
1Kermit File Transfer Package                                                 199
-
 A.5.7.  Host Errors
0Various error conditions can occur on the remote host  that  could  affect  file
 transmission.   Whenever  any  such  error  occurs,  the  remote Kermit normally
 attempts to send an informative error message to the local one, and then  breaks
 transmission, putting you back at Kermit command level on the local system.
-A.6.  File is Garbage
0There are certain conditions under which Kermit can  believe  it  transferred  a
 file  correctly  when in fact, it did not.  The most likely cause has to do with
 the tricky business of file attributes, such  as  text  vs.  binary,  7-bit  vs.
 8-bit, blocked vs. stream, and so forth.  Each system has its own peculiarities,
 and each Kermit has special commands to allow you to specify how a  file  should
 be  sent  or  stored.   However,  these  difficulties  usually crop up only when
 sending binary files.  Text files should normally present no problem between any
 two Kermit programs.
-A.7.  Junk After End of File
0When transferring a text file from a microcomputer to a mainframe, sometimes you
 will  find  extraneous characters at the end of the file after it arrives on the
 target system.  This is because many microcomputers don't have a consistent  way
 of  indicating  the end of a file.  CP/M is a good example.  The minimum unit of
 storage on a CP/M floppy is a "block" of 128 bytes.  Binary files always consist
 of  a  whole  number of blocks, but a text file can end anywhere within a block.
 Since CP/M does not record a file's  byte  count,  it  uses  the  convention  of
 marking  the  end  with  an imbedded Control-Z character.  If your microcomputer
 version of Kermit is not looking for this character, it  will  send  the  entire
 last  block,  which may contain arbitrary junk after the "real" end of the file.
 To circumvent this problem, most microcomputer Kermits have  commands  like  SET
 FILE  ASCII  or  SET FILE TEXT to instruct Kermit to obey the CTRL-Z convention.
 Some microcomputer Kermits operate in "text" mode by default, others in "binary"
 or "block" mode.
0To complicate matters, certain software on other microcomputer systems, such  as
 MS-DOS,  follows the CP/M end-of-file convention.  Under MS-DOS, certain editors
 and other programs use Control-Z for end-of-file, and  other  programs  do  not.
 MS-DOS Kermit provides a SET command to choose the desired format.
-
-
-
-
-                                              Appendix A -- When Things Go Wrong
1200                                                 Kermit File Transfer Package
-
 A.8.  Data Set Problems Under TSO
0You may get unclear error messages when TSO cannot  find  a  data  set  you  are
 trying  to  use.   Make  sure  the  data  set  is  cataloged; TSO only processes
 cataloged data sets.  Make sure the data set conforms to the IBM standard naming
 conventions  as  described  in  Section  6.1  of this manual.  If you have set a
 prefix, make sure it is set completely.  A common mistake is to  leave  off  the
 period separator (e.g., if you have data sets qualified by "ABC", set the prefix
 to "ABC.", not "ABC").  If the files you  have  sent  to  TSO  are  mysteriously
 disappearing, you probably forgot to set the volume parameter, which defaults to
 TMP.  Files on the TMP packs are scratched within days after their creation.
0If a file is sent to TSO from Kermit-MS with no error messages, but only part of
 the  file  is  transferred,  then  the file probably contains one or more Ctrl-Z
 characters before the real end of file.  To  circumvent  the  problem,  set  the
 Kermit-MS  EOF  parameter  to  NOCTRL-Z  (see  Section  7.3.6 of this manual for
 details).
-
-
-
-
-
-
-
-
-
-
-
-
-When Things Go Wrong -- Appendix A
1Kermit File Transfer Package                                                 201
-Appendix B -- ASCII and EBCDIC Tables
0B.1. The ASCII Character Set
0There are 128 characters in the ASCII (American Standard  Code  for  Information
 Interchange) "alphabet".  The characters are listed in order of ASCII value; the
 columns are labeled as follows:
0ASCII Dec       Decimal (base 10) representation.
 ASCII Oct       Octal (base 8) representation.
 ASCII Hex       Hexadecimal (base 16) representation.
 EBCDIC Hex      EBCDIC hexadecimal equivalent for Kermit translate tables.
 Char            Name or graphical representation of character.
 Remark          Description of character.
0The caret (X) character notation used in the first column in the  remarks  shows
 the  association  of  control  characters  and capital letters (plus a few other
 characters).  Each control character is  exactly  64  (decimal)  less  than  the
 letter  shown.  For example, the ASCII code for "A" is decimal 65; XA is 65-64=1
 which is the code for SOH.  This notation also indicates a method  for  entering
 control  characters from the keyboard:  depress the CONTROL key and, while it is
 held down, type the letter.   Thus,  SOH  is  entered  by  depressing  CTRL  and
 striking  "A".   Many  computers  which  use   ASCII  for  internal  storage  of
 characters use this notation for displaying control  characters  which  have  no
 special significance to it (e.g., XA).
0The first group consists of nonprintable control characters:
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char  Remarks
 000   000   00   00    NUL   X@, Null, Idle
 001   001   01   01    SOH   XA, Start of heading
 002   002   02   02    STX   XB, Start of text
 003   003   03   03    ETX   XC, End of text
 004   004   04   37    EOT   XD, End of transmission
 005   005   05   2D    ENQ   XE, Enquiry
 006   006   06   2E    ACK   XF, Acknowledge
 007   007   07   2F    BEL   XG, Bell, beep, or fleep
 008   010   08   16    BS    XH, Backspace
 009   011   09   05    HT    XI, Horizontal tab
 010   012   0A   25    LF    XJ, Line feed
 011   013   0B   0B    VT    XK, Vertical tab
 012   014   0C   0C    FF    XL, Form feed (top of page)
 013   015   0D   0D    CR    XM, Carriage return
 014   016   0E   0E    SO    XN, Shift out
 015   017   0F   0F    SI    XO, Shift in
 016   020   10   10    DLE   XP, Data link escape
 017   021   11   11    DC1   XQ, Device control 1, XON
 018   022   12   12    DC2   XR, Device control 2
 019   023   13   35    DC3   XS, Device control 3, XOFF
 020   024   14   3C    DC4   XT, Device control 4
-
-                                           Appendix B -- ASCII and EBCDIC Tables
1202                                                 Kermit File Transfer Package
-.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char  Remarks
 021   025   15   3D    NAK   XU, Negative acknowledge
 022   026   16   32    SYN   XV, Synchronous idle
 023   027   17   26    ETB   XW, End of transmission block
 024   030   18   18    CAN   XX, Cancel
 025   031   19   19    EM    XY, End of medium
 026   032   1A   3F    SUB   XZ, Substitute
 027   033   1B   27    ESC   X[, Escape, prefix, altmode
 028   034   1C   1C    FS    X\, File separator
 029   035   1D   1D    GS    X], Group separator
 030   036   1E   1E    RS    XX, Record separator
 031   037   1F   1F    US    X_, Unit separator
0The  last  four  are  usually associated with the control version of backslash,
 right square bracket, uparrow (or circumflex),  and  underscore,  respectively,
 but some terminals do not transmit these control characters.
0The following characters are printable:
0First, some punctuation characters.
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char  Remarks
 032   040   20   40    SP    Space, blank
 033   041   21   5A    !     Exclamation mark
 034   042   22   7F    "     Doublequote
 035   043   23   7B    #     Number sign, pound sign
 036   044   24   5B    $     Dollar sign
 037   045   25   6C    %     Percent sign
 038   046   26   50    &     Ampersand
 039   047   27   7D    '     Apostrophe, accent acute
 040   050   28   4D    (     Left parenthesis
 041   051   29   5D    )     Right parenthesis
 042   052   2A   5C    *     Asterisk, star
 043   053   2B   4E    +     Plus sign
 044   054   2C   6B    ,     Comma
 045   055   2D   60    -     Dash, hyphen, minus sign
 046   056   2E   4B    .     Period, dot
 047   057   2F   61    /     Slash
0Numeric characters:
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char
 048   060   30   F0    0
 049   061   31   F1    1
 050   062   32   F2    2
 051   063   33   F3    3
 052   064   34   F4    4
 053   065   35   F5    5
 054   066   36   F6    6
 055   067   37   F7    7
 056   070   38   F8    8
 057   071   39   F9    9
0ASCII and EBCDIC Tables -- Appendix B
1Kermit File Transfer Package                                                 203
-More punctuation characters:
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char  Remarks
 058   072   3A   7A    :     Colon
 059   073   3B   5E    ;     Semicolon
 060   074   3C   4C    <     Less than, left angle bracket
 061   075   3D   7E    =     Equal sign
 062   076   3E   6E    >     Greater than, right angle bracket
 063   077   3F   6F    ?     Question mark
 064   100   40   7C    @     "At" sign
0Upper-case alphabetic characters (letters):
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char
 065   101   41   C1    A
 066   102   42   C2    B
 067   103   43   C3    C
 068   104   44   C4    D
 069   105   45   C5    E
 070   106   46   C6    F
 071   107   47   C7    G
 072   110   48   C8    H
 073   111   49   C9    I
 074   112   4A   D1    J
 075   113   4B   D2    K
 076   114   4C   D3    L
 077   115   4D   D4    M
 078   116   4E   D5    N
 079   117   4F   D6    O
 080   120   50   D7    P
 081   121   51   D8    Q
 082   122   52   D9    R
 083   123   53   E2    S
 084   124   54   E3    T
 085   125   55   E4    U
 086   126   56   E5    V
 087   127   57   E6    W
 088   130   58   E7    X
 089   131   59   E8    Y
 090   132   5A   E9    Z
0More punctuation characters:
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char  Remarks
 091   133   5B   AD    [     Left square bracket
 092   134   5C   E0    \     Backslash
 093   135   5D   BD    ]     Right square bracket
 094   136   5E   5F    X     Circumflex, up arrow
 095   137   5F   6D    _     Underscore, left arrow
 096   140   60   79    `     Accent grave
-
                                            Appendix B -- ASCII and EBCDIC Tables
1204                                                 Kermit File Transfer Package
-Lower-case alphabetic characters (letters):
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char
 097   141   61   81    a
 098   142   62   82    b
 099   143   63   83    c
 100   144   64   84    d
 101   145   65   85    e
 102   146   66   86    f
 103   147   67   87    g
 104   150   68   88    h
 105   151   69   89    i
 106   152   6A   91    j
 107   153   6B   92    k
 108   154   6C   93    l
 109   155   6D   94    m
 110   156   6E   95    n
 111   157   6F   96    o
 112   160   70   97    p
 113   161   71   98    q
 114   162   72   99    r
 115   163   73   A2    s
 116   164   74   A3    t
 117   165   75   A4    u
 118   166   76   A5    v
 119   167   77   A6    w
 120   170   78   A7    x
 121   171   79   A8    y
 122   172   7A   A9    z
0More punctuation characters:
0.....ASCII.... EBCDIC
 Dec   Oct  Hex  Hex    Char  Remarks
 123   173   7B   8B     $    Left curly brace
 124   174   7C   4F     |    Vertical bar
 125   175   7D   9B         Right curly brace
 126   176   7E   A1     ~    Tilde
-Finally, one more nonprintable character:
0127   177   7F   07    DEL   Delete, rubout
-
-
-
-
 ASCII and EBCDIC Tables -- Appendix B
1Kermit File Transfer Package                                                 205
-B.2. ASCII to EBCDIC Translation Table
0     (For text data received by TSO Kermit)
0How to read the table:  the ASCII hexadecimal representation of the character  P
 is  50; this character can be found in the table in column 5, row 0.  Below this
 character you will find the EBCDIC hexadecimal representation that results  from
 the  translation  of  ASCII  to EBCDIC.  In short, an ASCII 50 (P) is translated
 into an EBCDIC D7.  The meanings of the two and three letter codes  (e.g.,  SOH)
 can  be  found  in the remarks section of the table in Section B.1.  - the ASCII
 Character Set.
0Notes: (1) ASCII characters with their 8th bit on are translated as if their 8th
            bit were off.  For example, hex B1 is translated like hex 31 (ASCII 1
            - hex B1 without the 8th bit on) to hex F1 (EBCDIC 1).
0       (2) Hex 5E (ASCII X) translates to hex 5F (EBCDIC ^).
-
-
-
-
-
-
-
-
-
-
-
-
-
                                            Appendix B -- ASCII and EBCDIC Tables
1206                                                 Kermit File Transfer Package
-    ASCII to EBCDIC Translation Table
0              First Digit
       0   1   2   3   4   5   6   7
    +----+---+---+---+---+---+---+----+
   0| NUL DLE SP   0   @   P   `   p  |0
    | 00  10  40  F0  7C  D7  79  97  |
    |                                 |
   1| SOH DC1  !   1   A   Q   a   q  |1
    | 01  11  5A  F1  C1  D8  81  98  |
    |                                 |
   2| STX DC2  "   2   B   R   b   r  |2
    | 02  12  7F  F2  C2  D9  82  99  |
    |                                 |
 S 3| ETX DC3  #   3   C   S   c   s  |3 S
    | 03  35  7B  F3  C3  E2  83  A2  |
 e  |                                 |  e
   4| EOT DC4  $   4   D   T   d   t  |4
 c  | 37  3C  5B  F4  C4  E3  84  A3  |  c
    |                                 |
 o 5| ENQ NAK  %   5   E   U   e   u  |5 o
    | 2D  3D  6C  F5  C5  E4  85  A4  |
 n  |                                 |  n
   6| ACK SYN  &   6   F   V   f   v  |6
 d  | 2E  32  50  F6  C6  E5  86  A5  |  d
    |                                 |
   7| BEL ETB  '   7   G   W   g   w  |7
    | 2F  26  7D  F7  C7  E6  87  A6  |
 D  |                                 |  D
   8| BS  CAN  (   8   H   X   h   x  |8
 i  | 16  18  4D  F8  C8  E7  88  A7  |  i
    |                                 |
 g 9| HT  EM   )   9   I   Y   i   y  |9 g
    | 05  19  5D  F9  C9  E8  89  A8  |
 i  |                                 |  i
   A| LF  SUB  *   :   J   Z   j   z  |A
 t  | 25  3F  5C  7A  D1  E9  91  A9  |  t
    |                                 |
   B| VT  ESC  +   ;   K   [   k   $  |B
    | 0B  27  4E  5E  D2  AD  92  8B  |
    |                                 |
   C| FF  FS   ,   <   L   \   l   |  |C
    | 0C  1C  6B  4C  D3  E0  93  4F  |
    |                                 |
   D| CR  GS   -   =   M   ]   m     |D
    | 0D  1D  60  7E  D4  BD  94  9B  |
    |                                 |
   E| SO  RS   .   >   N   X   n   ~  |E
    | 0E  1E  4B  6E  D5  5F  95  A1  |
    |                                 |
   F| SI  US   /   ?   O   _   o  DEL |F
    | 0F  1F  61  6F  D6  6D  96  07  |
    +----+---+---+---+---+---+---+----+
       0   1   2   3   4   5   6   7
               First Digit
0ASCII and EBCDIC Tables -- Appendix B
1Kermit File Transfer Package                                                 207
-B.3. EBCDIC to ASCII Translation Table
0       (For text data sent by TSO Kermit)
0How to read the table:  the EBCDIC hexadecimal representation of the character 9
 is  F9; this character can be found in the table in column F, row 9.  Below this
 character you will find the ASCII hexadecimal representation that  results  from
 the translation from EBCDIC to ASCII.  In short, an EBCDIC F9 is translated into
 an ASCII 39.  The meanings of the two and three letter codes (e.g., SOH) can  be
 found in the remarks section of the table in Section B.1.  - the ASCII Character
 Set.
0Notes: (1) Hex 33 and 37 both translate  to  hex  04  (ASCII  EOT),  37  is  the
            preferred code.
0       (2) Hex 5F (EBCDIC ^) and BE (EBCDIC X) both translate to hex  5E  (ASCII
            X).   For  received  data,  hex  5E (ASCII X) is translated to hex 5F
            (EBCDIC ^).
0       (3) Hex 8B and C0 both translate to hex 7B (ASCII $).  For received data,
            hex 7B (ASCII $) is translated to hex 8B.
0       (4) Hex 9B and D0 both translate to hex 7D (ASCII ).  For received data,
            hex 7D (ASCII ) is translated to hex 9B.
0       (5) Hex 60 (EBCDIC -) and 62 (WYLBUR inserted hyphen) both  translate  to
            hex  2D  (ASCII -).  For received data hex 2D (ASCII -) is translated
            to hex 60 (EBCDIC -).
0       (6) EBCDIC characters not shown are translated to hex 3A (ASCII :).
-
-
-
-
-
-
-
-
-                                           Appendix B -- ASCII and EBCDIC Tables
1208                                                 Kermit File Transfer Package
-                    EBCDIC to ASCII Translation Table
0                               First Digit
       0   1   2   3   4   5   6   7   8   9   A   B   C   D   E   F
    +----+---+---+---+---+---+---+---+---+---+---+---+---+---+---+----+
   0| NUL DLE         SP   &   -                       $      \   0  |0
    | 00  10          20  26  2D                      7B  7D  5C  30  |
    |                                                                 |
   1| SOH DC1                  /       a   j   ~       A   J       1  |1
    | 01  11                  2F      61  6A  7E      41  4A      31  |
    |                                                                 |
   2| STX DC2     SYN          -       b   k   s       B   K   S   2  |2
    | 02  12      16          2D      62  6B  73      42  4B  53  32  |
    |                                                                 |
 S 3| ETX         EOT                  c   l   t       C   L   T   3  |3 S
    | 03          04                  63  6C  74      43  4C  54  33  |
 e  |                                                                 |  e
   4|                                  d   m   u       D   M   U   4  |4
 c  |                                 64  6D  75      44  4D  55  34  |  c
    |                                                                 |
 o 5| HT      LF  DC3                  e   n   v       E   N   V   5  |5 o
    | 09      0A  13                  65  6E  76      45  4E  56  35  |
 n  |                                                                 |  n
   6|     BS  ETB                      f   o   w       F   O   W   6  |6
 d  |     08  17                      66  6F  77      46  4F  57  36  |  d
    |                                                                 |
   7| DEL     ESC EOT                  g   p   x       G   P   X   7  |7
    | 7F      1B  04                  67  70  78      47  50  58  37  |
 D  |                                                                 |  D
   8|     CAN                          h   q   y       H   Q   Y   8  |8
 i  |     18                          68  71  79      48  51  59  38  |  i
    |                                                                 |
 g 9|     EM                       `   i   r   z       I   R   Z   9  |9 g
    |     19                      60  69  72  7A      49  52  5A  39  |
 i  |                                                                 |  i
   A|                      !       :                                  |A
 t  |                     21      3A                                  |  t
    |                                                                 |
   B| VT               .   $   ,   #   $                             |B
    | 0B              2E  24  2C  23  7B  7D                          |
    |                                                                 |
   C| FF  FS      DC4  <   *   %   @                                  |C
    | 0C  1C      14  3C  2A  25  40                                  |
    |                                                                 |
   D| CR  GS  ENQ NAK  (   )   _   '           [   ]                  |D
    | 0D  1D  05  15  28  29  5F  27          5B  5D                  |
    |                                                                 |
   E| SO  RS  ACK      +   ;   >   =               X                  |E
    | 0E  1E  06      2B  3B  3E  3D              5E                  |
    |                                                                 |
   F| SI  US  BEL SUB  |   ^   ?   "                                  |F
    | 0F  1F  07  1A  7C  5E  3F  22                                  |
    +----+---+---+---+---+---+---+---+---+---+---+---+---+---+---+----+
       0   1   2   3   4   5   6   7   8   9   A   B   C   D   E   F
                                First Digit
0ASCII and EBCDIC Tables -- Appendix B
1Kermit File Transfer Package                                                 209
-
 Appendix C -- Microcomputer to Microcomputer File Transfer
0This appendix is provided as a courtesy, the methods  and  techniques  presented
 are not supported by the NIH Computer Center.
0This section explains to the novice user how to get  KERMIT  to  transfer  files
 between  microcomputers.   It  is  useful  to  those  who  are  in the difficult
 situation of needing to  send  information  between  incompatible  microcomputer
 systems,  either directly or across telephone lines.  This section is taken from
 "How to Use Kermit for Transferring Files Between Microcomputers:  CP/M  and  MS
 DOS  Systems"  by  Norman  Weatherby,  Ph.D.,  Center  for Population and Family
 Health, Columbia University.
-C.1.  Getting Ready to Use Kermit
0You will need the following items in order to use  KERMIT  for  file  transfers.
 The  only real problem is given last--determining what kind of cable(s) you will
 need for the systems.
0     1. Two microcomputers.  It is best if each one has two or more disk drives.
         Each one should have a serial port that can be used with a modem.
0        Each microcomputer system should have a DTE  (Data  Terminal  Equipment)
         port on an asynchronous communications adapter (the serial port), called
         COM1:  or COM2:  on IBM  PC-compatible  systems.   Perhaps  there  is  a
         serial  port,  but  it  is used to send information to a serial printer.
         Nearly all serial ports on IBM PCs and compatibles are DTE, however, the
         port may be a DCE (Data Communication Equipment) port.  Using a DCE port
         will not cause problems if you have the correct cable.   Note  that  the
         IBM  PC  dot  matrix  printer  is  a  parallel  printer and not a serial
         printer.  Never connect a modem or other serial device to  the  parallel
         port  used  for the parallel printer, even though it may appear that the
         cable will plug into the connection.
0     2. If the  two  microcomputers  are  nearby  each  other,  modems  are  not
         necessary.   If  you  are going to transfer files across telephone lines
         two full duplex modems are required such as the Hayes Smartmodem 2400 or
         the AT&T 2224B.  You should be able to set at least one of the modems to
         automatic answer mode.  File transfers work well but slowly at 300  bits
         per  second (around 30 characters per second), so it is best to have two
         1200 or 2400 bits per second modems.
0     3. A copy of Kermit for each computer.
-
-
-
-                      Appendix C -- Microcomputer to Microcomputer File Transfer
1210                                                 Kermit File Transfer Package
-
      4. The right cable(s).  You should be able to  plug  in  the  ends  of  the
         cable(s)  to  the  equipment that you are using.  For a connection using
         DTE ports and modems, or a DTE and a DCE port, at least pins  1  through
         8, 20, and 22 should be connected.  Do not "jumper" or short-circuit any
         pins in the cable.  For a direct connection, without modems and  with  2
         DTE  or DCE ports, a "null modem" cable will be necessary.  Wiring for a
         null modem may be done as shown:
0          Pin to Pin
+          __________
           1    -   1
           2    -   3
           3    -   2
         5,6,8  -  20
          20    - 5,6,8
           7    -   7
0              or
-          1    -   1
           2    -   3
           3    -   2
           6,8  -  20
          20    - 6,8
           7    -   7
         4&5 jumpered at each end
-IF YOU ARE DIRECTLY CONNECTING THE COMPUTERS:
0     a. Do not use a null modem cable if you are connecting a modem  (DTE)  port
         on one system to a printer (DCE) port on the other system.
0     b. Use a null modem cable if you are connecting a modem (DTE) port  on  one
         system  to  a  modem  (DTE)  port  on  the  other  system, or if you are
         connecting a printer (DCE) port on one system to a printer (DCE) port on
         the other system.
-IF YOU ARE USING MODEMS TO COMMUNICATE THROUGH TELEPHONE LINES:
0For each system,
0     a. Do not use a null modem cable if you are connecting a modem  (DTE)  port
         to the modem.
0     b. Use a null modem cable if you are connecting a printer (DCE) port to the
         modem.
-
-
0Microcomputer to Microcomputer File Transfer -- Appendix C
1Kermit File Transfer Package                                                 211
-
 C.2.  Connecting the Computers
0IF YOU ARE GOING TO USE MODEMS:
0Use the correct cable to hook up a full duplex modem to each  computer's  serial
 communications port.
-IF YOU ARE GOING TO DIRECTLY CONNECT THE COMPUTERS:
0     a. Directly connect the serial modem ports of the two machines.
0                               OR
0     b. Directly connect the serial modem port of one  computer  to  the  serial
         (not parallel) printer port of the other computer.
0One benefit of using a direct connection between the computers is that  you  can
 use high speeds, such as 9600 bits per second, to transfer the files.  Since you
 are not using modems and telephones, ignore  the  parts  of  this  section  that
 concern use of the modems and dialing of the telephone.
-LOADING KERMIT INTO MEMORY:
0Start Kermit on each machine.
-SETTING KERMIT'S OPTIONS
0To see the options that are available in your version of  KERMIT,  type  at  the
 prompt the command
0status<cr> or show<cr>
0Note that the toggle command SET  IBM  (set  on  or  off)  is  NOT  FOR  IBM  PC
 MICROCOMPUTERS--it  is a command for IBM VM/CMS mainframes and it is not used at
 all at NIH.
-SETTING THE PARITY:
0A computer "byte" is composed of eight bits, where each bit is a  zero  or  one.
 All  (English) printable letters, numbers, punctuation marks, and spaces between
 words can be represented by seven of the eight bits.  Sometimes the  eighth  bit
 is  used as a parity bit for checking to make sure that the other seven bits are
 correct.  However, some microcomputer software packages (such as  WordStar)  use
 the  eighth  bit  for  special  characters  that  allow  features  such as right
 justification.  In any event, if both computers  allow  the  following  command,
 issue it to allow the transmission of all eight bits:
0set parity none<cr>
-
                       Appendix C -- Microcomputer to Microcomputer File Transfer
1212                                                 Kermit File Transfer Package
-
 SETTING THE SPEED
0If you can set the speed from within KERMIT, make the  communication  speeds  of
 both computers equal by typing at the prompt the command
0SET SPEED ?
0and select the correct speed from a menu that is given on the screen.   Then  go
 to  the  portion of this section that discusses communicating between computers.
 For a direct connection, the correct  speed  is  the  highest  speed  that  both
 computers  can handle.  For a modem connection, the correct speed is the highest
 speed supported by both computers and modems.
0If you get messages that the SET SPEED command is not implemented, you will have
 to get out of Kermit and set it from your operating system, as discussed below.
0Note that a faster way to set the speed is to type
0SET SPEED XXXX<cr>
0where xxxx is the speed you want.
0If you cannot set the speed from within  KERMIT,  such  as  on  Heath/Zenith  89
 systems,  then  you  can  get  back  to  your operating system by typing, at the
 prompt,
0QUIT<cr>
0Then use the computer's software to set the speed of the serial  port  to  which
 the  cable  is  attached.   Refer to the specific section in this manual for the
 type of computer you are running Kermit on.
-
-
-
-
-
-
-
-
 Microcomputer to Microcomputer File Transfer -- Appendix C
1Kermit File Transfer Package                                                 213
-
 C.3.  Communicating Between Computers
0After Kermit is loaded into the memory of each computer,  and  its  options  are
 set, type at the prompt the command
0CONNECT<cr>
0on each computer.  This will put you into the connect  mode,  which  allows  one
 computer  operator  to send messages to the other operator through the modems or
 the direct connection.  Note that KERMIT replies with an "escape"  message  that
 tells you how to get back to the command state of the program.
0In fact, it is a good idea to test the command now.  The way you get back to the
 Kermit prompt varies by the type of system.  Note that you may have to issue the
 command but add a C (upper or lower case) to  it  to  get  back  to  the  Kermit
 prompt.  On MS-DOS systems the command is:
0X]c
0After some experimentation, you will see the Kermit prompt, and  you  can  again
 type the command:
0CONNECT<cr> .
0IF YOU ARE USING MODEMS:
0From  the  originate  modem,  dial  the  answering  modem.   If   you   have   a
 Hayes-compatible  auto-dial  modem,  you  can issue the dial command to it.  For
 example, with a touch tone telephones and a Hayes Smartmodem, the  only  command
 that is necessary for the originate modem is
0ATDTxxxxxxx<cr>
0where ATDT is in capital letters and xxxxxxx is the telephone  number  to  dial.
 The answering Smartmodem should be issued the command
0ATA<cr>
0if it does not automatically answer the phone.
-IF YOU ARE USING MODEMS OR A DIRECT CONNECTION:
0When the connection is made, each of you  will  be  able  to  send  and  receive
 messages that serve to test the connection.
0If you want to see what you are typing, get back to the KERMIT prompt by  typing
 the  "escape"  command  that  you  wrote  down and tested above.  Then issue the
 command
0SET LOCAL-ECHO ON<cr>
-
0                      Appendix C -- Microcomputer to Microcomputer File Transfer
1214                                                 Kermit File Transfer Package
-
 If the connection is not made, so that it is not possible to  send  AND  receive
 messages, then you should check
0     the speeds of the computers
      the modems, and the wiring to the modems
      or the wiring between the directly-connected
      computers.
0Make sure that the computer is sending or receiving data to the correct port  on
 the computer.  It is also helpful, as a last resort, to check whether or not the
 telephone is working.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-Microcomputer to Microcomputer File Transfer -- Appendix C
1Kermit File Transfer Package                                                 215
-
 C.4.  Sending and Receiving Files
0When each computer operator is satisfied that a connection has been  made,  then
 both operators return to the Kermit prompt, as explained above.
0The operator that wants to receive a file types
0RECEIVE<cr>
0The file name will be sent from the other system.
0The operator that wants to send a file types the command
0SEND [drive:]filename.ext<cr>
0For example, to send the file on disk B that is named  myfile.txt,  the  sending
 operator would type
0SEND b:myfile.txt<cr>
0It is not necessary to type in the drive specification if it is the same as your
 default  disk  drive, but it is always safe to do so.  If the receiving operator
 hits the return after the sending operator hits the return, it may be  necessary
 for the receiving operator to hit another return before the file will be sent.
0KERMIT will wait for a few seconds, and then the operators  will  see  on  their
 screens  that  packets of information are being sent and received.  Kermit first
 sends the file name, and it is a good sign to the receiving  operator  when  the
 file name appears on his or her screen.  The number of packets will increment on
 both machines until the transfer is complete, and then each computer will return
 to  the  Kermit prompt.  At that time, the receiving operator can check the file
 or another file can be sent.
-CHECKING WHAT WAS SENT
0Once a connection has been established with KERMIT, it is not broken if  one  or
 both of the operators return to the operating system of their computers to check
 something such as the length or name of  a  file.   Thus,  when  a  transfer  is
 complete, the receiving operator can get out of Kermit by typing
0EXIT<cr>
0at the Kermit prompt.  The file that was received can be  examined,  usually  by
 issuing the command
0TYPE [drive:]filename.ext<cr>
0The file will scroll by on the screen,  and  you  will  see  that  it  has  been
 transferred without error!
-
-                      Appendix C -- Microcomputer to Microcomputer File Transfer
1216                                                 Kermit File Transfer Package
-
 The receiving operator can then return to Kermit (e.g., X]C).  If you  need  to,
 reset  the  speed  and the parity, and you will then be able to transfer another
 file or get into connect mode and send messages.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0Microcomputer to Microcomputer File Transfer -- Appendix C
1Kermit File Transfer Package                                                 217
-
 C.5.  Figuring Out Why (If) Kermit Does Not Work
0KERMIT is very reliable.  It accurately transfers files even when the  telephone
 line is unusable for voice transmissions because of static and noise.
0Operators do, however, tend to make mistakes.  One such problem  is  impatience.
 Please  let  Kermit wait for a few seconds before you touch a carriage return on
 the receiving computer to "make it work."  If Kermit  seems  to  be  dead  after
 about  thirty  seconds of waiting, then something is wrong.  If you were able to
 send messages back and forth in connect mode, or if Kermit fails after the first
 four or five packets, then probably the problem is that the file that you wanted
 to send does not exist, or the sending operator misspelled its name in the  send
 command.
0Occasionally, Kermit will fail for reasons beyond  its  control.   The  transfer
 will  fail  if  one of the computers involved goes down.  A feature such as call
 waiting or intercom messages on a telephone line will stop the  transmission  if
 they  happen during a transfer.  These failures are advantages in that they show
 that Kermit is smart enough to quit when there is a major problem.
-
-
-
-
-
-
-
-
-
-
-
-
                       Appendix C -- Microcomputer to Microcomputer File Transfer
1218                                                 Kermit File Transfer Package
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
0Microcomputer to Microcomputer File Transfer -- Appendix C
1DOCUMENT COMMENT SHEET
0Is the Kermit File Transfer Package manual
0                                              YES   NO
0Clear?                                        ___   ___
 Well Organized?                               ___   ___
 Complete?                                     ___   ___
 Accurate?                                     ___   ___
 Suitable for the beginner?                    ___   ___
 Suitable for advanced user?                   ___   ___
-Comments:_____________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
0______________________________________________________________
-Please give page references where appropriate.  If you wish a
 reply, include your name and mailing address.
-                   Send to:  NIH
                              DCRT
                              Computer Center
                              Technical Information Office
                              Building 12A, Room 1017
                              Bethesda, Maryland  20892
1